## Slide 1
RP-250665
3GPP TSG RAN Meeting #107
Incheon, Korea, 12th to 14th March, 2025
Views on Scope for R20 “Sensing/ISAC for 5G-Adv and 6G”
Agenda Item: 15.2.9.1
Source: Tejas Networks
Document for: Discussion

## Slide 2
3GPP SA1: The rel-19 of 3GPP has defined multiple scenarios related to Integrated Sensing and Communication (ISAC):
  Object/Target detection and tracking. e.g. UAVs, automotive vehicles, human beings, etc.
  Weather monitoring. e.g. rainfall, floods, etc.
3GPP RAN1: The rel-19 SI of 3GPP has been discussing:
  ISAC channel modeling,
    Target Channel, Background Channel, RCS modelling, etc.
  ISAC deployment scenarios.
The channel modeling and calibration work is expected to be completed by 3GPP RAN1#121 in Release-19. During RAN#106, companies agreed to study and discuss the RAN architecture related to ISAC within RAN3 for Release-20. Therefore, RAN1 should wait for RAN3 to make progress on the architectural aspects before initiating its own study and evaluation work.
Motivation
The channel modeling and calibration work is expected to be completed by 3GPP RAN1#121 in Release-19. During RAN#106, companies agreed to study and discuss the RAN architecture related to ISAC within RAN3 for Release-20. Therefore, RAN1 should wait for RAN3 to make progress on the architectural aspects before initiating its own study and evaluation work.

## Slide 3
For ISAC channel modeling, the following use-cases were prioritized by RAN-1:
UAV detection and weather monitoring use cases should be prioritized for study and evaluation in RAN1.
The OFDM waveform used in 5G is not suitable for sensing, especially for monostatic sensing.
Furthermore, the standards impact for most sensing modes, particularly gNB-to-gNB sensing, is very high.
We propose that ISAC should not be studied by 3GPP RAN1 in Release-20 under the 5G-Advanced track. Instead, it should be considered under the 6G track, once RAN3 makes adequate progress on the relevant architecture aspects.
ISAC Use-cases
Use-Case` | Sensing Functionality/Parameters
UAV related | UAV detection, UAV localization, UAV tracking.
Human related | VRU detection, fall detection.
Weather related | Rainfall detection, flood detection, snow fall detection.
Infrastructure related | Automated guided vehicle tracking in indoor factories.
Hazard related | Objects creating hazards on roads/railways.
We propose that ISAC should not be studied by 3GPP RAN1 in Release-20 under the 5G-Advanced track. Instead, it should be considered under the 6G track, once RAN3 makes adequate progress on the relevant architecture aspects.

## Slide 4
  For ISAC, RAN-1 should study the sensing performance for the following mode:
  The gNB-to-gNB multi-static sensing mode is the most reasonable and practical option and should be prioritized in the ISAC study by 3GPP RAN for all its works.
    This also aligns with views of the majority stakeholders in SA2#167 prioritizing gNB based sensing.
gNB based Sensing
Sensing Mode | Merit | Limitation
gNB monostatic | Very low overhead | Self interference cancellation is very difficult
gNB-gNB multi-static | Low overhead | New SFI formats required
gNB-UE multi-static* | Low standards impact | High reporting overhead
UE monostatic | Low overhead | Self interference cancellation is extremely difficult. Poor sensing performance
UE-UE multi-static |  | Poor sensing performance Localized sensing Synchronization and calibration issues
Note: * 1. One or multiple gNB(s) transmits and One or multiple UE(s) receives the sensing signal in downlink or, 2. One or multiple UE(s) transmits and One or multiple gNB(s) receives the sensing signal in uplink. |  | 
The gNB-to-gNB multi-static sensing mode should be prioritized in the ISAC study by 3GPP RAN for all its works.

## Slide 5
RAN WGs should prioritize the gNB-to-gNB multi-static sensing use case.
  Low reporting overhead from gNB to Sensing Function,
  We believe this case has the least impact on existing standards,
  High sensing accuracy due to large bandwidth and multiple antennas at gNB,
  Excellent LOS probability with targets like UAVs in gNB-to-gNB sensing,
  Superior sensing coverage and tracking with advanced transmitters and receivers,
  Reduced network overhead (e.g., fewer handovers) compared to other sensing modes
  Static nature of gNBs, with precisely known location, simplifies initial implementation compared to bistatic scenarios with UEs
gNB based Sensing
Sensing
Communication

## Slide 6
Proposal 1: The channel modeling and calibration work is expected to be completed by 3GPP RAN1#121 in Release-19. During RAN#106, companies agreed to study and discuss the RAN architecture related to ISAC within RAN3 for Release-20. Therefore, RAN1 should wait for RAN3 to make progress on the architectural aspects before initiating its own study and evaluation work.
Proposal 2: We propose that ISAC should not be studied by 3GPP RAN1 in Release-20 under the 5G-Advanced track. Instead, it should be considered under the 6G track, once RAN3 makes adequate progress on the relevant architecture aspects.
Proposal 3: The gNB-to-gNB multi-static sensing mode should be prioritized in the ISAC study by 3GPP RAN for all its works [RAN-3 led].
Conclusions
Proposals
RAN-1 should consider the following observations on the sensing modes for ISAC
  gNB-gNB multi-static sensing mode is the most reasonable and practical use-case to study for ISAC
    Low reporting overhead from gNB to Sensing Function,
    We believe this case has the least impact on existing standards,
    High sensing accuracy due to large bandwidth and multiple antennas at gNB,
    Excellent LOS probability with targets like UAVs in gNB-to-gNB sensing,
    Superior sensing coverage and tracking with advanced transmitters and receivers,
    Reduced network overhead (e.g., fewer handovers) compared to other sensing modes
    Static nature of gNBs, with precisely known location, simplifies initial implementation compared to bistatic scenarios with UEs
  The OFDM waveform used in 5G is not optimal for sensing and the standards impact for important practical sensing modes is very high
Observations