## Slide 1: Way forward on AI/ML for 2nd priority cases
12th – 14th March, 2025, Incheon, KR
3GPP RAN #107
NEC, KT Corp, China Unicom, Sharp, Vivo
RP-250769

## Slide 2: Overview on Rel-19
In Rel-19, five cases for AI/ML-based positioning accuracy enhancement have been defined. After RAN#102, these cases have been categorized into two distinct priorities. The specific WID following RAN#105 is as follows:
Positioning accuracy enhancements, encompassing [RAN1/RAN2/RAN3]:
  Direct AI/ML positioning:
    (1st priority) Case 1: UE-based positioning with UE-side model, direct AI/ML positioning
    (2nd priority) Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
    (1st priority) Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning
  AI/ML assisted positioning
    (2nd priority) Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
    (1st priority) Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
  Specify necessary measurements, signalling/mechanism(s) to facilitate LCM operations specific to the Positioning accuracy enhancements use cases, if any
  Investigate and specify the necessary signalling of necessary measurement enhancements (if any)
  Enabling method(s) to ensure consistency between training and inference regarding NW-side additional conditions (if identified) for inference at UE for relevant positioning sub use cases
  Note: RAN1 will not discuss any proposals targeting 2nd priority issues in Q4 of 2024.
The primary motivation behind categorizing all the cases into two types of priorities in Rel-19 is merely to alleviate the workload, but the technical reasons supporting such categorization are insufficient.
Observation 1: There is insufficient reason to categorize the five uses as different priorities in Rel-19.

## Slide 3: Progress in Rel-19
Currently, AI/ML-based positioning accuracy enhancement is specified in RAN1, RAN2, and RAN3 currently. However, when it comes to the handling of 2nd priority cases, the working groups have yielded different results:
RAN1 agreed not to discuss 2nd priority cases in Q4 of 2024, but specification of 2nd priority cases in the first half of 2025 is not precluded.
RAN2 never discussed 2nd priority cases in the past, and RAN2 has an agreement that will preclude Case 2a and Case 2b in Rel-19.
RAN3 have no definite plan on how to deal with 2nd priority cases, as the specification impacts of Case 2a and Case 2b for RAN3 is unclear.
Observation 2: Different WGs adopt different methodologies to deal with 2nd priority cases in Rel-19.
Observation 3: Companies have proposed for the removal of 2nd priority features in Rel-19

## Slide 4: Expected progress in Rel-20 5GA
Given that we are currently in the late stage of Rel-19 and the significant number of unresolved issues related to 1st priority cases, it is highly unlikely that the standardization work for 2nd priority cases can be completed satisfactorily within the remaining time slots of Rel-19. Therefore, it is recommended that the support for 2nd priority cases be continued and specified in Rel-20 5GA. The reasons for this recommendation are as follows:
Case 2a and Case 2b show the advantages of DL positioning.
Some of the reached/to be reached agreements/conclusions in Rel-19 can be reused for Case 2a and Case 2b in principle.
  For example, Rel-19 enhanced measurement for Case 3b can be reused in Case 2b with the necessary adaptations.
After offline discussions with other companies, we propose to adopt one of the following additional alternatives:
Alt1. 2nd priority cases will be removed from Rel-19 scope, and specify them in Rel-20 5GA
Alt2. 2nd priority cases will be specified in Rel-19 scope, and not pursue them in Rel-20 5GA

## Slide 5: Summary
Observation 1: There is insufficient reason to categorize the five uses as different priorities in Rel-19.
Observation 2: Different WGs adopt different methodologies to deal with 2nd priority cases in Rel-19.
Observation 3: Companies have proposed for the removal of 2nd priority features in Rel-19
After offline discussions with other companies, we propose to consider one of the following additional alternatives:
Alt1. 2nd priority cases will be removed from Rel-19 scope, and specify them in Rel-20 5GA
Alt2. 2nd priority cases will be specified in Rel-19 scope, and not pursue them in Rel-20 5GA