## Slide 1
Huawei, HiSilicon, China Unicom, Google, LGU+, China Telecom
WF for Long Term Covariance Feedback in Rel-20 MIMO
3GPP TSG RAN#107 RP-250774
Incheon, South Korea, March 12-14, 2025
Agenda Item: 15.2.2

## Slide 2
SRS Interference issue in multi/single-TRP Network
  CJT/JR is commercially deployed by tens of operators globally. In commercial deployments, more than 10 TRPs are in a CRAN structure for CJT transmission. With large scale multi-TRP coordination (6 or 9 TRPs), significant gain can be observed especially for cell edge users, since inter-cell PDSCH interference are avoided in the multi-TRP coordination. In following preliminary evaluation results, 70%~110% performance gain for cell edge can be observed with 6TRPs and 9TRPs coordination compared to 3TRPs.
Signal S1
Residual interference S2'
  However, due to the limitation of SRS channel estimation, currently, CJT transmission is only with 2 or 3 TRPs. The key issue is that: the interference from other cells is much larger than the required SRS from remote UE in the large scale multi-TRP coordination network. As shown in the following preliminary evaluation, only enlarge the number of TRPs in the coordination group but without any SRS interference mitigation, the system performance even decrease.
  To address the SRS interference issue is also beneficial for single TRP case, especially for cell edge UE interfered by SRS transmission in neighboring cell.
Strong inter-cell interference for SRS measurement
Required SRS
Remote UE
Interference
Observation: SRS interference is a bottle neck issue which need to be addressed both for multi-/single TRP cases.
1X
Cell Average
0.9X
Cell Edge
1X
0.62X
R19 with 3 measured TRPs
R19 with 9 measured TRPs
2.1X
1X
9TRPs Coordination
6TRPs Coordination
3TRPs Coordination
1.7X
1.5X
1X
9TRPs Coordination
6TRPs Coordination
3TRPs coordination
1.36X
Large scale multi-TRP coordination
Cell Average Gain
Cell Edge Gain

## Slide 3
Solution to address SRS interference:
  To address the issue of strong interference on SRS from other TRPs, gNB can use long term channel covariance matrix （） to filter out interference and noise (e.g., using MMSE/LMMSE: ) outside the signal space to assist SRS channel estimation, while the channel covariance matrix is based on DL signal measurement and UE feedback to guarantee the accuracy.
channel energy
Signal space
Interference + noise
Signal space
Filtered out part
3.5 GHz
30kHz
7*3 Cell
200m
80% indoor 20% outdoor
20ms
64T,4R
FTP3, 50% RU
UE calculates the long term channel covariance RHH
  where channel covariance could be calculated per subband and average across subbands and time.
UE quantize the channel covariance: using DFT projection to matrix s, and select L largest coefficients to report
  is the DFT matrix
gNB recover channel covariance = , and use it to filter out interference and noise with MMSE/LMMSE channel estimation
Procedure:
Spec impact:
Only feedback coefficients of DFT projection from Covariance matrix, no new codebook introduced.
1X
1.24X
Cell Average
Cell Edge
1.48X
1X
Preliminary Simulation results
1.17X
1.39X
Single-TRP with RHH reporting
1X
Cell Average
Cell Edge
1X
1.09X
1.22X
m-TRP
s-TRP
R19 with 3 TRPs without RHH reporting
6 TRPs coordination with RHH reporting
9 TRPs coordination with RHH reporting
R19 with Single-TRP without RHH reporting

## Slide 4
Proposal
Proposal : Specify long term channel covariance feedback in R20, specifically,
    Specify procedure for covariance matrix calculation, i.e. averaging in frequency and time domain [RAN4 or RAN1]
      is with dimension Nt/2*Nt/2, where Nt is number of antennas at gNB
      Example of frequency domain averaging: 16RBs
      Example of time domain averaging: 320ms
    Specify procedure for covariance matrix quantization, i.e. projection base, reporting contents (how many values to report and number of bits per value) [RAN1]
      Example of projection base: where , N1，N2 is antennas in horizontal and vertical in a polarization
      Example of reporting contents: largest Nt/4 elements (real numbers), where each element is quantized to 4 bits
    Specify procedures for covariance matrix reporting, i.e. standalone CSI reporting for coefficients and bitmap of element position [RAN1]
      Example: Nt/4 * 4 + Nt/2=3/2 Nt bits per TRP per 320ms
  No new codebook design, Reuse legacy CSI-RS, and Up to 6 TRPs