## Slide 1: Views on 6G WG SI for REL-20
RAN#108 RP-251142
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 16.2

## Slide 2: Air Interface Security
Motivation
Confidentiality of Basic Identifiers Against Man-in-the-Middle Attacks
  Weakness of DMRS Scrambling
    Current configuration of shift-register sequences allows reasonably simple determination of scrambling seed by basic devices
  Weakness of RNTI and PDCCH scrambling
    Reasonably easy to intercept scheduling information
    Sniffing and blind detection of PDCCH and PDSCH allows for inference-type attacks on traffic profiles and network usage even if data itself is secure
Denial of Service Attacks
  Protection of RA procedure against flooding-type attacks
Covert Channel Scenarios
  Establishment of BWP supporting two-way channels with low-probability of detection signal design
Proposal
Study techniques to enhance security and confidentiality of the 6G air interface

## Slide 3: DMRS-less Transmission for Short Block Length
Motivation
Asymptotic performance of 3GPP short block length codes (Reed-Muller code) is far from optimal with significant room for improvements
DMRS constitute a significant overhead for short block length transmissions
Base-station are capable to use more complex receivers to improve decoding/coverage of uplink control channels  non-coherent receivers
Proposal
Study efficient encoding/transmission strategies in the short block length regime

## Slide 4: Cache-Aided MU-MIMO Transmission
Motivation
Significantly enhances spectral efficiency for delivery of popular multimedia content (e.g. VoD, VR) where most of the content can be cached in advance
Relies on paradigm of coded caching where memory at the receiver is used to intelligently store interfering data prior to transmission
Multiple low-dimensional MU-MIMO transmissions are super-imposed and interference is cancelled using the cached data in the device memory
Proposal
Study cache-aided transmission schemes

## Slide 5: Low-Power Waveforms
Motivation
Low-power waveforms (e.g. OOK-based) have been an add-on to 5G, e.g. Ambient IoT and LP-WUS
Resulting in significant overhead, e.g. periodic LP-SS transmissions for energy detection receivers
Proposal
Integrate waveforms for low-power detection more efficiently

## Slide 6: Summary
Study enhanced security and confidentiality of the 6G air interface
Enhanced coding schemes for short block lengths transmissions
Enhanced spectral efficiency with cache-aided MU-MIMO
Efficient integration of waveforms for low-power detection

## Slide 7: Thank You!