## Slide 1
3
Views on
Rel-20 Mobility Enhancements
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.2.8.1
Source: Ofinno
Document for: Discussion
RP-251606

## Slide 2
Conditional LTM
  Justification
    Rel-19 conditional LTM supports the intra-CU scenario. Mobility across different gNBs relies on L3 conditional handover
    Supporting the inter-CU conditional LTM will increase mobility robustness and reduce interruption during a handover to a different gNB
    Rel-19 conditional LTM is supported only on MCG, and without DC. DC is released when conditional LTM is executed
    Supporting conditional SCG LTM, and conditional MCG LTM with DC will increase mobility robustness and reduce interruption for a handover with DC
  Objective
    Support expansion of LTM scope to:
      Inter-CU conditional LTM (RAN2, RAN3, RAN4)
      conditional SCG LTM and conditional MCG LTM with DC (RAN2, RAN3, RAN4)

## Slide 3
Reduction of Resource Waste and signal overheads
  Justification
    Network reserves CG resources for RACH-less LTM after configuring the corresponding LTM to UE
    The CG resources are wasted until the UE executes the RACH-less LTM
    To release/update the CG resources, additional RRC reconfiguration for LTM configuration, which stops subsequent LTM, is required
    To improve resource utilization efficiency and avoid additional RRC reconfiguration, dynamic resource management mechanisms are needed for RACH-less LTM
  Objective
    Reduce resource waste and signal overheads by supporting:
      Dynamic management of CG resources for RACH-less LTM (RAN2, RAN3, RAN4)

## Slide 4
Expansion of LTM Scope
  Justification
    In Rel-19 discussion, it is limited that only SN can initiate the procedure for inter-SN LTM without MCG change.
    However, in legacy dual connectivity, either the serving SN or the serving MN can initiate inter-SN PSCell change
    In network deployment, MN normally has a full picture and better view than SN
    Supporting MN-initiated inter-SN LTM without MCG change will increase the freedom to configure LTM in dual connectivity
    Rel-19 inter-CU LTM is limited to using an Xn interface between a source gNB and a target gNB
    If a source gNB and a target gNB are not connected via an Xn interface, a UE is enforced to use L3 handover, which causes much longer interruption time during the switch
    NG-based inter-CU LTM will reduce those interruption time during handover procedures when an Xn interface is not available
    Rel-19 supports MCG LTM with SN addition not MCG LTM with SN change, so UE should release existing SCG configuration and add SCG configuration received within MCG LTM configuration
    Supporting MCG LTM with SN change will reduce interruption
  Objective
    Support the following LTM enhancements:
      MN-initiated inter-SN LTM without MCG change (RAN2, RAN3, RAN4)
      NG-based inter-CU LTM (RAN3)
      MCG LTM with SN change (RAN2, RAN3)

## Slide 5
Conclusion
Summary of Objectives
  Conditional LTM:
    Inter-CU conditional LTM (RAN2, RAN3, RAN4)
    conditional SCG LTM and conditional MCG LTM with DC (RAN2, RAN3, RAN4)
  Reduce resource waste and signal overheads by supporting:
    Dynamic management of CG resources for RACH-less LTM (RAN2, RAN3, RAN4)
  Support expansion of LTM scope to:
    MN-initiated inter-SN LTM without MCG change (RAN2, RAN3, RAN4)
    NG-based inter-CU LTM (RAN3)
    MCG LTM with SN change (RAN2, RAN3)

## Slide 6
contactus@ofinno.com
https://ofinno.com