## Slide 1
Huawei, HiSilicon
Rel-20 AI/ML for NR Air Interface
3GPP TSG RAN#108 RP-251646
Prague, Czech, June 09-13 2025
Agenda Item: 15.1.1

## Slide 2
Views on CSI compression with two-sided model
Summary of Rel-19 study on CSI compression
  Key conclusions on performance improvement:
    For temporal domain Case 0, compared to Rel-18 evaluations, Rel-19 evaluations show improved performance/complexity trade-off.
    Reasons for the improved performance/complexity trade-off include the use more optimized AI/ML model structures and the use of different inputs
    Temporal domain Case 2 can achieve higher gain compared to Case 0 with similar or increased complexity
    Temporal domain Case 3 can achieve better performance than Rel-18 Doppler eType II benchmark. The amount of gain of Case 3 over Rel-18 Doppler eType II benchmark is similar to the amount of gain of Case 0 over Rel-16 eType II
    On average, for each inference, FLOPs of Case 3 is higher than that of Case 0.
  Main aspects under Rel-19 study for CSI compression:
    Improving trade-off between performance and complexity/overhead
    Alleviate/resolve issues related to inter-vendor training collaboration

## Slide 3
  Key conclusions on inter-vendor collaboration: RAN1 concludes that both Direction A and Direction C are feasible. For Direction A, RAN1 concludes that the feasible sub-options are sub-option 4-1 and sub-option 3a-1, and in case of sub-option 3a-1, with and without target CSI sharing from NW side.
  Other issues that have been studied in RAN1: NW/UE side performance monitoring, NW/UE side training data collection
  RAN1 recommendations
  Testability and interoperability: RAN4 provides observations to the testability of Option 3 and Option 4
Views on CSI compression with two-sided model
Summary of Rel-19 study on CSI compression

## Slide 4
Potential scope for Rel-20 work on CSI compression
  Potential scope in Rel-20: Provide specification support for CSI compression, encompassing:
    Specify the sub-use cases of temporal domain CSI compression (Case 0) and temporal domain CSI compression Case 2 (using past CSI)
    Specify necessary signaling/mechanism(s) to enable inter-vendor collaboration
    Specify necessary signaling/mechanism(s) to facilitate LCM operations, including
    Model pairing procedure including ID and applicability reporting
    Inference aspects including target CSI type, measurement and report configuration, CQI / RI determination, payload determination, quantization configuration / codebook, UCI mapping, CSI processing criteria and timeline, priority rules for CSI reports
    NW and UE side data collection for training, considering Target CSI format
      Note: The framework defined in BM and CSI prediction use cases could be reused
    Specify performance monitoring, if needed
  Huawei assessment on the study:
    The key study is complete and is able to convert to normative work
    For use cases, cases and solutions bring promising performance gain should be preserved, e.g. Temporal domain Case 0 with channel matrix as input and Temporal domain Case 2
    For inter-vendor collaboration, if both direction A and direction C are included,
    Option 4-1 can be led by RAN1, focusing on the dataset type/format related discussion
    Both Option 3a-1 and Direction C can be led by RAN4, focusing on model standardization related aspects
    For Option 3a-1/4-1, signaling related discussion can be handled by RAN2 and/or SA WGs
Views on CSI compression with two-sided model

## Slide 5
Views on other issues of Rel-19 study
UE side training data collection for one-sided model
  Potential scope in Rel-20: Continue the study for UE side training data collection for UE-sided model
  Summary of study
    UE side training data collection for one-sided model is still under study in both RAN and SA.
    Based on the study outcome of RAN/SA (when available), TSG RAN will make a final decision on the way forward, with checkpoint in Q2, 2025
Option | Relevant WG | Progress
Option 2-UP | SA2 | SA2 approved the LS S2-2505713 (from SA2 to RAN). A new Rel-20 SID has been approved, and the study is ongoing and no conclusion has been reached yet. The study outcome is to be sent for information at Sep 2025 and for approval at Dec 2025.
Option 3-UP | SA5, RAN2 | SA5 has coordinated with RAN2 via the LS R2-2501759 (from SA5 to RAN, RAN2) and R2-2503168 (from RAN2 to SA5). SA5’s view: UP tunnel between UE and server is the same as Option 1a; UE tunnel between UE and 5GC is the same as Option 2. RAN2’s view: UP tunnel between UE and gNB is not considered for 5G-A Rel-19/20. Based on the clarifications, Option 3-UP can be categorized to other options.
Option 2/3-CP | RAN2 | RAN has already concluded that transfer of data over CP for Solution 2 and 3 can meet the visibility and controllability RAN requirements. RAN2 is discussing scalability with CP solution related to large amount of data (if there is a large amount of data) to be transferred for a UE.

## Slide 6
Model identification
Model transfer/delivery
  Potential scope in Rel-20: Consider model identification as part of the normative work of CSI compression, included by “Model pairing procedure including ID and applicability reporting”
  Summary of study
    RAN1 has concluded Model identification is applicable to two-sided model
    No study at RAN2
  Observation: Model transfer/delivery are mainly motivated for two sided CSI compression use cases
  Summary of study
    RAN1 has concluded the feasibility of Option 3a-1 for two-sided model, and has no consensus for model transfer/delivery of one-sided model
    No study at RAN2
Views on other issues of Rel-19 study

## Slide 7
There is strong need to explore new use cases with high gains obtainable in widely deployed scenarios in Rel-20 for 5G-Advanced, to make AI/ML more likely to be commercialized
The Rel-19 use cases for AI/ML air interface are exemplary and not all of them are related to widely commercialized features
  Beam management: not widely commercialized
  Positioning: not widely commercialized
  CSI compression: focuses on FDD in Rel-19
  CSI prediction: focuses on FDD
Adoption of AL/ML in commercial deployments requires strong justification from cost-benefit point of view. New use cases, with high gains obtainable in widely deployed scenarios, make AI/ML features more likely to be commercialized.
The start of commercialization for AI/ML air interface in 5G-A can pave the way for commercialization from day 1 in 6G.
Potential way to explore new use cases for 5G-A
Option 1: Study and specify a limited set of new use cases for AI/ML air interface for 5G-Advanced in Rel-20 5G-A WI, e.g. overlaid DMRS and data with one-sided AI/ML channel estimation
Option 2: Study new use cases for AI/ML air interface in Rel-20 6G SI, and specify the applicable use cases for 5G-A in Rel-21 depending on the outcome of the study in Rel-20
Views on whether to explore new use cases for 5G-A

## Slide 8
Summary
  Proposal 1: Provide specification support for CSI compression, encompassing:
    Specify the sub-use cases of temporal domain CSI compression (Case 0) and temporal domain CSI compression Case 2 (using past CSI)
    Specify necessary signaling/mechanism(s) to enable inter-vendor collaboration
    Specify necessary signaling/mechanism(s) to facilitate LCM operations, including
    Model pairing procedure including ID and applicability reporting
    Inference aspects including target CSI type, measurement and report configuration, CQI / RI determination, payload determination, quantization configuration / codebook, UCI mapping, CSI processing criteria and timeline, priority rules for CSI reports
    NW and UE side data collection for training, considering Target CSI format
      Note: The framework defined in BM and CSI prediction use cases could be reused
    Specify performance monitoring, if needed
Proposal 2: Continue the study for UE side training data collection for UE-sided model
Proposal 3: Take one of the following options to explore new use cases for 5G-A:
    Option 1: Study and specify a limited set of new use cases for AI/ML air interface for 5G-Advanced in Rel-20 5G-A WI, e.g. overlaid DMRS and data with one-sided AI/ML channel estimation
    Option 2: Study new use cases for AI/ML air interface in Rel-20 6G SI, and specify the applicable use cases for 5G-A in Rel-21 depending on the outcome of the study in Rel-20