## Slide 1: Release 20 5G-Adv RAN1/RAN2/RAN3/RAN4 Package
RAN/RAN1/RAN2/RAN3/RAN4 Chairs
Tdoc#: RP-250859

## Slide 2: Outline
References
Overall Release 20 5G-Adv package for RAN1, RAN2, RAN3, RAN4
  General guidance
  RAN1-led topics
  RAN2-led topics
  RAN3-led topics
  RAN4-led topics
Appendix
  RP-250812 endorsed slides

## Slide 3: References
Summary for RAN Release 20 5G-Adv in RP-250812
  General guidance and potential RAN1-led, RAN2-led, and RAN3-led items along with their first-order TU allocations were endorsed (slides 7 ~ 23 of RP-250812)
Additional details can be found in following moderator summaries
    RP-250802 Moderator's summary for RAN1 led REL-20 topics RAN1 Chair (Samsung)
    RP-250803 Moderator's summary for RAN2 led REL-20 topics RAN2 Chair (InterDigital)
    RP-250787 Moderator's summary for RAN3 led REL-20 topics RAN3 Chair (ZTE)
    RP-250797 Moderator's summary for other RAN1/RAN2/RAN3 led REL-20 topics RAN Vice Chair (Deutsche Telekom)
    RP-250817 Moderator's summary for RAN4 led REL-20 topics RAN4 Chair (Huawei)

## Slide 4: General Guidance
It is critical to ensure all WGs’s load for 5G-Advanced Rel-20 is reasonable, and that sufficient TUs should be given to 6G to ensure successful study for future 6G success
All approved items should address real and critical commercial deployment needs
The scope for each 5G-Adv project should be finalized with careful consideration on required workload – not only on primary working group but also on the secondary working group(s)
The scope for each 5G-Adv project should have clarity – avoid scope which leaves room for interpretation and possibly wide range of enhancements

## Slide 5: Overall Release 20 5G-Adv Package for RAN1, RAN2, RAN3, RAN4

## Slide 6: RAN1-led Topics (1/3)
AI/ML Air Interface: Work item
  Focus on CSI compression for two-sided model
    Further discuss how to handle inter-vendor collaboration
    Further discuss and down-select which CSI compression cases to support (e.g. with/without temporal aspects, with prediction, …)
  Further discuss how to handle data collection
  No new use cases in Release 20, no further work on Rel-19 positioning 2nd priority cases in Release 20
Ambient IoT
  Study item (9 months, start in 2025.Q3) – RAN1 and RAN4
    Study outdoor scenarios including whether new device type is necessary or existing device type can be used (e.g. device 2B in outdoor scenarios)
    In RAN#111 (March, 2026), decide whether or not to include outdoor scenarios as part of Rel-20 A-IoT WI
  Work item (start in 2025.Q4 in RAN2 and RAN3, start in 2026.Q1 in RAN1)
    Specify support for D1T1 + Device 2B (RAN1-led), D2T2 + Device 1/2B (RAN2-led), DO-A traffic
    Update the WID to reflect outcome of Rel-20 A-IoT study item on outdoor scenarios in RAN#111

## Slide 7: RAN1-led Topics (2/3)
MIMO: Work item
  Focus on the following for further down-selection (at most 3 items from this list):
    Cross-slot SRS, SRS frequency hopping for partial sounding
    Asymmetric DL sTRP/UL mTRP beam management enhancements
    Early SRS/CSI/CSI-RS triggering for UEs in IDLE/INACTIVE to CONNECTED; and SCell activation/out-of-dormancy in CONNECTED
    CSI-RS frequency domain overhead reduction for larger number of ports
Coverage Enhancement: Work item
  Multiple PRACH TX over different beams including beam selection for Msg3
  PUSCH repetition scheduled by DCI 0_0 with C-RNTI
  Specify enhancements to improve PUSCH coverage for high uplink data rate by extending pi/2-BPSK to more MCS entries in MCS tables
  Check if RAN2 TU is needed

## Slide 8: RAN1-led Topics (3/3)
NR-NTN (GNSS resilient operation): Study item
  RAN1-led study item on GNSS resilient operation for 4 quarters (starting in 2025.Q3)
    Check in RAN#112 (June, 2026) to decide whether to proceed with normative work, extend the study item, or postpone normative work to Release 21
  Avoid duplicated work under 6G study related to GNSS resilient or GNSS free support
ISAC: Study item
  RAN1-led study item focusing on UAV use case for 3 quarters (starting in 2025.Q3)
    Check in RAN#111 (March, 2026) to decide whether to proceed with RAN3 only normative work
  Focus the study item on the following areas
    Evaluate the performance of gNB mono-static mode for UAV use case [RAN1]
      At least NR waveform/RS should be used for evaluation
    Study network architecture for gNB mono-static mode for UAV use case [RAN3]
      Including study on the support of bistatic mode using this network architecture
    Study the procedures and signaling support between RAN and CN, and the corresponding sensing measurements [RAN3, RAN1]

## Slide 9: RAN1 TU Allocation
Rel-20 RAN1 WI/SI | 2025.Q3 | 2025.Q4 |  | 2026.Q1 | 2026.Q2 |  | 2026.Q3 | 2026.Q4 |  | 2027.Q1
 | RP#109 | RP#110 |  | RP#111 | RP#112 |  | RP#113 | RP#114 |  | RP#115
 | R1#122 | R1#122b | R1#123 | R1#124 | R1#124b | R1#125 | R1#126 | R1#126b | R1#127 | R1#128
Nominal TUs for maintenance | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 
Additional TUs for maintenance | 8 | 4 | 4 | 2 | 0 | 0 | 0 | 0 | 0 | 
Misc. impact from other WGs |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
Reserved TUs | 2.5 | 3 | 3 | 2.5 | 3 | 3 | 2 | 2 | 2 | 
Rel-20 TEI |  |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 
AI/ML Air Interface | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 
A-IoT (Study Item) | 3.5 | 3.5 | 3.5 | 2 |  |  |  |  |  | 
A-IoT (Work Item) |  |  |  | 1.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 
NR-MIMO | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
Coverage Enh |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  |  |  | 
ISAC (Study Item) | 1 | 1 | 1 | 1 |  |  |  |  |  | 
NR-NTN GNSS resilient (SI, WI – TBD) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
IoT-NTN (RAN2-led) |  |  |  | 0.5 | 0.5 | 0.5 |  |  |  | 
6G study | 8 | 10 | 10 | 12 | 14 | 14 | 16 | 16 | 16 | 16
Total RAN1 TUs | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 
NR-NTN GNSS resilient: TUs for 2026.Q3 and 2026.Q4 are pre-allocated for a possible WI depending on the outcome of study item and decision in RAN#112

## Slide 10: RAN2-led Topics (1/2)
AI/ML Mobility: Work item
  Use endorsed scope for AI/ML mobility in RP-250812 for WID finalization
NB-IoT-NTN: Work item
  Work item on voice over NB-IoT-NTN via GEO in Release 20 5G-Adv
    Study phase until 2026.Q1 to down-select between control plane and user plane. Check point in RAN#111 (March, 2026)
  Consider how to coordinate with SA
NR-NTN: Work item
  Support E-UTRA TN to NR NTN handover in RRC connected mode
Mobility Enhancement: Work item
  Use endorsed scope for mobility endorsement in RP-250812 for WID finalization
  Further discuss whether the following objective for RAN4 is needed
    Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4]. ????

## Slide 11: RAN2-led Topics (2/2)
XR: Work item
  Use endorsed scope for XR in RP-250812 for WID finalization
  Further discuss whether the following objective for RAN3 is needed
    [Specify coordination between gNB and CN to enable/disable N3 interface delay measurement from CN to gNB, for better latency guarantee [RAN3]
UAV
  Specify a UAV/UAM specific frequency/cell/beam prioritization mechanism for IDLE/INACTIVE mobility.
    Can be handled as a candidate RAN2 TEI19 or TEI20 proposal
  CHO: Do not further pursue in Rel-20

## Slide 12: RAN2 TU Allocation
RAN2 TU has been added for (RAN3-led) SON/MDT which was missing in RP-250812
Rel-20 RAN2 WI/SI | 2025.Q3 | 2025.Q4 |  | 2026.Q1 | 2026.Q2 |  | 2026.Q3 | 2026.Q4 |  | 2027.Q1 | 2027.Q2 | 
 | RP#109 | RP#110 |  | RP#111 | RP#112 |  | RP#113 | RP#114 |  | RP#115 | RP#116 | 
 | R2#131 | R2#131b | R2#132 | R2#133 | R2#133b | R2#134 | R2#135 | R2#135b | R2#136 | R2#137 | R2#137b | R2#138
Nominal TUs for maintenance |  | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 |  | 
Additional TUs for maintenance |  | 18 | 18 | 12 | 7 | 7 |  |  |  |  |  | 
Misc. impact from other WGs |  |  |  |  | 0.5 | 0.5 | 1 | 1 | 1 | 1 |  | 
Reserved TUs |  | 3 | 2.5 | 3 | 2 | 2 | 4 | 3.5 | 3.5 | 3.5 |  | 
Rel-20 TEI |  |  |  |  |  |  | 1 | 1 | 1 | 1 |  | 
AI/ML Mobility |  | 0.5 | 0.5 | 1 | 1.5 | 1.5 | 1.5 | 1 | 1 | 1 |  | 
IoT-NTN |  |  | 0.5 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 |  | 
Mobility Enh |  |  |  | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 |  | 
XR |  |  |  | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 |  | 
(RAN1-led) NR-NTN (SI, WI - TBD) |  |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  | 
(RAN1-led) AI/ML Air Interface |  |  |  | 1 | 2 | 2 | 2 | 2 | 2 | 2 |  | 
(RAN1-led) Ambient IoT |  | 0.5 | 0.5 | 1 | 2 | 2 | 2 | 2 | 2 | 2 |  | 
(RAN1-led) MIMO |  |  |  |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 |  | 
(RAN1-led) Coverage Enh - TBD |  |  |  |  |  |  |  |  |  |  |  | 
(RAN3-led) SON/MDT |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  | 
6G study |  | 4 | 4 | 6 | 7 | 7 | 10 | 11 | 11 | 11 | 11 | 11
Sum of Assigned TUs |  | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 11 | 11
RAN2 TU Capacity |  | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40

## Slide 13: RAN3-led Topics
AI/ML for NG-RAN
  Select one of the following use cases
    QoE Optimization;
    Network energy saving
    Mobility (including Multiple-hop target node UE trajectory)
SON/MDT
  Focus on MRO enhancement for R19 LTM targeting specific use case (e.g. inter-CU LTM, LTM with dual connectivity, conditional LTM) [RAN3, RAN2]

## Slide 14: RAN3 TU Allocation
ISAC: First half of the TU allocation is for SI. TUs for 2026.Q3, 2027.Q1, 2027.Q2 are pre-allocated for a possible WI depending on the outcome of the SI and decision in RAN#112
Rel-20 RAN3 WI/SI | 2025.Q4 |  | 2026.Q1 | 2026.Q2 |  | 2026.Q3 | 2026.Q4 |  | 2027.Q1
 | RP#110 |  | RP#111 | RP#112 |  | RP#113 | RP#114 |  | RP#115
 | R3#129b | R3#130 | R3#131 | R3#131b | R3#132 | R3#133 | R3#133b | R3#134 | R3#135
TUs for LSs/TEIs/maintenance | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Additional TUs for TEIs/maintenance | 3.5 | 3.5 | 2 | 0.5 | 0.5 | 0 | 0 | 0 | 0
Reserved TUs including misc. impact from other WGs | 1 | 1 | 1 | 1 | 1 | 1.5 | 1.5 | 1.5 | 1.5
Comebacks | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
AI/ML for NG-RAN | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SON/MDT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
ISAC (SI, WI - TBD) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
(RAN1-led) Ambient IoT | 0.5 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 | 1
(RAN2-led) Mobility |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
(RAN2-led) XR - TBD |  |  |  |  |  |  |  |  | 
6G study | 4 | 4 | 5 | 6 | 6 | 6 | 6 | 6 | 6
Sum of Assigned TUs | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19
RAN3 TU Capacity | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19

## Slide 15: RAN4-led Topics
Similar to RAN1/RAN2/RAN3, it is critical to ensure adequate 5G-Adv Rel-20 workload considering sufficient TUs for 6G study
  When finalizing RAN1, RAN2, RAN3 study/work items, relevant RAN4 workload needs to be carefully checked and reflected accurately
Proposal: For the approval of new packages — whether led by RAN4 or other working groups—it is proposed that, starting from Release 20, all RAN4 TUs be combined into a single pool rather than allocating separate TUs for RF and RRM/Demod
  The current 50-50 TU split between RF and RRM/Demod was established a long time ago and no longer reflects the actual distribution of work. The actual TU allocation depends on the specific package being approved and cannot be reliably determined in advance.
  For each approved WI/SI, the TU distribution between RF and RRM/Demod should still be detailed in the corresponding WID/SID.
  TU requests for core and performance components should continue to be submitted separately as before.

## Slide 16: RAN4 TU Allocation
Preliminary Rel-20 RAN4 TU status taking into account, maintenance, 6G study, the expected impact from RAN1/RAN2/RAN3, and 3 TU allocation for spectrum related RAN4 work
Rel-20 RAN4 WI/SI | 2025.Q4 |  | 2026.Q1 | 2026.Q2 |  | 2026.Q3 | 2026.Q4 |  | 2027.Q1 | 2027.Q2 | 
 | RP#110 |  | RP#111 | RP#112 |  | RP#113 | RP#114 |  | RP#115 | RP#116 | 
 | R4#116b | R4#117 | R4#118 | R4#118b | R4#119 | R4#120 | R4#120b | R4#121 | R4#122 | R4#122b | R4#123
Nominal TUs for maintenance | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 |  | 
Additional TUs for maintenance | 2.5 | 2.5 | 1 |  |  |  |  |  |  |  | 
Reserved TUs | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | 4 |  | 
Rel-19 Performance | 18 | 18 | 13.5 |  |  |  |  |  |  |  | 
Non-Spectrum related | First order TU allocation to be decided in RAN#108 |  |  |  |  |  |  |  |  |  | 
Spectrum related | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  | 
(RAN1-led) AI/ML for Air Interface | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 |  | 
(RAN1-led) MIMO | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  | 
(RAN1-led) Coverage Enh |  |  |  | 0.5 | 0.5 | 0.5 |  |  |  |  | 
(RAN1-led) Ambient IoT (Study Item) | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  |  |  |  |  | 
(RAN1-led) Ambient IoT (Work Item) |  |  |  | 1 | 1 | 1.5 | 1.5 | 1.5 | 1.5 |  | 
(RAN1-led) NR-NTN GNSS resilient (SI, WI - TBD) |  |  | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 |  | 
(RAN2-led) NR-NTN |  |  | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 |  | 
(RAN2-led) AI/ML Mobility | 0.5 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 
(RAN2-led) Mobility Enhancement |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |  | 
6G study | 7 | 7 | 10 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20
Sum of Assigned TUs | 40.5 | 40.5 | 39 | 38 | 38 | 38 | 37.5 | 37.5 | 37.5 | 20 | 20
RAN4 TU Capacity | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45

## Slide 17: Appendix: RP-250812 Endorsed Slides

## Slide 18
A list of items organized by the leading WG (RAN1/2/3) are provided in the following, which is to be used for subsequent discussion till RAN#108
  No email discussion is intended during 2Q’2025
The final topics for Rel-20 (RAN1/2/3) are expected to be discussed and finalized at RAN#108
  The topics captured in the following slides are subject to discussion and justification, and may be potentially split, consolidated, or dropped, until RAN#108
  Additional topics can be considered as part of Rel-20 considering strong commercial needs and overall workload
  It is critical to ensure all WGs’s load for 5G-Advanced Rel-20 is reasonable, and that sufficient TUs should be given to 6G to ensure successful study for future 6G success
  In approving RAN1/2/3-led projects in RAN#108 (see also RP-243292)
    Some RAN1/2/3 WG capacity (in terms of # TUs) will be reserved ([~10%]); All WGs would have dedicated TUs to handle impacts from other WGs (including other WG-led projects and misc. impact within RAN and from other TSGs)
A first order estimate of the expected TU for the leading WG is also provided for each project
  The final TU allocation (including both the primary and second WGs) is to be decided in June; The detailed TU allocation may be different across WG meetings and/or across different projects; The scopes for each item are to be further discussed in RAN#108
General Guidance

## Slide 19
List of Potential RAN1-led Items for Subsequent Discussion till RAN#108
Title | First-order TU Estimate (# TUs)
Enhancements on AI/ML Air Interface | [2]
NR-MIMO Phase 6 | [1]
Enhancements on Ambient IoT | [3 ~ 3.5]
NR-NTN Enhancement | [1]
Coverage Enhancement | [0.5 for 3 quarters]
(RAN2-led) IoT-NTN | [0.5 for 2 quarters]
ISAC | [1 for 3 quarters]
RAN1 total capacity is 31 TUs
Reserved TUs: 2 TUs per meeting
Miscellaneous impact from other WGs: 1 TU per meeting
Maintenance (12 TUs per meeting in Q3, 8 TUs per meeting in Q4, eventually decreasing to 4 TUs per meeting)
Rel-20 TEI: 0.5 TU per meeting (in last 2~3 quarters of Rel-20)
Additional details can be found in moderator summary in RP-250802
RP-250802 Moderator's summary for RAN1 led REL-20 topics RAN1 Chair (Samsung)

## Slide 20
List of Potential RAN2-led Items for Subsequent Discussion till RAN#108
Additional details can be found in moderator summary in RP-250803
RP-250803 Moderator's summary for RAN2 led REL-20 topics RAN2 Chair (InterDigital)
Title | First-order TU Estimate (# TUs)
AI Mobility | [1.5]
NTN IoT | [1]
Mobility | [1]
XR | [1]
(RAN1 led) AI PHY | [2]
(RAN1 led) Ambient IoT | [2]
(RAN1 led) MIMO | [0.5]
(RAN1 led) NR NTN | [0.5]
RAN2 total capacity is 40 TUs
Maintanence: 14 TUs
Reserved TUs (~10% capacity): 4 TUs
TEI20: 1 TU
Other impacted WGs: 1 TU
TUs left for Rel-20 5G A and 6G: 20

## Slide 21
RAN2: AI/Mobility
Only the following objectives are considered as baseline:
Specify support for RRM measurement prediction for both UE and network sided models [RAN2]:
  Specify signalling and protocol aspect to enable reporting inference outcome of UE sided model for RRM measurement prediction
  Specify signalling and protocol aspect to enable reporting information from UE for inference operation of network sided model for RRM measurement prediction
  At least the use cases studied so far in RAN2 SI are supported: Temporal domain prediction and Frequency domain prediction. FFS Spatial domain pending RAN2 Study progress. FFS Cell level vs beam level prediction
NOTE: network sided models can be concluded in RAN#108 after RAN2 discussions
  Specify support for measurement event prediction for UE sided models [RAN2]:
  Specify signalling and protocol aspect to enable reporting inference outcome of UE sided model for measurement event prediction
  For both RRM measurement prediction and measurement event prediction [RAN2]:
  Specify signalling and protocol to facilitate functionality-based LCM procedures
  To be based on the LCM framework for Rel-19 AI/ML for NR air interface WI as much as possible
  For both RRM measurement prediction and measurement event prediction: [RAN4]
  Specify core requirements identified in study item phase
  Specify LCM-related requirements, if any

## Slide 22
RAN2: Mobility
The following objectives are considered as baseline for Rel-20
Specify LTM SCell improvements for further reducing interruption delays
  SCell activation
    Specify the necessary configuration and UE procedures for NW triggering of LTM SCell activation with LTM cell switch [RAN2, RAN3].
    Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4].
NOTE: Reuse the candidate cell LTM measurement and reporting procedures where possible for the SCell improvements
NOTE: This objective is NOT applicable to non-co-located CA and is NOT applicable to C-LTM
NOTE: This objective is applicable to MCG and SCG
Dynamic L1 measurement and reporting configuration change
  Specify the necessary configuration and procedures for MAC CE based configuration selection among prior provided RRC configurations of UE L1 measurement and reporting LTM configuration [RAN2]
  Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4]. ????
NOTE 1: This sub-objective is applicable to C-LTM as well.
NOTE 2: For this objective, we strive to avoid RAN1 impact (including reporting)
NOTE 3: RAN1/RAN3/RAN4(?) involvement is based on LS if necessary
No further RAN2 objectives are considered for Rel-20

## Slide 23
RAN2: XR
The following objective is used as a starting point for XR WI:
  Study and specify (if justified) potential enhancements (e.g., mobile AI awareness, PDU set for mobile AI data), for uplink mobile AI traffic by taking into account transmission characteristics of uplink mobile AI traffic [RAN2]
  The study focuses on identifying potential RAN protocol enhancements.
  NOTE: RAN2 will discuss/understand the transmission characteristics before discussing possible enhancements
  Checkpoint in RAN#113 to determine whether we do normative work and the potential scope of normative work for the first objective
The following objective will be discussed and refined in RAN#108. Further refinement on the objective to limit the impact to SA2.
  [Specify coordination between gNB and CN to enable/disable N3 interface delay measurement from CN to gNB, for better latency guarantee [RAN3]

## Slide 24
RAN2: NR NTN
Conclusion for GNSS resilient operation
Study Item with checkpoint to determine whether we have normative work and the scope based on results of study item phase.
  Study should consider Rel-16 as baseline for discussion. Study should focus on NR NTN and be backward compatible with legacy UEs. Aim to minimize physical layer procedures impact to 5GA and avoid physical layer channel/signal changes.
  Objective to be narrowed down for RAN#108
No additional NR NTN enhancements with RAN1 impact can be considered at this point given limited 5GA TUs
Additional topic to be included in objective.
Specify necessary enhancements to support E-UTRA TN to NR NTN handover in RRC connected mode
TU estimate RAN2 (0.25 TU), RAN4 (0.5)
Deadline to complete the work (first half of release)

## Slide 25
RAN2: NTN IoT
Only the following objective will be considered as baseline for IoT NTN WI:
Voice over NB-IoT-NTN via GEO
  Study phase for 1 or 2 Quarters to downselect between CP or UP. Checkpoint by RAN#1xy (TBD)
  Work on detailed objectives for RAN#108

## Slide 26
RAN2: UAV
As a starting point we consider:
  Specify a UAV/UAM specific frequency/cell/beam prioritization mechanism for IDLE/INACTIVE mobility. TBD next meeting whether we have a separate WI or TEI
  FFS CHO for RAN#108
If this is a WI, the work should be completed in 2 Quarters

## Slide 27
Title | First-order TU Estimate (# TUs)
AI/ML for NG-RAN | [1-1.5]
(RAN1-led) Ambient IoT | [1]
SON/MDT Enhancements | [0.5-1]
ISAC | [1]
List of Potential RAN3-led Items for Subsequent Discussion till RAN#108
RAN3 total capacity is 19 TUs
~10% RAN3 capacity is planned to be reserved
~[1] TU reserved per meeting including additional TU for TEI/maintenances
Additional details can be found in moderator summary in RP-250787
RP-250787 Moderator's summary for RAN3 led REL-20 topics RAN3 Chair (ZTE)

## Slide 28
The following to be endorsed as WF:
Rel-20 AI/ML for NG-RAN should be based on current 5G architecture and interfaces.
The objectives of AI/ML for NG-RAN in Rel-20 are listed below:
  Study the following new AI/ML based use cases and down-scope (1 or 2 use cases) in next plenary [RAN3]:
    QoE Optimization;
    Network energy saving
    Mobility (including Multiple-hop target node UE trajectory)
  Note: Other Leftovers depend on Rel-19 outcome, if any.
  Note: Coordination based on LSs with other working groups, when needed.
6 months for the Rel-20 Study Item on AI/ML for NG-RAN, followed by 12 months for the subsequent Work Item.
RAN3: AI/ML for NG-RAN

## Slide 29
The following to be endorsed as WF:
The objectives of SON/MDT in Rel-20 including and to be down-selected on the following (1 or 2 use cases):
  MRO enhancement for R19 LTM (the detail scope should be limited and needs to be further checked based on the progress in R19 LTM). [RAN3, RAN2]
  Support of SON/MDT enhancements for UAV or LP-WUS/WUR [RAN3, RAN2]
Note: Coordination with other working groups when needed.
18 months for the Rel-20 SON/MDT WI.
RAN3: SON/MDT

## Slide 30
RAN3: ISAC
The following are discussed and to be further checked in RAN#108:
The discussion on sensing/ISAC in 5GA and 6G are independent.
A set of possible objectives of Sensing/ISAC in Rel-20 are listed below:
  Study on gNB mono-static mode and possibly bi-static mode for UAV use case. [RAN3, RAN1]
  Study the procedures and signaling support between RAN and CN, and the corresponding sensing measurements. [RAN3, RAN1]
  Performance evaluation for gNB sensing. [RAN1]
  Note: No new waveform/RS to be specified in RAN1 and no UE impact is expected.
  Note: Coordination with SA2 when needed.

## Slide 31
200 MHz and Others Topics for Rel-20 5G-A topics
For RAN#108, focus on the following topics:
  200 MHz CBW or aggregated BW for n104
  SBFD (limited scope)
  Sidelink enh. (incl. SL relay)*
Additional details can be found in moderator summary in RP-250797
RP-250797 Moderator's summary for other RAN1/RAN2/RAN3 led REL-20 topics RAN Vice Chair (Deutsche Telekom)

## Slide 32
RAN4 Considerations
It is critical to maintain RAN4 load reasonable
  The load from the projects led by RAN1/2/3
    An estimate of RAN4 TU impact is necessary for all RAN1/2/3-led items
    A certain amount of RAN4 capacity is to be reserved when approving the package in June
  The load from RAN4-led projects
It is critical to make sure the projects are rooted in commercial interests
  For any RAN4-led non-spectrum related projects to be further considered for Rel-20, strong commercial need and overall workload shall be considered!
    Note: it is NOT intended to be “number counting” driven discussion, but rather as an indication of some tangible commercial interests
To organize RAN#108 agenda for RAN4 Rel-20 as (Note: no discussion on spectrum related items)
  General
  Candidate RF/OTA Topics for Rel-20
  Candidate Demod/RRM Topics for Rel-20
  Candidate Topics Impacting both RF/OTA and Demod/RRM for Rel-20
  Others