## Slide 1
RAN#108 June 2025
Agenda 15.4.4
RP-250891
3 MHz (e)Redcap
Rel-20 Proposal

## Slide 2
LTE to 5G Migration – The Reason for (e)Redcap
Several MNOs (Anterix, SouthernLinc, Rakuten) and NTN operators only have or utilize a single 3 MHz CBW low band allocation of FDD spectrum
E.g. Band n106, n26 , n28 and NTN bands requiring 3 MHz CBW like n255, n253, n251, n250
Most devices are for IoT services and utilize LTE CAT-M1 or NB-IoT.
Network transition to 5G requires update of devices to support 3 MHz CBW for NR IoT use cases.
Low cost, power efficient (e)Redcap enabled 5G devices are necessary to supplement the millions of existing LTE IoT devices. Up to 50% less cost.
Potential 6G mIoT timeline uncertain and MNOs need a 5G transition path for IoT devices
Prior to 3 MHz 5G upgrade need low cost LTE CAT-M1 and NB-IoT solution

## Slide 3
Why 3 MHz RedCap (Rel-20) Matters Now
  Migration from LTE CAT-M/NB-IoT to 5G is urgent and unavoidable.
  Anterix, Southern Linc, Rakuten and several NTN operators require low-cost, low-complexity 5G SA solutions for existing 3 MHz spectrum blocks (e.g., Band n106, n26, n28, n255..etc).
  Utilities and IoT networks need solutions today.
Wide industry support in 3GPP
  Anterix, Nokia, Southern Linc, Futurewei, Itron, Sony, T-Mobile, Qualcomm, Rakuten Mobile, Semtech, Nordic Semiconductor, Aalyria Technologies, Novamint, Viasat, Immarsat, Ericsson
Leverages existing RedCap features (Rel-17/18/19) with added support for 3 MHz (15 PRB) channel bandwidth.
  Reduced complexity (no CA/DC, reduced modulation)
  Power efficiency (eDRX)
  Coverage & control optimizations
  NTN support
  Standalone 5G only
Summary – Strategic Need

## Slide 4
Proposed 3 MHz (e)Redcap WI/SI features
Utilize existing (e)Redcap capabilities defined in Rel-17, Rel-18 and Rel-19 unless otherwise specified.
  1 Rx and/or 1 Tx antenna support, No CA/DC, Reduced modulation: Max 64-QAM DL, 16-QAM UL, Reduced MIMO, Power-saving: eDRX, small data transmissions, RRM measurement relaxations, Standalone (SA) only, No UL beam management, HD/FD-FDD operation, Early UE identification support, Small data transmission optimizations, NTN support
RAN4 led WI to support less than 5 MHz FR1 CBW and to support deploying NR in spectrum allocations for (e)Redcap in bands supporting 3 MHz (15 PRB) channel bandwidth
  e.g. Band n106, n85, n26, n28 and NTN bands requiring 3 MHz channels such as n255, n253, n251, n250
  Support 15 PRB implementations of 3 MHz channel bandwidths
  FR1
  15 kHz SCS

## Slide 5
Additional <5 MHz (e)Redcap) WI/SI features
Specify core RRM requirements while minimizing specification impact to support operation in 3 MHz (15 PRB) channel bandwidth led by RAN4.
Mostly RAN 4 led items such as
  Specify necessary RRM performance requirements (RAN4)
  Specify necessary UE RF requirements, demodulation performance and CSI reporting requirements (RAN4)
  Specify necessary BS demodulation performance requirements (RAN4)
  Specify necessary BS conformance tests (RAN4)
Minimal work for RAN1 if necessary, i.e. specify cell edge performance issues
Minimal work for RAN2 on data rates, removing 3 MHz restrictions for certain UE/capabilities

## Slide 6
Anterix is seeking a low cost and low complexity solution for existing NB-IoT and CAT-M1 devices to migrate to 3 MHz 5G networks using (e)RedCap enabled modules.
  Moving to 5G SA and increased throughput for next generation use case(s) are accelerating demand for a solution.
  E.g. meter data rate 5 Mbps exceed NB-IoT and CAT-M1 specs.
Anterix, Southern Linc and Rakuten networks need an upgrade path for lower cost devices in our spectrum portfolio
  Potential 6G Massive IoT solution features and timeline unknown.
Multiple NTN networks will deploy 3 MHz channels and will also require (e)RedCap support for outdoor broadband IoT, small drones and other low-cost devices that exceed the requirements supported by NB-IoT.
Network Operator Needs for 5G (e)Redcap
Imminent and crucial need to get support for 3 MHz (e)Redcap for multiple global network operators.

## Slide 7: Thanks
Emil Olbrich
eolbrich@anterix.com

## Slide 8
Use Case and Market Growth Examples

## Slide 9
2023 there were 149.9 million electric smart readers in the North American market
  3.8% CAGR.
  80% market penetration
  Expected to reach 94% market penetration by 2028
1st generation Advanced Metering Infrastructure (AMI) is mix on non-3GPP and 3GPP technologies.
  Reaching EOL starting in 5 years
5G Opportunities with Meter Growth
Source: Research and Markets June 2024

## Slide 10
Transition from AMI 1.0 to AMI 2.0 signifies a substantial evolution in smart meter technology. Use cases include:
  location awareness
  active transformer load monitoring
  load management
  EV supply management.
These new use cases, in addition to existing use cases, are adding a significant increase in data demand and increased system utilization with peak data throughputs of 5 Mbps per device and less than a few seconds end-to-end latency.
  Exceeds NB-IoT & CAT-M1 specifications
Use Case Demand