## Slide 1: Overview of RAN4-led Rel-20 package
3GPP TSG RAN#108
Prague, Czech Republic
9th – 13th June, 2025
RP-250903

## Slide 2
RAN4 5G-A package should include only topics that are immediately implementable and beneficial for the ecosystem or foundational for 6G readiness.
Majority of the RAN WG capacity should be for 6G:
Aim for around 30% / 70% split between 5G-A & 6G.
Focus on big picture of Release 20,
while keeping the package reasonable

## Slide 3: BS RF
High priority topics:
  Enhancement of co-location and co-existence requirements
    OTA co-location requirement designed for BS up to 3 GHz
    New solution needed to cover co-location testing for higher frequencies and large antenna panels
  OTA requirements enhancement
    At least in-band and out-of-band blocking levels to be re-evaluated
Other topics:
  NB-IoT in AAS BS specifications
    In-band scenario can be considered

## Slide 4: UE RF Non-spectrum
Principles:
The greatest benefits for the ecosystem today would come from specifying high power classes for FWA using existing power amplifier designs, i.e. PC2 and PC3.
Combining existing PAs brings the additional benefit of making UL-MIMO inherently implementable.
  In order to maximize the benefits of this work, UL-MIMO could be considered mandatory for 4 Tx “PC1bis” FWA devices (where PC1-bis corresponds to devices with 4 x 26dBm = 32dBm)
HPUE should be the only objective, in order to keep the 5G-A package size reasonable.
Detailed objective:
High power PC1.5/PC1 UE for TN single carrier in NR FR1
  PC1bis* with 4Tx with 4-layer UL-MIMO for FWA.
  PC1bis* with 8Tx with 8-layer UL-MIMO for FWA
    Redo coexistence studies for FWA UE to see if ACLR can be relaxed.
  PC1.5 FDD with 2Tx handheld and FWA
  *) 32 dBm

## Slide 5: UE RF Spectrum items
Rel-20 basket WIs should be power class agnostic.
Rel-19 HPUE baskets should be merged into the Rel-20 proposed “normal” baskets as shown in table.
All band-related feature baskets are merged into NR_bands_xFeature_20
New operating bands can be considered based on operator requests
Rel-19 Baskets: | Rel-20 Basket(s)
DC_R19_xBLTE_yBNR | HPUE objective is added into DC_R20_xBLTE_yBNR
HPUE_DC_LTE_NR_R19 | 
NR_CADC_SUL_R19 | HPUE objective is added into NR_CADC_SUL_R20
HPUE_NR_CADC_SUL_R19 | 
LTE_CA_R19_xBDL_yBUL | LTE_CA_R20_xBDL_yBUL
HPUE_NR_FR1_bands_R19 | HPUE_NR_FR1_bands_R20
HPUE_LTE_bands_R19 | Not needed in R20
NR_bands_CA_ENDC_R19_BWs | NR_bands_CA_ENDC_R20_BWs
NR_bands_xFeature_R19 | All band related feature baskets are merged into NR_bands_xFeature_20
DL_intrpt_combos_TxSW_R19 | 
LTE_NR_R19_Simult_RxTx | 
Complete the transition from Word-based tables into band combination database in Rel-20.

## Slide 6: Cross-domain: RedCap
Target a single common WI addressing (e)RedCap.
Two objectives:
  RLM/BFD relaxation for (e)RedCap UE
    Reuse Rel-17 solution as baseline
    Include both 1Rx and 2Rx
  3MHz channel bandwidth for at least n26, n85 and n106 for (e)Redcap devices
    Reuse Rel-18 solution as baseline
    Include both 1Rx and 2Rx
    Impact on RAN1/RAN2, if any, shall be minimized.

## Slide 7: RRM
Principles:
Some RRM capacity will be taken by RedCap item (see previous slide) and by RAN1/2-led items
Hence other RRM work should be very limited or zero, and should aim at not having any RAN1/2 impact.
Details:
  If any additional RRM work is included in addition to RedCap, top priority would be one specific case of SCell activation enhancements, namely: UE requirements for a UE allowed to not perform serving cell measurements (continuation of Rel-19 work), i.e.:
    Completion of missing Rel-19 RRM intra-band serving cell measurement reduction:
      Define SCell activation delay for intra-band contiguous CA by defining SCell activation time (Tactivation_time) and the CSI reporting (TCSI_reporting) for a non-measured SCell:
        Define the requirements provided network allows serving cell measurement relaxation for intra-band contiguous CA using Rel-19 solution as baseline.
        Include both FR1 and FR2.
    If any SCell activation enhancements are included, focus shall be limited to the scenario when UE is allowed not to perform measurements on contiguous intra-band SCell carrier. Details in RP-250905.

## Slide 8: Demod
Spatial Channel Model Demodulation Requirements is a top priority for operators
Principles:
Introduction of SCM requirements, with UE capability, is foundational to deliver confirmed feasibility for 6G.
Priority should be given to this: Hence no other RAN4-led demod-focused WI in Rel-20.
Objectives for Rel-20:
SCM based requirements derivation for:
  SU-MIMO:
    1st priority: 2 codeword case
    2nd priority: 4-layer eTypeII cases.
  Study how to handle MU-MIMO:
    1st priority: advanced receiver cases
    2nd priority: eTypeII.
Where SCM is relevant for other use cases (e.g., AIML, ISAC), the work should be done in the respective WIs.