## Slide 1
[RP-250985]
16.2. Tejas views on Release 20 6G RAN WG SIDs
RAN#108
June 09th-13th 2025, Prague, CZ
RP-250985

## Slide 2
The design considerations for 6G architecture fall mainly into:
  Evolutionary changes involving enhancing existing 5G features such as
    Immersive communication (Improved User and system throughput, Supporting higher mobility, Improved spectrum efficiency, High accuracy positioning)
    Massive Communication (Higher density deployment)
    Hyper Reliable low latency communication (reducing latency and reliable handover)
  6G specific features designed from ground-up to support new scenarios and requirements such as
    Ubiquitous connectivity (improving TN coverage, TN-NTN integration)
    ISAC (Sensing based application)
    AI and communication (Network for AI and AI for Network),
  6G includes other overarching aspects
    Sustainability (Energy efficiency)
    Security and privacy
Considerations for 6G architecture design

## Slide 3
Objective and Scope for 6G RAN Study

## Slide 4
As concluded in RP-250784 after the 6G workshop Tejas proposes to study the following topics for 6G RAN working groups:
Study a New Energy Efficient RAN (NEER) to improve coverage, spectral efficiency, energy efficiency and for supporting wider channel bandwidths (Slide 6) [RAN1-led]
Study ultra-Massive MIMO (uM-MIMO) for improve spectral efficiency and ISAC (Slide 7) [RAN1-led]
Study duplex flexibility to improve coverage esp at cell edge (Slide 8) [RAN1-led]
Study joint energy optimization across network and device (JEOND) for further improving energy efficiency and for getting additional energy saving (Slide 9) [RAN2-led]
Study harmonized design for integrated terrestrial and non-terrestrial network (Satellite, HAPS, UAV) or ITTN for ubiquitous connectivity (Slide 10) [RAN3-led]
Study 6G-IoT devices for new class of integrated TN and NTN devices for massive communication and HRLLC (Slide 11) [RAN1-led]
Key objectives for 6G RAN SID

## Slide 5
As concluded in RP-250784 after the 6G workshop Tejas proposes to study the following topics for 6G RAN working groups:
Study RIS (Reconfigurable Intelligent Surface) for use in improved coverage and for better sensing (Slide 13)[ RAN1 led]
Study AI/ML techniques to improve performance and efficiency of physical layer procedures (Slide 14) [RAN1 led]
Study ISAC for specific use case of detection and localization of 2D/3D fixed/flying objects (e.g. UAV) (Slide 15) [RAN1, RAN3]
Study standard framework for deploying AI driven network optimizations for NES and load balancing (Slide 16) [RAN3 led]
Study security and privacy aspects addressing 6G in AI and post-quantum era (Slide 17) [RAN2 led]
Study spectrum sharing and co-existence aspects of 6G with 4G and 5G RAT (Slide 18) [RAN1, RAN4]
Key objectives for 6G RAN SID

## Slide 6
Detailed proposals for 6G

## Slide 7
Motivation
To meet the IMT-2030 requirements for immersive communication, several key performance improvements are essential, including
  enhanced user and system throughput
  support for higher mobility
  improved spectral efficiency
  high-precision positioning.
Achieving these KPIs will require advancements such as increased bandwidth and enhancements to the underlying waveform.
Deploying FWA with higher bandwidth (e.g., >100 MHz in FR1 and >400 MHz in FR2) and higher subcarrier spacing (SCS) offers significant advantage with increased throughput , lower latency, efficient spectrum utilization & enhanced network flexibility.
To streamline Multi-RAT Spectrum Sharing (MRSS), the 6G air interface can be designed using the 5G waveform as a foundational baseline.
Enabling native AI capabilities will require the introduction of new measurements as well as enhancements to existing measurement frameworks.
Proposal
Study Items for Enhanced 6G Air Interface:
The 6G air interface can be envisioned as an evolution of the 5G-NR waveform, continuing to build on OFDM while incorporating several key enhancements like
  Waveform and Bandwidth Enhancements
    Support for wider bandwidths: over 100 MHz in FR1 and over 400 MHz in FR2.
    Use of additional Subcarrier Spacings (SCS), including both lower (<15 kHz) and higher (>960 kHz) SCS.
    Increased FFT sizes (e.g., 8K, 16K) to accommodate higher throughput.
    Enhanced data rates through smart and flexible frame structure.
  Capacity and Modulation Improvements
    Integration of NOMA over MIMO for improved spectral efficiency and capacity.
    Context-aware Dynamic interleavers for enhanced performance.
    Support for layer- and sub-band-specific modulation orders.
    Reduction in reference signal overhead & enhancement of port combinations.
    Adoption of enhanced constellations, such as non-uniform constellations, for improved efficiency.
  Coverage and Transmission Enhancements
    Use of DFT-S OFDM in the downlink for improved coverage.
    Support for multi-layer DFT-S OFDM in both uplink and downlink.
  Latency Reductions
    Reduction in HARQ-related latency.
    Simplification and optimization of PDCCH search space and decoding complexity.
  Measurement Enhancements
    Improved CSI-RS-based measurements for reporting detailed channel statistics & characteristics (eg Delay spread , Doppler spread ..etc)
  Native Energy Efficient RAN (NEER) design
    Energy savings considered from the outset ("Energy Efficiency from Day-1").
    Inclusion of on-demand reference signals, including SSB, SIB, and common signals, to reduce power consumption.
Enhancements to the Air interface
Impact: RAN1 led
Enabling Immersive communication
Notes: This slide alone is enhanced in child slide

## Slide 8
Motivation
MIMO evolution to support larger ports and higher frequencies is inevitable to realize the 6G vision of higher throughput, massive connectivity, low latency, and high reliability with user fairness
Progressing in this direction requires addressing a few key challenges in current 5G NR;
  Imbalance in feedback overhead/computational complexity and beamforming precision in the current CSI sounding and reporting mechanisms
  Favoring the usage of diverse codebook design formats for different requirements
  Limited attention currently offered to high-order MIMO port support and FWA co-scheduling requirements
  Reference signal overhead with higher-order MIMO
Proposal
Study unified and scalable codebook design
  A cohesive design that adapts across different scenarios and antenna architectures
  A scalable design that supports adaptive beam management and CSI framework for larger port counts exceeding 128
Study enhancements to user co-scheduling strategies and signaling by considering the new MIMO requirements in 6G
Study reference signal and signaling enhancements
Study distributed ultra massive MIMO for energy efficient networks with enhanced capacity and coverage
Enabling Immersive Communication
Impact: RAN1 led
ultra-Massive MIMO
Notes: This slide alone is enhanced in child slide

## Slide 9
Motivation
Static SBFD has been standardized in 5G; the logical next step for 6G is to investigate context-driven dynamic duplexing mechanisms. This bring in following benefits
Low latency, Improved coverage and Improved spectral efficiency.
Proposal
Study duplex flexible design to address :
Capability to support Traffic Aware Duplex solution
Self-interference handling at UE for Full Duplex solution ​
Collision handling of Uplink and Downlink data.​
Capability to handle legacy and 6G Duplex aware UEs​
Study to enhance UL coverage & capacity.
Duplex Flexibility in 6G
Frame structure progression with Duplex Evolution
DL
DL
UL
DL
DL
UL
DL
DL
UL
DL
UL
DL
Rel 19 SBFD
DL
DL
UL
D
X
X
X
U
DL
DL
DL
DL
UL
Frequency
Time
Rel 16 TDD
DL
DL
6G – Traffic-Aware Duplex
UL overlapped
with DL slot
DL
antenna
panel
UL
antenna
panel
6G supporting both full duplex and non full duplex UEs
Enabling Immersive Communication
Impact: RAN1 led, RAN4, RAN2, RAN3
Notes: This slide alone is enhanced in child slide

## Slide 10
Impact: RAN1 led, RAN2, RAN4
Motivation
Network energy saving(NES) was studied and specified in 5G in Release 18 and release 19:
  NES techniques were developed as an afterthought in later stage of 5G resulting in reduced support for large UE footprint (due to issues in supporting legacy UEs).
Energy saving techniques such as UE DRX was specified in release 15 of 5G NR, NES in release 18 & 19 LPWUS WI is specified in release 19.
  Enhancement restricted to Low Load scenarios
  In 5G NR energy saving techniques at UE and network side are studied independently.
Aspects which needs to be tackled in 6G:
  Energy saving in Medium and High Load Scenarios,
  Seamless network reconfiguration,
  Exploitation of Spatial and Temporal Distribution of UE.
Proposal
  Study energy efficiency KPI as the relative power saving gain between the evaluated case and reference case at given tolerance of communication performance impact.
  Study on UE assisted NES techniques.
  Study of categorization of coverage cell and capacity cell and enabling capacity cell only when required.
  Study NES techniques in duplex system.
  RACH optimization: Study improved initial access methods for improved resource utilization.
  Study on enhanced dynamic adaptation techniques for UE specific signals or channels for network energy saving.
  Study on Joint Energy saving technique between Network and UE
  Study of energy saving techniques in medium load and full load scenarios.
Joint Energy Optimization in Network & Device (JEOND)
Enabling sustainability : Energy Optimality for 6G must be built Natively
Notes: This slide alone is enhanced in child slide

## Slide 11
6G Integrated Terrestrial and Non-Terrestrial Networks (ITTN)
Motivation
The IMT 2030 requirements for NTN include
  Improved Capacity and Coverage Requirements than 5G NR-NTN
  High-Speed Mobility and Seamless Handover and a unified design with 6G TN
  Support of Multiple Satellite Architectures and Constellations
GNSS dependency Issues
  Increases UE Complexity and Cost
  Weak GNSS Signal and Inaccuracy(indoor and NLOS users) can effect the NTN Integration into NR TN
NTN architectures "still evolving" with TN dependence
NTN till now only has static beam prediction even with fast moving LEO beams
Enabling Ubiquitous Connectivity
Proposal
The study item should focus on the following aspects
GNSS-Independent Operation
  Study on the RACH Enhancements
  Time-Frequency Synchronization process Enhancements
  The SI can think of alternative Positioning , Navigation and Timing(PNT) estimation
Multi-waveform support: NTN Specific Waveform
  Study on Doppler Resilient and Delay tolerant Waveform with Low PAPR in addition to CP-OFDM and DFT-S-OFDM
  Study on the Advanced Modulation and Coding aspects
Multi Connectivity , Multi-TRP and enhanced MIMO support for NTN
  Study on Simultaneous connection into multiple satellites or multiple beams and between TN and NTN
  Study on localized beamforming , delay-doppler based beams along with adaptive beam management
  AI/ML based beam prediction and control methods
  Native Architecture:
    Study to Embed NTN support in 6G protocols (Doppler compensation, latency-aware scheduling).
Impact: RAN1, RAN2, RAN3, RAN4

## Slide 12
Limitations of existing IoT technologies and motivation
NBIoT supports large coverage but provides very low BW with higher complexity.
eMTC supports higher BW compared to NBIoT but the coverage is much lower than NBIoT
LoRa supports coverage of approx. 2KM but also has a low bandwidth up to 500kHz
Redcap supports higher bandwidth of upto 20MHz, however, doesn't support the low-end applications
Ambient IoT devices are ultra-low power consuming, however, the coverage is very low with low bandwidth
The existing different IoT technologies have different applications that do not support single network with common signaling. Therefore, deploying independent network infrastructure for different IoT systems is very challenging.
Proposal
A technology that support:
Single RAT supporting eMBB/IC and IoT/MC
  Any IoT device can connect to any 3GPP BS either directly or indirectly through intermediate UE
Both fixed and Mobile IoT devices
Both indoor and outdoor application which otherwise cannot use the existing IoT technologies (e.g.: NBIoT and Redcap)
Both device initiated and network-initiated data transmission
Flexible BW support from network side
Multiple device types based on the capabilities such as complexity, bandwidth, coverage, etc. and use cases
6G IoT devices
Enabling Massive communication
Primary Impact: RAN1-led, RAN2, RAN4
Notes: This slide alone is enhanced in child slide

## Slide 13
Motivation
IAB/WAB/NCR is still not a cost-effective option for coverage enhancement
Better coverage, overall 6G network power saving improvements possible with RIS
RIS consisting of a large array of controllable antenna elements can also be used for sensing/object detection.
Proposal
Study on RIS integration
  Study channel model and channel estimation for gNB-RIS-UE path (RAN1).
  Study applicable RIS architecture (RAN3-led)
  Study signaling interface design between gNB-RIS (R1) and RIS-UE (R2). (RAN2 led)
  Study additional use case for RIS (for e.g. sensing and object detection) (RAN3 led)
Reconfigurable Intelligent Surfaces (RIS)
Enabling Ubiquitous Connectivity
Primary Impact: RAN1-led, RAN2, RAN3, RAN4
Notes: This slide alone is enhanced in child slide

## Slide 14
Motivation
Normative work for AI/ML was restricted to CSI compression and beam management for 5G
Potential improvement in CSI compression, Beam Management, Coding, Codebook, and Rate Matching for FR3 (6.5-24 GHz)
Potential energy saving gains by reduction of actual measurement and using predicted measurement
Proposal
Study AI/ML-Driven Optimization for 6G in the following areas:
  Measurement framework: Predict & compress feedback, reducing overhead including CSI
  Beam Management: Real-time beam selection & tracking.
  Channel Coding: Neural network-based encoders/decoders for better error correction.
  Codebook: Dynamic updates based on real-time conditions.
  Resource Allocation: AI-optimized resource allocation.
AI/ML-Driven Optimization for Air interface
Enabling AI for Network design
Impact: RAN1 led
Notes: This slide alone is enhanced in child slide

## Slide 15
Motivation
Basic channel model study was done in 5G-Adv
ISAC is a key usage scenario enabled in 6G and is expected to help in indoor obstacle sensing, outdoor detection of UAV, identify railway and road crossing etc.
Proposal
Study new 6G RAN architecture and 6G air-interface to have native support for ISAC use cases (e.g. UAV) including:
The reference signal designs and SFIs should be considerate of at least gNB-based sensing.
The 6G frame structure should be designed with the requirements (eg. waveform) of both monostatic and multi-static sensing in consideration.
Integrated Sensing and Communication
Enabling joint sensing and communication use case
Impact: RAN3 led, RAN1, SA2, CT
Notes: This slide alone is enhanced in child slide

## Slide 16
Motivation
To utilize state of the art AI/ML based approaches for network optimization:
  Leverage cloud-native technologies to provide contextualized, on-demand network data
  Utilizing state-of-the art AI/ML techniques for optimization that result in increased spectrum efficiency, QoE, with reliability, security, trust and reduced energy consumption.
Aspects which needs to be tackled in 6G:
  HetNets with disparate data types
  Volume and velocity of data
  Zero / low-touch deployment
  Agile and adaptable to varying network topologies.
  Intent based / declarative workflows enabling quick, no-code use case definition
  Encourage EdgeAI
Proposal
  Study architecture for AI native RAN including optimization
    High quality data set maintenance with limited amount of measurements
  Study intent driven agentic AI for
  Network Energy Saving
  Load balancing
  Study on Federated and Distributed learning for
  model generalization
  data privacy
AI enabled Network optimization
Enabling AI for Network design
Impact: RAN3, SA2, SA5
Notes: This slide alone is enhanced in child slide

## Slide 17
Motivation
Lack of protection for System Information messages lead to Man-in-the-Middle (MITM) type of attack
MAC-CE is currently used for critical triggers such as LTM cell switch and lack of security at MAC-CE level is an open issue.
Security for SI and MAC-CE can be considered as baseline requirement in 6G
Existing security maximum key length (128 bits) might not be sufficient for a Post-Quantum world
Proposal
Study methods to protect broadcasted System information block messages
Study security for MAC-CE messages
Study security for other unprotected Layer 2 messages such as RLC Status PDU, PDCP status PDU etc
Study use of 256bits or higher length keys for encryption and integrity protection will be sufficient security in a post quantum world.
Security related aspects for 6G
Enabling Security and Privacy in 6G
Impact: SA3 and RAN2
Notes: This slide alone is enhanced in child slide

## Slide 18
Motivation
5G provided an option to spectrum share with 4G based on DSS
5G discussed about Dual connectivity
6G should also provide spectrum sharing with respect to Multi-RAT spectrum sharing
4G will continue to be widely deployed even when 6G is being rolled out. Only with 4G, 5G and 6G will the coverage be good enough.
Proposal
Study MRSS based spectrum sharing between 5G and 6G [RAN1-led]
Study either of the following [RAN2 led]:
  Dual connectivity between 5G and 6G and Dual stack between 4G and 6G
  Triple stack of 4G, 5G, 6G
Spectrum sharing and co-existence aspects of 6G
Enabling seamless migration from 5G
Impact: RAN1, RAN2 and RAN3 WGs
Notes: This slide alone is enhanced in child slide

## Slide 19
JISHNU@TEJASNETWORKS.com