## Slide 1
Views on Rel-20 AI/ML Enhancement
Agenda Item: 15.1.1
Source: Google
Document for: Discussion for decision
RP-250987

## Slide 2: Background
RAN1 recommended the following on AI/ML based CSI compression
Recommend Case 0
  Case 2 and 3 can be considered for further enhancement built upon the specification of case 0.
Recommend following specification impacts for the two-sided CSI compression use case
  Model pairing procedure including ID and applicability reporting
  Inference aspects including target CSI type, measurement and report configuration, CQI / RI determination, payload determination, quantization configuration / codebook, UCI mapping, CSI processing criteria and timeline, priority rules for CSI reports
  NW and UE side data collection for training,
    Target CSI format
    Note: The framework defined in BM and CSI prediction use cases could be reused.
  Specify performance monitoring, if needed

## Slide 3: Background (Cont’d)
RAN1 identified the potential spec impact on inter-vendor collaboration
Reference model / structure specification (for sub-option 3a-1 and Direction C)
  Note: The so called fully specified reference model discussed in RAN1 for Direction C is assumed to be equivalent to the to-be-specified model, if specified, for performance requirements in RAN4.
  Note: The model structure(s) for the reference encoder in inter-vendor collaboration sub-option 3a-1 can be same as/equivalent to the structure of the RAN4 defined/specified (if defined/specified for testability) reference encoder.
    To reduce the workload of the potential normative work scope, the model structure(s) for the reference encoder in inter-vendor collaboration sub-option 3a-1 is(are) same as/equivalent to the structure of the RAN4 defined/specified (if defined/specified for testability) reference encoder.
  Note: RAN1 has studied and agreed on a scalable model structure for feasibility study during Rel-19 study, and considers that can serve as a starting point for the model structure specification for the potential normative work.
Format and contents of parameter/dataset/information exchange: dataset (for 4-1 and 3a-1 with target CSI)/ encoder parameter (for 3a-1) / additional information (for 3a-1 and 4-1).
The workload can be reduced by identifying the common part among different aspects.

## Slide 4: Discussion
According to RP-250812, 2 TUs are recommended for the enhancements for AI/ML Air Interface
The performance for Case 2 and Case 3 are concluded as follows
Case 2 can achieve higher gain compared to Case 0 with similar/increased complexity
Case 3 can achieve better performance than Rel-18 Doppler eType2
  The gain is similar to Case 0 over Rel-16 eType2
Feasibility for inter-vendor collaboration Direction A (sub-option 3a-1 and 4-1) are not clear
There is no feasibility related concern for Direction C
It is preferred to support one solution, i.e., Direction C, for inter-vendor collaboration in Rel-20

## Slide 5: Proposal
Proposal 1: Confirm that 2 TUs are allocated Rel-20 enhancements for AI/ML air interface in RAN1
Proposal 2: The objectives of the Rel-20 enhancements for AI/ML air interface include the followings for the AI/ML based CSI compression Case 0/2/3
Model pairing procedure including ID and applicability reporting
Inference aspects including target CSI type, measurement and report configuration, CQI / RI determination, payload determination, quantization configuration / codebook, UCI mapping, CSI processing criteria and timeline, priority rules for CSI reports
NW and UE side data collection for training based on the Rel-19 framework for data collection for AI/ML based BM/CSI prediction
Specify performance monitoring, if needed
Inter-vendor collaboration Direction C