## Slide 1
Views on Rel-20 Coverage Enhancement
Agenda Item: 15.1.4
Source: Google
Document for: Discussion for decision
RP-250988

## Slide 2: Background
In RP-250812, 0.5TU for 3 quarters are recommended for coverage enhancement
In RP-250802, the followings are summarized for coverage enhancement
PRACH repetition with different TX beams
PUSCH coverage enhancement
  Msg5 PUSCH repetition
  PUSCH coverage for high UL data rate
  RIS

## Slide 3: Discussion
UL coverage is still an important aspect to improve the performance
A lot of coverage enhancement has been specified in previous releases
The coverage enhancement should strive to provide high UL data rate instead of maintaining basic communication
FR2 has been deployed in the field for a long time
No beam correspondence issue observed in the field
No strong motivation for the enhancement for PRACH repetition with different beams
If the PRACH repetition with different TX beam is included in Rel-20, the target use case should be well-defined and the scope should be limited

## Slide 4: Discussion (Cont’d)
For PUSCH coverage enhancement for high UL data rate
CG-PUSCH becomes more and more important for some types of traffic, e.g., XR
  Timing related enhancement, e.g., UTO, has been specified for CG-PUSCH for XR in Rel-18
  CG-PUSCH is also essential for the UE initiated beam report introduced in Rel-19
To improve the coverage for Type1 CG-PUSCH, the analog beam for CG-PUSCH can be dynamically changed based on unified TCI state introduced in Rel-17
  However, the precoder for CG-PUSCH is still fixed, which could cause significant coverage loss
It is necessary to specify dynamic precoder update for CG-PUSCH to improve its coverage
Further, pi/2 BPSK with higher coding rate is also beneficial for PUSCH coverage enhancement for high UL data rate

## Slide 5: Proposal
Proposal 1: Confirm that 0.5 TU with 3 quarters are allocated to the Rel-20 coverage enhancement in RAN1
Proposal 2: The Rel-20 coverage enhancement should focus on the PUSCH coverage enhancement with high UL data rate including the followings:
  Dynamic precoder update for CG-PUSCH
  Extending pi/2-BPSK to more MCS entries