## Slide 1
Views on Rel-20 NES Enhancement
Agenda Item: 15.1.6
Source: Google
Document for: Discussion for decision
RP-250989

## Slide 2: Background
In RP-250802, the following potential objectives for Rel-20 NES enhancement have been discussed
Enhancements on SSB for NES
Enhancements for cell DTX/DRX
Enhancements on SIB1 for NES
Enhancements for OD CSI-RS/TRS

## Slide 3: SSB for NES
For SSB for NES, the followings for Rel-20 NES enhancement have been discussed
OD-SSB for UEs in idle/inactive mode
SSB periodicity extension
SSB adaptation within a burst
UE-initiated OD-SSB
The OD-SSB for UEs in idle/inactive mode and SSB periodicity extension could have a significant impact on legacy UEs
Such features can only be enabled for CCs without legacy UE
The benefit is minor
SSB adaptation within a burst can already be supported based on Rel-19 NES
UE-initiated OD-SSB is beneficial for the NES, since the NW would have better information on when to transmit the OD-SSB
Proposal 1: Specify UE-initiated OD-SSB for Rel-20 NES

## Slide 4: Enhancements for cell DTX/DRX
For enhancements for cell DTX/DRX, the followings for Rel-20 NES enhancement have been discussed
Extending cell DTX/DRX operation to common signals
Cell DTX/DRX enhancements for RRC connected UE
Cell DTX/DRX enhancements for RRC idle/inactive UE
The Extending cell DTX/DRX operation to common signals and cell DTX/DRX enhancements for RRC idle/inactive UEs could have a significant impact on legacy UEs
Such features can only be enabled for CCs without legacy UE
The benefit is minor
The enhancements for cell DTX/DRX should focus on RRC connected mode UE
One potential enhancement is UE recommended cell DTX/DRX via UAI
It is beneficial for joint NW/UE energy saving
Proposal 2: Specify UE-recommended cell DTX/DRX via UAI for Rel-20 NES

## Slide 5: Enhancements for SIB1
For enhancements for SIB1 for NES, the followings for Rel-20 NES enhancement have been discussed
OD-SIB1 for UEs in idle/inactive mode
SIB-less NES cell for UEs in idle/inactive mode
Standalone OD-SIB1
According to the evaluation result in Rel-19, the power saving gain for OD-SIB1 is small
There is no strong need for additional SIB1 enhancement for Rel-20 NES
Proposal 3: Do not include any additional SIB1 enhancement for Rel-20 NES

## Slide 6: Enhancements for OD CSI-RS/TRS
For OD CSI-RS/TRS,
Rel-19 specified time-domain adaptation for SSB and NW-triggered on-demand SSB
  The NW can dynamically change the periodicity for SSB
TRS is also an always-on downlink signal
  The time-domain location for TRS is currently configured by RRC
  The number of TRSs is usually no less than the number of SSBs
  The periodicity of the TRS depends on the channel variation status of the UEs
Proposal 4: Specify OD-TRS for Rel-20 NES

## Slide 7: Conclusion
Proposal 1: Specify UE-initiated OD-SSB for Rel-20 NES
Proposal 2: Specify UE-recommended cell DTX/DRX via UAI for Rel-20 NES
Proposal 3: Do not include any additional SIB1 enhancement for Rel-20 NES
Proposal 4: Specify OD-TRS for Rel-20 NES