## Slide 1
Views on scope of Rel-20 AI/ML for NG-RAN Phase 3
Agenda: 15.3.1
Source: Samsung
Document for : Discussion and decision

## Slide 2
Background
R19 study item:
  Study two new AI/ML based use cases: network slicing and CCO
  Study Rel-18 leftovers as candidates for normative work: mobility optimization for NR-DC, split architecture support for Rel-18 use cases, energy saving enhancement, continuous MDT collection targeting the same UE across RRC states, multi-hop UE trajectory across gNBs.
R19 work item:
  Specify data collection enhancements and signaling support for two new use cases: network slicing and CCO
  Support of the Leftovers in Rel-18 AI/ML for NG-RAN: mobility optimization for NR-DC, split architecture support for Rel-18 use cases, continuous MDT collection targeting the same UE across RRC states
  It should be noted that:
  Due to no consensus on the solution, energy saving is concluded to be out of scope of R19 WI.

## Slide 3
Introduction
Upon the discussion in RAN#107, the initial scope for R20 AI/ML for NG-RAN endorsed as WF:
Rel-20 AI/ML for NG-RAN should be based on current 5G architecture and interfaces.
The objectives of AI/ML for NG-RAN in Rel-20 are listed below:
  Study the following new AI/ML based use cases and down-scope (1 or 2 use cases) in next plenary [RAN3]:
    QoE Optimization;
    Network energy saving
    Mobility (including Multiple-hop target node UE trajectory)
  Note: Other Leftovers depend on Rel-19 outcome, if any.
  Note: Coordination based on LSs with other working groups, when needed.
6 months for the Rel-20 Study Item on AI/ML for NG-RAN, followed by 12 months for the subsequent Work Item.
In this paper, the potential scope for Rel-20 AI/ML for NG-RAN is discussed.

## Slide 4
Down scoping on the new use cases
Considering TUs status for 6G SI and Rel-20 5G-A, it is realistic to have 1 TU for AI/ML for NG-RAN. In this case, one new use cases is reasonable in Rel-20 AI/ML for NG-RAN (2 new use cases in Rel-19 with 2 TUs).
As far as we know, there is no commercial deployment for QoE. Therefore QoE optimization based on AI/ML could be down selected.
For Network energy saving, it is part of the study in Rel-19, but the discussion is very controversial and there is no good solution identified, that’s why Network energy saving is excluded from Rel-19 normative work. It will again bring controversial and repeated discussion in RAN3 if NES is included.
Mobility is important for user experience and network performance. If good solution can be identified in 5G-A Rel-20, similar solution could be adapted to 6G from day-1. The work on mobility will benefit for both 5G-A and 6G.
Proposal 1: Study new AI/ML based use cases: Mobility.

## Slide 5
Use case for R20
AI/ML for mobility:
  Rel-18/Rel-19 discussed the basic mobility cases, e.g. L3 handover, single connectivity.
  LTM mechanism has been designed to achieve the seamless handover.
  The existing LTM mechanism can be optimized in several aspects, e.g.:
    Target cell selection:
      Each candidate cell needs to setup/store the UE context from the LTM preparation until UE context release. UE accesses one target cell among the candidate cells, so UE context setup/storage of other prepared cells is not necessary.
    TA transfer and maintenance
      Heavy signaling to transfer the TA value from target DU to source DU for the cells that source DU may decide to trigger the cell switch.
      Source DU maintains the TA validity time based on implementation. Wrong TA maintenance leads to the failure.
UE context setup
RRCreconfig
S-DU
CU
Each prepared candidate cell setup/stores the UE context from the LTM preparation stage to the end of release stage;
The preparation of the candidate target cells which UE does not access is a kind of waste.
UE context modification
UE context modification
RRC message transfer
PDCCH order
UE
Preamble
TA information
TA information
Cell switch command with TA
Access target cell based on TA
Other procedure: TCI state transfer, UE access detection, UE context release/modification
Separated procedure to transfer the TA value;
Wrong TA validity time maintenance in source DU could result in failure
T-DU3
T-DU2
T-DU1

## Slide 6
Use cases for R20
AI/ML for mobility:
  AI/ML functionality:
    Generate proper (candidate) target cells to reduce the redundant target preparation, e.g. UE context setup and storage.
    TA validation time and/or TA value predication for UE to access the target cell, therefore improve the access robustness and reduce the additional signaling to transfer the TA
  The impacts will be the network interfaces in RAN3 domain. There is no RAN2 impact. Similar like in the previous releases: RAN3 did AI/ML for L3 mobility in Rel-18 and RAN2 started the AI/ML for L3 mobility in Rel-19. RAN3 study on AI/ML for LTM will not impact further work in RAN2 on it in future releases.
  Proposal 2: For AI/ML for Mobility, LTM is included in the scope.

## Slide 7
Use cases for R20
AI/ML for mobility:
multi-hop data collection:
  AI/ML for NG-RAN aims to set the proper decision with proactive view.
  Rel-18 took the single-hop data collection as the starting point.
  Multi-hop data collection can give the more foreseen information, which helps the node to have a future full picture of UE.
  Potential issue to be solved:
    How to forward the collected data
    How to avoid keeping UE context in intermediate node
  Proposal 3: For AI/ML for Mobility, multi-hop data collection is included in the scope.
Data collection reporting
Handover req
AI model training/inference based on the collected data
AI model
Data collection reporting
Handover req
An example of multi-hop data collection

## Slide 8
Proposal for Rel-20 scope of AI/ML for NG-RAN
R20 scope
Rel-20 AI/ML for NG-RAN should be based on current 5G architecture and interfaces.
The objectives of AI/ML for NG-RAN in Rel-20 are listed below:
  Study the new AI/ML based mobility including AI/ML for LTM, Multiple-hop target node UE trajectory[RAN3].
  Note: Coordination based on LSs with other working groups, when needed.
6 months for the Rel-20 Study Item on AI/ML for NG-RAN, followed by 12 months for the subsequent Work Item
To allocate 1 TU for the Rel-20 AI/ML for NG-RAN.

## Slide 9
Thanks!