## Slide 1: Motivation for HD-FDD operation for NR NTN in bands above 10 GHz
Eutelsat Group, SES, Hispasat, Intelsat, Sky Perfect JSAT, ESA, LG electronics, MediaTek Inc., Thales, Sharp, Airbus, Gilat, Lockheed Martin Corporation
3GPP TSG-RAN Meeting # 108 RP-251137
Prague, Czech Republic, June 9-13, 2025 Agenda Item 15.4.4

## Slide 2: Background
In RP#107 meeting, RAN4 Rel-20 5G-A package was discussed. The discussions were summarized in RP-250817.
In the same meeting, there were contributions raising the strong commercial demand of reducing the antenna size and/or support for half duplex mode for Ku band (RP-250240, RP-250457, RP-250483, RP-250648).
In this contribution, we provide a consolidated motivation of introducing half-duplex FDD (HD-FDD) devices for antenna size reduction on Ku/Ka band and suggest considering it as part of the RAN4 Rel-20 5G-A package.

## Slide 3: Motivation
Current market landscape
  HD-FDD technology has been widely used, demonstrating the fact that cost reduction is a key driving factor for successful market in other non-3GPP satellite communication systems, including
    Starlink’s progression from generation 1 to generation 4
    Amazon’s Kuiper project, except for its high-end, larger antennas.
    Eutelsat OneWeb terminals (Intellian 10HX, HNS HL-1100)
Commercial demand
  Automotive-mounted VSAT is considered as a very important segment for Ku/Ka band NR-NTN market penetration due to its large volume. The global automotive antenna market is expected to be $12.2Bn by the end of the decade [1].​
  HD-FDD antennas cost less that FD antennas and better match the consumer expected price point
[1] https://www.globenewswire.com/news-release/2023/04/26/2654771/0/en/Global-Automotive-Antenna-Market-Size-To-Grow-USD-7253-13-Million-By-2030-CAGR-of-6-30.html

## Slide 4: Motivation
Implementation constraints
  HD-FDD can either avoid implementing high-complexity duplexer for single antenna panel or avoid separate antenna panels for transmission and reception (~50% antenna size reduction).
  Footprint and cost are critical factors for general adoption, and especially in the automotive market. Passenger vehicles, especially those with more aerodynamic designs and glass roofs, require compact antenna arrays due to limited physical space.
Service impact
  Assuming HD-FDD for the UE, the SAN can continue operating under FD-FDD. Therefore, the overall system capacity is not compromised.
  In principle, the amount of radio resource assigned to Rx and to Tx respectively can be flexibly allocated. So peak performance of the UE is only slightly reduced

## Slide 5: Proposals
We propose RAN to consider the objective to introduce half-duplex (HD) NR-NTN devices for Ku band and Ka band as part of RAN4 Rel-20 5G-A package.
Only small workload is expected
  Rel-19 NR_NTN_Ph3 WI already introduced HD Redcap devices for NTN in FR1, providing a good starting point for defining HD-FDD requirements for Ku/Ka band.
  On RAN1 specs, at least no additional RAN1 spec impact is needed for operating Ku bands with FR1 SCS. For FR2 SCS, the additional workload, if identified, is expected to be minimum.
Proposal: Consider HD-FDD NR-NTN device for bands above 10 GHz as an essential part of the RAN4 Rel-20 5G-A package

## Slide 6: Thank you!