## Slide 1: Rel-20: RRC_INACTIVE enhancements
Source: Ericsson, China Unicom, T-Mobile , CHTTL, BT, Telia Company, Lenovo, KT Corp, Jio Platforms (JPL), Sateliot
3GPP TSG RAN#108
Prague, Czech Republic
June 9th -13th , 2025
Agenda Item: 15.3.4
RP-251191

## Slide 2: Introduction
RRC_INACTIVE state is more efficient compared to RRC_IDLE state.
  The time to enter RRC_CONNECTED from RRC_INACTIVE is significantly faster and results in less signalling than from RRC_IDLE.
A large RAN Notification Area (RNA) provides benefits, e.g. less signalling load from RNA updates and less UE power consumption, but this requires the network to ensure Xn connectivity between involved gNBs, see 3GPP TS 38.300
However, Xn connectivity between any pair of gNBs cannot be assumed at all times, for example:
  Xn connection is not setup between the gNBs
  Network policies may prevent Xn links between certain nodes / areas
  After an intermittent planned or unplanned downtime of a gNB or an Xn link, it takes some time until the Xn connectivity is back
  Other reasons

## Slide 3: Detailed problem #1 RAN paging
In case of Mobile Terminated (MT) data or signalling for the UE, RAN paging triggered by the old gNB may not reach a UE in RRC_INACTIVE in case the UE has moved to a new gNB (while still in the same RNA) and there is no Xn connectivity between old gNB and new gNB
  Upon no paging response, in case the RAN paging was triggered by DL user data, there is no requirement on the old gNB to release the N2 connection with AMF for this UE.
  This results in hanging applications and MT calls will not reach the UE.
Zzz…
BS cannot
find the UE

## Slide 4: Detailed problem #2 RRC resume
In case of Mobile Originated data or signalling, RNA update, or MO small data transmission from a UE in RRC_INACTIVE, the new gNB which receives a RRC resume request will not be able to retrieve the UE context from the old gNB if
  there is no Xn connectivity between these gNBs, or
  and the new gNB does not have sufficient information to retrieve the UE context from the information in the RRCResumeRequest message.
  This results in a delay and data loss
Zzz…
BS cannot retrieve the UE context

## Slide 5: Proposal: Enhancements for RRC_INACTIVE to support non-existing Xn connections between gNBs
Justification
  RRC_INACTIVE state is more efficient compared to RRC_IDLE state when the probability that the UE leaves its RAN Notification Area is small.
  However, using larger RNAs spanning over multiple larger gNBs have a negative impact on reliability.
  When there is lack of Xn connectivity between gNBs, a UE in RRC_INACTIVE crossing gNB borders may experience major disruptions at RAN paging, when UE resumes or uses MO small data transmission.
Objective
  Study solutions and specify support for improved resilience from network failures for UEs in RRC_INACTIVE
    Scope should include at least resilience from non-existing Xn connections affecting UEs in RRC_INACTIVE
  Note: solutions are expected to be applicable to both TN and NTN