## Slide 1: Discussion on Rel-20 AI/ML air-interface

## Slide 2: Background of R19 CSI compression
Study objectives of R19 additional study on CSI compression
  Improve trade-off between performance and complexity/overhead
    e.g., considering extending the spatial/frequency compression to spatial/temporal/frequency compression, cell/site specific models, CSI compression plus prediction (compared to Rel-18 non-AI/ML based approach), etc.
  Alleviate/resolve issues related to inter-vendor training collaboration
For trade-off performance and complexity/overhead
  RAN 1 studied following cases with prioritization
For inter-vendor training collaboration
  RAN1 studied following directions and its sub-options with prioritization
    Direction A: Sharing parameters/reference model/dataset that enables UE-side offline engineering
      Option 3a-1: encoder parameter exchange, with and without {target CSI}
      Option 4-1: dataset exchange (target CSI, CSI feedback)
    Direction C: Fully standardized reference model(s) and parameters with specified CSI generation part and/or CSI reconstruction part (option 1)
Case | Target CSI slot(s) | Whether the UE uses past CSI information | Whether the network uses past CSI information
0 | Present slot | No | No
2 | Present slot | Yes | Yes
3 | Future slot(s) | Yes | No

## Slide 3: Discussion on Rel-20 AI/ML air-interface
RAN1’s conclusion on inter-vendor collaboration
Discussion
  Direction C requires standardized reference model which is heavy burden for standardization, also Direction C only ensures minimum performance requirement, so it may provide lower performance than Direction A with sub-option 4-1 and 3a-1.
  For Direction A with sub-option 3a-1, compared to sub-option 4-1, it requires standardized model structure and method to deliver/transfer model parameters. In addition, considering explosive growth of AI/ML technology, relying on certain reference model may limit performance in the field, and it may not be appropriate future-proof direction.
Proposal
  For inter-vendor training collaboration, support Direction A with sub-option 4-1 for normative work.

## Slide 4: Discussion on Rel-20 AI/ML air-interface
RAN1’s recommendation for normative work for CSI compression
Discussion
  As shown above, Case 0 is recommended for normative work and case 2 and 3 which are enhanced schemes over case 0 can be further considered. However, given limited time budget, it is preferred to focus on Case 0 only in Rel-20.
  For performance monitoring, during the study, NW side performance monitoring and UE side performance monitoring were studied. In addition, for NW-side performance monitoring, it was concluded that legacy codebook can be used for target CSI reporting meaning that it can be supported without specification enhancement. Therefore, it is better to focus on the UE-side performance monitoring, if needed.
Proposal
  For normative work of CSI compression, consider following modification from RAN1’s recommendation.
    Focus on Case 0 only
    Specify UE-side performance monitoring, if needed

## Slide 5: Proposals
Proposal for Rel-20 AI/ML for air-interface
  For inter-vendor training collaboration, support Direction A with sub-option 4-1 for normative work.
  For normative work of CSI compression, consider following modification from RAN1’s recommendation.
    Focus on Case 0 only
    Specify UE-side performance monitoring, if needed
.