## Slide 1: Discussion on Rel-20 AI/ML for NG-RAN

## Slide 2: Status on AI/ML for NG-RAN
  Rel-19 is expected to support the following use case
  AI/ML-based slicing
  AI/ML-based CCO
  Leftovers in Rel-18
    Mobility optimization for NR-DC
    Split architecture support for Rel-18 use cases
    Continuous MDT collection targeting the same UE across RRC states
  Study objectives in Rel-19
  Study two new AI/ML based use cases, i.e., Network Slicing and CCO, with existing NG-RAN interfaces and architecture (including non-split architecture and split architecture).
  Rel-18 leftovers as candidates for normative work, based on the Rel-18 principles, as follows:
    Mobility optimization for NR-DC
    Split architecture support for Rel-18 use cases based on the conclusions from Rel-18 WI
    Energy Saving enhancements, e.g., Energy Cost Prediction
    Continuous MDT collection targeting the same UE across RRC states
    Multi-hop UE trajectory across gNBs

## Slide 3: Discussion on Rel-20 AI/ML for RAN
Agreements in the RAN#107 meeting
  Rel-20 AI/ML for NG-RAN should be based on current 5G architecture and interfaces.
  The objectives of AI/ML for NG-RAN in Rel-20 are listed below:
    Study the following new AI/ML based use cases and down-scope (1 or 2 use cases) in next plenary [RAN3]:
      QoE Optimization;
      Network energy saving,
      Mobility (including Multiple-hop target node UE trajectory)
  6 months for the Rel-20 Study Item on AI/ML for NG-RAN, followed by 12 months for the subsequent Work Item.
Discussion
  In the last RAN meeting, several use cases (e.g., QoE Optimization, Multiple-hop target node UE trajectory), which were proposed but excluded from the Rel-19 scope, have gathered attention and support from many companies.
  Motivation for QoE Optimization
    It is necessary to find new AI/ML-based use cases that can ensure user experience based on the existing 5G network architecture.
    AI/ML-based QoE optimization can improve the UE’s user experience by predicting service quality issues and adjusting radio resource allocation accordingly.
  Motivation for Multiple-hop target node UE trajectory
    In Rel-18, UE trajectory prediction for the next one-hop target NG-RAN node was considered for subsequent mobility decisions.
    UE trajectory prediction from the NG-RAN node beyond one hop can still provide meaningful information for subsequent mobility decisions.
  Considering companies’ interests, support, motivation for use cases, and the agreed period of Rel-20 AI/ML for NG-RAN, etc., QoE Optimization and/or Multiple-hop target node UE trajectory can be selected.

## Slide 4: Proposals
Proposal for Rel-20 AI/ML for NG-RAN
  For NG-RAN, Rel-20 focus on one or two use cases from the following
    QoE optimization
    Multi-hop UE trajectory across gNBs
.