## Slide 1: PML views on 6G RAN WG SI
3GPP RAN#108
Prague, Czech, June 09-13, 2025
RP-251268

## Slide 2
Introduction
3GPP TSG RAN approved at their meeting #106 the Study Item on 6G Scenarios and Requirements [1] which aims to identify typical usage scenarios for 6G radio technology and the required capabilities for each scenario, and contains an objective to define Minimum Technical Performance Requirements (MTPRs) for 6G, and, where applicable, the associated target values and key assumptions.
The 6G overall plan was endorsed : Studies for 6G in 3GPP are expected to start from Release 20. RAN-WG SIDs are expected to be approved in June, 2025. IMT-2030 submission and normative work for 6G in 3GPP are expected to start from Release 21. Release 21 is expected to produce the 1st set of 3GPP 6G technical specifications, and will be the release for IMT-2030 submission before 2030.
Regarding “New RAN WG SI on 6G”, it is noted in RAN #108 agenda: Max. one contribution led per company for this agenda item 16.2. Corresponding suggestions should be done via discussion papers (and not SID inputs). A moderator will try to generate a first version of a SID (based on these inputs) which will then be discussed during RAN #108.
In this contribution, we propose our views on scope of 6G RAN WG study, and candidate items.

## Slide 3
Views on D-MIMO / Cell Free study
Motivations
  6G RAN should enable a user-centric network to provide flexible and autonomous architecture, customized service, and efficient resource reuse.
  Both centralized XL-MIMO and cell-free XL-MIMO (XL D-MIMO) can provide higher spectral efficiency, reliability, sensing accuracy, throughput, and lower latency.
  Centralized XL-MIMO is a special case of cell-free XL-MIMO. To support cell-free networking, a unified design should be studied to provide ubiquitous services, including micro-/macro-coverage, ultra-long-range coverage, etc.
Observation 1
    To support user-centric network, design philosophy of “cell-free” for both L1 and L2 should be considered during the study item.
    Random access and mobility management should be enhanced to support user-centric TRP association and dynamic TRP selection.
Proposal 1
  The WG study should cover following aspects:
    Unified design of reference signals：1) Study DMRS designs based on different scale of the number of ports; 2) Study unified design of CSI-RS for various measurements; 3) Study uplink measurement for long-range coverage; 4) Study phase coherence measurement for XL D-MIMO.
    Uplink/downlink transmission enhancements beyond 5G: 1) Study unified design for downlink precoding; 2) Study the uplink power control for XL D-MIMO.

## Slide 4
Views on AI-Native study: Real-Time Intelligence
Motivations
  AI-Native is expected to improve 6G network performance and empower diverse use cases.
Observation 2
    Large AI Models for 6G have three main challenges, which may block the deployment of AI-Native.
      Green: high computing of large models introduces high energy consumption
      Real-time: large models are too heavy and slow for delay-sensitive services
      Security:“black box”AI algorithms are unexplainable for QoS garantee
Proposals 2
  The RAN WG study should cover following aspects:
    Lightweight real-time intelligence needs to studied by 6G RAN WG , considering power-saving, data-efficient, small-scale AI for delay-sensitive services.
    Hierarchical AI RAN architecture study, covering the deployment framework of real-time, near-real-time, non-real-time AI.
    Digital twin of networks study ,covering closed-loop data collection, model training and validation.
    Preferred use cases to be studied: 1) MAC scheduling for MU-MIMO; 2) time-frequency-space radio resource allocation for multiple users; 3) Interference prediction and management; 4) manage inter-cluster interference; 5) Beam prediction and management; 6) reduce beam training overhead and delay for FR2.

## Slide 5
Views on HRLLC study: Deterministic Wireless
Motivations
  5G is continuously improving deterministic communication, and wide-area deterministic communication (with DetNet) is covered by 5G Release 18.
  6G aims to support native deterministic service from Day 1 for HRLLC scenarios.
Observation 3
    Channel fading, inter-cell interference and best-effort scheduling introduce uncertainty of latency, jitter, and reliablity.
    Challenges caused by RAN basic technology are trivialized, while its native deterministic communication needs to be further explored.
Proposal 3
  The RAN WG study should cover following aspects:
    Study new architecture for RAN native deterministic communication.
    Study new functionalities to support time synchronization, time awareness, traffic awareness, etc.
    Study HRLLC techniques, e.g., ultra-high reliable transmission based on cell-free networks.
    Study time-aware scheduling and shaping mechanisms for wireless networks.
    Study high-precision time synchronization mechanisms via air interface, and cross-domain high-precision time synchronization mechanisms.
    Study new architecture and technologies to support specified scenarios, e.g., industrial ethernet.

## Slide 6
Views on Coordinated ISAC study
Motivations
  Sensing capabilities focus on : 1) missed detection probability and false alarm probability; 2) sensing accuracy; 3) sensing resolution.
Observation 4
  Reusing communication device, spectrum and signals for sensing will reduce complexity for 6G Day 1 target .
  Unified service including seamless coverage, wide range sensing for UAV network, supporting aircraft management and control.
Proposal 4
  The RAN WG study should cover following aspects:
    Study new architecture with sensing function in 6G RAN architecture.
    Study sensing frames: supporting long-range detection and high-resolution.
    Study waveform: OFDM, OTFS or Radar waveform.
    Study multi-TRP nanosecond sync for sensing, including wired sync, OTA reciprocity calibration.
    Study multi-TRP coherent enhancement for super high accuracy sensing.
    Study multi-TRP sensing beam scanning and tracking solutions

## Slide 7
References
RP-243276, RAN Chair’s Guidance for 6G Study: ITU Focused, RAN#106, Dec., 2024.
Recommendation ITU-R M.2160-0, Framework and overall objectives of the future development of IMT for 2030 and beyond, Nov. 2023.
PR-243325, Reply Liaison Statement on Minimum requirements related to technical performance for IMT-2030 radio interface(s), RAN#106, Dec. 2024
REPORT ITU-R M.2410-0, Minimum requirements related to technical performance for IMT-2020 radio interface(s), 2017
3GPP TS 22.137, Service requirements for Integrated Sensing and Communication; Stage 1 (Release 19), V19.1.0, 2024
RP-250826, Draft Meeting Report for TSG RAN meeting #107, Apr. 2025
RP-250825, Agenda for RAN#108, June, 2025

## Slide 8: Thanks!