## Slide 1
On Rel-20 Mobility Enhancements – Phase 5
RP-251340
3GPP TSG RAN#108
Prague, CZ.
June 9 – 13, 2025
Agenda Item: 15.2.3

## Slide 2: Mobility Enhancements Phase 5
  Overview
  Mobility enhancements have been specified since NR Release-15, these include conditional handover (CHO) and dual active protocol stacks (DAPS).
  In Release-18, L1/L2 Triggered Mobility (LTM) was introduced to reduce HO interruption time and provide improved HO performance – this makes it desirable by most operators. Expanding the scope of LTM in Rel-20 will further improve HO performance.
  Possible scope of enhancements in Rel-20 include:
    Inter-CU Conditional LTM (C-LTM)
    L1-SINR measurement quantity for LTM
    Dynamic update of L1 measurement/reporting for LTM

## Slide 3: Inter-CU Conditional LTM (C-LTM)
  Rel-19 Conditional LTM (C-LTM) is specified to reduce the interruption time by using UE evaluated conditions to trigger LTM and subsequent LTM.
  The Rel-19 C-LTM is however limited to intra-CU (i.e., mobility between cells of the same gNB-CU) and non-DC scenarios.
    To achieve better overall HO performance and efficiency, inter-gNB (or inter-CU) mobility is important to harness the benefits of C-LTM to further reduce interruption time and improve HO robustness.
  The potential enhancements for inter-CU C-LTM:
  Specify support for inter-CU C-LTM [RAN2, RAN3]
    In case DC is no configured and CU is actin as the MN.
    Specify support for DC case where inter-CU LTM is either configured in MN or SN with no change to MN or SN.
    Specify no support for DC case where inter-CU LTM is configured for both MN and SN simultaneously.
  Proposal 1: Support enhancements in inter-CU C-LTM.

## Slide 4: L1-SINR Measurement for LTM
  L1-SINR measurement for LTM will provide a more robust cell selection by taking interference magnitude into account, which is not possible with RSRP-based cell selection. With L1-SINR based LTM, throughput performance increases and the likelihood of ping-pong (or frequent) cell switch is reduced.
    L1-RSRP may not reveal the channel conditions (interference and noise levels).
  Specify support for L1-SINR as L1 measurement quantity for LTM:
    Support L1-SINR measurement and include L1-SINR measurements in MAC CE event triggered L1 measurement report [RAN1, RAN2, RAN3, RAN4].
    Support L1-SINR based triggering conditional LTM [RAN1, RAN2].
Proposal 2: Support L1-SINR as L1 measurement quantity for LTM in addition to the existing L1-RSRP based trigger.

## Slide 5: Dynamic Update of L1 Measurement/Reporting
  In Rel-19, measurement and reporting for LTM candidate cells is semi-statically configured via RRC. Introducing dynamic update of L1 measurement/reporting will reduce UE processing, measurement reporting overhead, interruption time etc.
  Support dynamic update of L1 measurement/reporting for LTM:
    Specify the necessary configuration and procedures for MAC CE based configuration selection from prior RRC configurations of UE L1 measurement and reporting LTM configuration [RAN2].
    Specify RAN4 specific requirements [RAN4].
Proposal 3: Support dynamic update of L1 measurement/reporting for LTM.

## Slide 6: References
  [1] RP-250036 Moderator's summary for RAN2 led REL-20 topics
  [2] RP-250812 Summary for RAN Release 20 5G-Adv

## Slide 7: Thank you