## Slide 1: Views on Rel-20 SON/MDT
RP-251348
RAN#108
Prague, CZ
June 9-13,2025
Agenda : 15.3.3

## Slide 2: Background (from RAN#107 scoping)
The objectives of SON/MDT in Rel-20 including and to be down-selected on the following (1 or 2 use cases):
  MRO enhancement for R19 LTM (the detail scope should be limited and needs to be further checked based on the progress in R19 LTM). [RAN3, RAN2]
  Support of SON/MDT enhancements for UAV or LP-WUS/WUR [RAN3, RAN2]

## Slide 3: Further MRO enhancements for LTM
Rel-19 MRO for LTM covered the following aspects for intra-CU LTM:
  Optimize MCG LTM failure and success scenarios (e.g., via RLF Report, SHR enhancements)
  Detect RACH-less LTM failures (e.g., due to wrong beam or outdated TA)
As a continuation, we propose the following to be considered as part of a potential Rel-20 SON/MDT WI:
  Optimize inter-CU LTM scenarios
  Optimize conditional LTM scenarios
  Optimize SCG LTM failure and success scenarios

## Slide 4: SON/MDT for Aerial UEs
Aerial UEs have been specified in NR in Rel-18 and have more likely deployment. Considering this, it would be useful to optimize aspects related to Aerial UEs
Rel-20 SON/MDT WI can consider the following aspects related to Aerial UEs e.g.,
  Logged MDT enhancements for Aerial UEs (e.g., height-dependent area scope or triggers)
  MRO for Aerial UEs (e.g., RLF/SHR enhancements)

## Slide 5: No need to consider any Rel-19/Rel-18 leftovers
There were several scenarios in Rel-19 SON/MDT or Rel-18 SON/MDT that were not considered due to lack of time or lack of consensus or to avoid LTE impacts e.g.,.
  CHO with candidate SCG “near-failure” scenarios (e.g., SPR and SHR enhancements)
  Intra-system inter-RAT SHR from LTE to NR
  Optimize CG-SDT
There is no need to open the discussion again in Rel-20 SON/MDT and rather focus on the new scenarios. Hence, the following is proposed:
Proposal: There is no need to consider any leftovers from Rel-19 SON/MDT or Rel-18 SON/MDT

## Slide 6: Summary - Rel-20 SON/MDT WI objectives
Potential objectives for Rel-20 SON/MDT WI
  MRO enhancements for R19 LTM (including SCG LTM, Inter-CU LTM, Conditional LTM) [RAN3, RAN2]
  SON/MDT enhancements for Aerial UEs [RAN3, RAN2]
NOTE: Rel-20 SON/MDT will also not consider any leftovers from Rel-19 SON/MDT or Rel-18 SON/MDT