## Slide 1: Views on Rel-20 AI/ML for mobility WI CMCC
3GPP TSG RAN Meeting#108 RP-251383
Prague, CZ, June 9-13, 2025
Agenda: 15.2.1
Document for: Discussion

## Slide 2: Progress in RAN#107
Based on Chair’s summary[1], only the following objectives are considered as baseline for AI Mob:
  Specify support for RRM measurement prediction for both UE and network sided models [RAN2]:
  Specify signalling and protocol aspect to enable reporting inference outcome of UE sided model for RRM measurement prediction
  Specify signalling and protocol aspect to enable reporting information from UE for inference operation of network sided model for RRM measurement prediction
  At least the use cases studied so far in RAN2 SI are supported: Temporal domain prediction and Frequency domain prediction. FFS Spatial domain pending RAN2 Study progress. FFS Cell level vs beam level prediction
NOTE: network sided models can be concluded in RAN#108 after RAN2 discussions
  Specify support for measurement event prediction for UE sided models [RAN2]:
  Specify signalling and protocol aspect to enable reporting inference outcome of UE sided model for measurement event prediction
  For both RRM measurement prediction and measurement event prediction [RAN2]:
  Specify signalling and protocol to facilitate functionality-based LCM procedures
  To be based on the LCM framework for Rel-19 AI/ML for NR air interface WI as much as possible
  For both RRM measurement prediction and measurement event prediction: [RAN4]
  Specify core requirements identified in study item phase
  Specify LCM-related requirements, if any
[1] RP-250812 Summary for RAN Release 20 5G-Adv Source: RAN Vice Chairs, RAN1, RAN2, RAN3, RAN4 Chairs

## Slide 3: FFS on spatial domain prediction
  RAN2#130 discussed the scenario of intra-frequency spatial domain prediction in cell dimension and beam dimension, and agreed to not consider predition in cell dimension by the UE-side model and will study predition in beam dimension. The agreements are as follows:
    The scenario of intra-frequency spatial domain prediction (in cell dimension) is not considered by the UE-side model in 5G. RAN2 assumes that a network-sided model requires no specification impacts. Intra-frequency spatial domain prediction (in cell dimension) involves measuring one or more cells as input to the model to derive L3 filtered cell-level measurements for the same time instance of another cell(s)
    The specification impact of intra-frequency spatial domain prediction in beam dimension will be studied by RAN2 for both UE-side and network-side model
  Based on RAN2’s progress, we support to consider spatial domain prediction in beam dimension for both UE-side and NW-side model in WI
  Proposal 1: Intra-frequency spatial domain prediction in beam dimension for both UE-side model and NW-side model are supported in WI.

## Slide 4: FFS on cell level vs beam level prediction
During the legacy handover procedure, the source gNB can configure the UE to report the beam level measurements of neighobor cells, which are used for target gNB to provide beam-specific access information of target cell to the UE
RAN2#129bis agreed that L3 Beam-level prediction specification impact will be studied
RAN2#130 agreed that for data collection for training of network-sided model, the UE can be configured to log one or more of the following data, including L3 beam level measurements:
    L3 cell level measurements
    L3 beam level measurements
    L1-filtered beam level measurements (if sub-case 1 and 3 is supported)
    Cell ID (FFS CGI of serving cell. If CGI is unavailable, or for neighboring cells the UE logs PCI-ARFCN as a fallback)
    Time info (if as agreed by AI/ML and/or if needed)
Based on the above analysis, we support to consider cell-level and beam-level RRM measurement prediction in WI
Proposal 2: Both L3 cell-level and L3 beam-level RRM measurement prediction are supported in WI.

## Slide 5: FFS on network sided model
RAN2#130 discussed the inference and report configuration, as well as data collection for training of network-sided model. The initial LCM framework has been established:
  Configuration and reporting framework: For network-side RRM measurement prediction, the legacy RRM measurement configuration and RRM measurement reporting framework can be used. FFS if there are specification impacts to support sub-case 1 and 3 (if supported) and interference for cell level prediction. To support cell/beam level prediction, one enhancements is to report RRM measurement results per cell at multiple time instances in one measurement report for NW-sided model
  Data collection for training: including data content (L3 cell/beam level measurments, L1 beam level measurements, cell ID, time info), logged mechanism (periodic and event-triggered logging), availability indication related info (data is available, full buffer, buffer threshold, low power), on-demand reporting, collected data handling during mobility scenario (idle/inactive, HO, RLF)
RAN2#129bis and RAN2#130 agreed to study NW-side model for temporal domain prediction, frequency domain prediction and intra-frequency spatial domain prediction in beam dimension
 | UE sided model | Network sided model
Measurement event prediction | Yes, | No (up to NW implementation)
Temporal domain case A | Yes, all sub cases | Yes
Temporal domain case B | Yes , all sub cases | Yes
Frequency domain | Yes , all sub cases | Yes
Spatial domain | intra-frequency, beam dimension | intra-frequency, beam dimension
L3 beam level measurement prediction | Yes, | Yes
Proposal 3: NW-sided model for temporal domain, frequency domain and spatial domain prediction are supported in WI.

## Slide 6: FFS on network sided model
Furthermore, RAN2 discussed whether to support all sub-use cases for network-sided model, but no consensus achieved
  According to the simulation results provided by companies, all sub-use cases show the gains for RRM measurement prediction
  We think that it is similar to UE-sided model, which sub-use case is used will be up to NW implementation, and the UE reports the measurement results (e.g. L1 beam level or L3 cell/beam level) based on NW configuration
Based on the above analysis, we think NW-sided model can be supported and all sub-use cases are considered in WI
Proposal 4: All sub-use cases for NW-sided model are supported in WI.
  Case 1: To predict L1 beam level results, then generate L3 cell/beam level results based on the predicted beam results
  Case 2: To directly predict L3 cell/beam level results based on L3cell/beam level results
  Case 3: To directly predict L3 cell/beam level results based on L1 beam level results

## Slide 7: Summary of Proposals
  Proposal 1: Intra-frequency spatial domain prediction in beam dimension for both UE-side model and NW-side mode are supported in WI.
  Proposal 2: Both L3 cell-level and L3 beam-level RRM measurement prediction are supported in WI.
  Proposal 3: NW-sided model for temporal domain, frequency domain and spatial domain prediction are supported in WI.
Proposal 4: All sub-use cases for NW-sided model are supported in WI.
  Case 1: To predict L1 beam level results, then generate L3 cell/beam level results based on the predicted beam results
  Case 2: To directly predict L3 cell/beam level results based on L3cell/beam level results
  Case 3: To directly predict L3 cell/beam level results based on L1 beam level results

## Slide 8: Potential WID scope
  Specify support for RRM measurement prediction for both UE and network sided models [RAN2]:
  Specify signalling and protocol aspect to enable reporting inference outcome of UE sided model for RRM measurement prediction
  Specify signalling and protocol aspect to enable reporting information from UE for inference operation of network sided model for RRM measurement prediction
  Temporal domain prediction, Frequency domain prediction and Spatial domain are supported
  Both cell level and beam level prediction are supported
  All sub-use cases studied in SI are supported for UE-sided model and NW-sided model
  Specify support for measurement event prediction for UE sided models [RAN2]:
  Specify signalling and protocol aspect to enable reporting inference outcome of UE sided model for measurement event prediction
  Both direct and indirect measurement event prediction are supported
  Specify signalling and protocol to facilitate functionality-based LCM procedures [RAN2]:
  To be based on the LCM framework for Rel-19 AI/ML for NR air interface WI as much as possible
  For both RRM measurement prediction and measurement event prediction: [RAN4]
  Specify core requirements identified in study item phase
  Specify LCM-related requirements, if any

## Slide 9: Thank you!