## Slide 1
CMCC
Views on ISAC for Rel-20
3GPP TSG RAN Meeting #1078
Prague, Czech, June 9-13, 2025
Agenda item: 15.3.2
RP-251386

## Slide 2
Overall consideration for ISAC
In RAN Chair’s Summary of 5G-A in previous meeting, it points out a study needs to be avoided duplicate scope in 5G-A and 6G in Rel-20. Thus, the study of ISAC for 5G-A should avoid overlap with the corresponding 6G study.
Now, companies have not anticipated the negative impacts of 5G-A ISAC, and proponents believe the RAN1 evaluation results are generally positive. In fact, the RAN3 ISAC should be based on validated RAN1 evaluations, the information exchanged via RAN3 interfaces would neither represents an urgent issue requiring immediate resolution nor pose a bottleneck for commercial deployment.
  E.g., In operator’s field test, the sensing result calculated by the SF deployed inside BBU can meet commercial requirements, so the ISAC currently can be supported by gNB implementation.
  Proposal 1: The study of ISAC for 5G-A should avoid overlap with the corresponding 6G study.
  Proposal 2: The RAN3-led ISAC should be based on validated RAN1 evaluations, the information exchanged via RAN3 interfaces would neither represents an urgent issue requiring immediate resolution nor pose a bottleneck for commercial deployment.

## Slide 3
RAN1 study on 5G-A ISAC
The scope of 5G-A RAN1 study on ISAC:
  Study and evaluate the performance of sensing for UAV use case
  Sensing modes: gNB mono-static mode
  No new waveform/RS to be specified in RAN1 and no UE impact is expected
In addition to the study of physical layer aspects of ISAC, the study should consider the data type for evaluation. The data type is highly related to the interface and architecture. To ensure the sensing data consistency for verification, the data type reported by RAN should be the sensing results and the raw measurement data used as verification data. It should be noted that the raw measurement data can be sampled randomly considered that the entire raw measurement data may be too large.
Therefore, a comprehensive study that addresses the physical layer aspects, data type and data consistency of ISAC should be studied in RAN1 before analyze the interface and architecture in RAN3.
  Proposal 3: Comprehensive study that addresses the physical layer aspects, data type and data consistency of ISAC should be studied in RAN1.
  Proposal 4: To ensure the sensing data consistency for verification, the data type reported by RAN should be the sensing results and the raw measurement data.

## Slide 4
RAN3 related aspects on 5G-A ISAC
The 5G-A ISAC regarding performance evaluation should be firstly studied in RAN1 for nine months from Aug, 2025 to Feb, 2026. Based on the outcome of RAN1 study, whether to have RAN3 SI/WI on 5G-A ISAC will be discussed in RAN#111 meeting (Mar, 2026).
The 5G-A ISAC SI has been already started in SA2 from April to Nov, 2025. Their study item aims at investigating the function enhancement, end to end service operations and procedures to support ISAC with the considerations of use cases based on the SA1 requirements.
The following aspects studied by SA2 will be coordinated with RAN groups:
  WT-1: Architecture and function enhancements to support sensing;
  WT-4: Sensing data and the associated information collection and transport mechanisms for result calculation;
If the RAN3 ISAC is finally determined in RAN plenary, RAN3 can directly enter the WI phase to follow the architecture designed by SA2 and specify the architectural aspects in RAN side based on the outcome of SA2 which avoids duplicate study of the same issue. Thus, it is unnecessary to start a parallel RAN3 SI for ISAC.
  Proposal 5: The 5G-A ISAC should be firstly studied in RAN1, whether to have RAN3 WI on 5G-A ISAC will depend on the outcome of RAN1 study.

## Slide 5
THANK YOU !