## Slide 1
0
Support of high power UAV UE in Rel-20
3GPP TSG RAN Meeting #108 RP-251389
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.4.4
Document for: Discussion
CMCC, China Telecom, China Unicom, SK Telecom, Verizon, Apple, CATT, Huawei, HiSilicon, MediaTek, OPPO, vivo, xiaomi, ZTE

## Slide 2
Motivation and Background
In recent years, the low altitude economy has been burgeoning with remarkable momentum, emerging as a new economic growth engine and attracting widespread attention. In China, low altitude economy has been considered as a new growth engine for the national economy. Many cities are planning UAV routes for technical trial.
The main application scenarios of UAV include low altitude logistics, travel, tourism, control and supervision, medical rescue, etc. so UL throughput and UL coverage is the key target compared with DL.
Deployment scenarios:
  BSs are deployed on the ground by adjusting the tilt angle upwards. The coverage height is up to 600~1000m. The ISD is about 2~4km.
  A direct radio link between BS on the ground and UAV UE
  Spectrum: TDD bands with same TDD pattern as TN, e.g. n41, n77/n78, n79
To reduce the network construction costs, the transmission power of the UAVs should be further increased to enhance the UL coverage for UAV.
  In China, the upper power limit of UAV UE is 33dBm for trial as issued by MIIT
To avoid severe interference to ground networks due to the increased uplink power limit, beamforming or directional antenna should be supported.
UAV BS
legacy BS
legacy BS
500m-1km

## Slide 3
Motivation and Background
Rel-18 NR_UAV
Directional antenna at UE side has been discussed in Rel-18 NR_UAV but no conclusion
  RAN1 has discussed the capability related issues, but no consensus has been reached.
  Conclusion from RAN1#112bis：
    There is no consensus on whether new UE UAV capabilities including beam related information, beam correspondence, or QCI Type-D should be reported and whether reporting the UE UAV beamforming capabilities only is sufficient or not to support beamforming based on beam switching among fixed directional antennas to limit interference and/or balance traffic load to adjacent cells in FR1 in Rel-18.
  RAN2 has not conducted any discussion on this objective.
RAN4 only supports PC3 omni-directional UAV with additional A-MPR and additional spurious emisison requirements
Rel-18 NR_ATG
ATG UE antenna types
  Considering the implementation freedom for ATG UE(e.g. for 2 GHz, to use omni antenna for ATG UE and for 4 GHz, to use antenna array for ATG UE), RAN4 agreed to introduce two ATG UE types to distinguish the antenna types for ATG UE. When define the RF and RRM requirements, RAN4 considered two kinds of UE types separately.
ATG UE power class
  Since the required power level for ATG might be varying in different aircraft types and also in different frequency ranges, it’s quite difficult to focus on one specific power class. A new capability for ATG UE is introduced to indicate the rated maximum output power (23dBm-40dBm) and its capability report granularity as 1dB.

## Slide 4
The interference for UAV-TN deployment scenario is less than the interference for TN-TN and TN-ATG deployment scenario.
No additional simulation is required. UAV BS and UE can reuse TN BS and PC3 UE co-existence requirements.
Case No. | interference case | analysis | ACLR/ACS requirements
1 | TN DL -> UAV DL | compared with TN DL->TN DL, antenna gain of aggressor TN BS towards UAV UE is at least 12-15dB less than the antenna gain towards UE on the ground if we assume UAV BS point above the horizontal line. So no further simulation and legacy TN requirements can be reused. | reuse TN UE PC3 ACS
2 | TN UL -> UAV UL | compared with TN UL->TN UL, antenna gain of victim UAV BS is at least 12-15dB less than the antenna gain of victim BS on the ground if we assume UAV BS point above the horizontal line. So no further simulation and legacy TN requirements can be reused. | reuse TN BS ACS
3 | UAV DL -> TN DL | compared with TN DL->TN DL, antenna gain of aggressor UAV BS towards TN UE is at least 12-15dB less than the antenna gain of TN BS towards TN UE on the ground if we assume UAV BS point above the horizontal line. So no further simulation and legacy TN requirements can be reused. | reuse TN BS ACLR
4 | UAV UL -> TN UL | compared with TN UL->TN UL, UAV UE has max 11dB antenna gain calculated from deployment scenario while victim BS antenna gain towards UAV UE is at least 12-15dB less than that towards TN UE. As for the pathloss, if we reuse the same model as used for ATG, UAV pathloss is 2dB, 4dB, 7dB and 11dB less than TN pathloss at 1km, 2km, 4km and 7km distance for LOS. but this pathloss can be compensated by the less number of UAV UE. for TN network, one network has 30-50 TN UE but UAV can only support less than 5 UE to avoid crash. so in total, legacy TN requirements can be reused. | reuse TN UE PC3 ACLR
 |  | compared with ATG UL->TN UL, ATG UE antenna gain is almost 12dB larger than UAV, i.e. ATG is 23dB and UAV is 11dB. Pathloss from ATG UE to TN BS is almost 20dB larger than UAV UE to TN BS when we consider UAV/ATG UE is just above the TN BS. so the interference is almost 8dB larger than ATG network. we re-simulate using ATG simulation by adding 8dB interference, final simulation results show legacy requirements is enough. | 
Note: related assumption for above analysis is listed in annex. |  |  | 
Co-existence Analysis
Notes: current minimum output level is much strict for UAV with higher power, i.e. larger dynamic range is required. the same logic for max input level
UAV fly speed = 8-15m/s, doppler shift 69~130Hz，0.1ppm =260 Hz

## Slide 5
Objectives for Rel-20
Scenario:
  BSs are deployed on the ground by adjusting the tilt angle upwards. The coverage height is up to 600~1000m. The ISD is about 2~4km.
  A direct radio link between BS on the ground and UAV UE
Specify RF requirements for UAV UE/BS to support higher UL output power and UL beamforming
  Example bands: only consider TDD with same TDD pattern, including n41, n77, n78, n79
  Consider UAV UE with antenna array with up to 33dBm maximum output power
  Specify RF requirements including output power, configured power, SEM, etc.
    Reuse legacy BS and PC3 UE co-existence requirements and no additional co-existence simulaiton is required
    Note: only define RF requirements for regions/areas without A-MPR and additional spurious requirement
Specify RRM requirements, if needed
Potential objectives
Notes: current minimum output level is much strict for UAV with higher power, i.e. larger dynamic range is required. the same logic for max input level
UAV fly speed = 8-15m/s, doppler shift 69~130Hz，0.1ppm =260 Hz

## Slide 6
THANK YOU！

## Slide 7
deployment parameter | typical value | 
max horizontal coverage distance | 3.5km for 2.6GHz, 2km for 4.9GHz | 
max coverage height | 1km | 
min coverage height | 0m | 
UAV BS antenna vertical beamwidth | 36 degree for 128TRx | 24 degree for 64TRx only for 2.6GHz
min coverage height | 1.38km | 2.25km
Annex: Evaluation parameters
Deployment Scenario: using following deployment scenarios for co-existence/RF requirements analysis
  Ground BS communicate with UAVs using main lobe.
  UAV BS located with TN BS from same operator
UAV UE parameter | typical value
antenna configuration | Tx: 2*2 or 4*1 for 2.6GHz and 4.9GHz
antenna element gain | 5dBi