## Slide 1
0
Views on RAN WG SI for 6G
June 2025
3GPP TSG RAN #108 RP-251398
Prague, Czech, June 9-13, 2025
Agenda Item: 16.2
Source: CMCC
Type: Discussion

## Slide 2
Background
This study item aims to
investigate a candidate set of items for minimum TPRs based on the Recommendation ITU-R M.2160, and, where applicable, the associated target values and key assumptions for the identified minimum TPRs.
  The outcome is expected to be shared by LS with ITU-R WP5D, as suitable, and used as a baseline for the subsequent study 6G in RAN
Identify typical and practical deployment scenarios defined by attributes such as carrier frequency, inter-site distance, user density, maximum mobility speed, and other relevant factors.
Develop 3GPP requirements for 6G Radio for improvement of existing services and for new services.
Determine the applicability of legacy services to 6G Radio, and define radio requirements for these, as appropriate.
Develop 3GPP requirements for 6G Radio for these practical deployment scenarios to ensure substantial gains in all relevant bands: overall performance, user experience, TCO reduction including at least:
  Ensure appropriate set of functionalities, minimize the adoption of multiple options for the same functionality, avoid excessive configurations, excessive UE capabilities and UE capabilities reporting
  Energy efficiency and energy saving: both for network and device
  Enhanced spectral efficiency
  Enhanced overall coverage, focus on cell-edge performance and UL coverage
  Wider channel bandwidth (at least 200MHz) support for 6G deployments at least above 2 GHz, around 7 GHz
  Re-use of existing 5G mid-band (~3.5GHz) site grid for 6G deployments in at least around 7 GHz and targeting comparable coverage to 5G mid-band
  Target scalable and forward compatible design for diverse device types
  Improved spectrum utilization and operations taking into account diverse spectrum allocations
  Aim at using common 6G Radio design, which meets mobile broadband service requirements as high priority, to also meet vertical needs
  Aim at a harmonized 6G Radio design for TN and NTN, including their integration
  System simplification, including reducing configuration complexity, enabling more efficient Cell/UE management, etc.
Define a time plan and steer work as appropriate for the RAN WGs during the 6G WG SI to deliver high-level decisions at least on the following areas:
  Fundamental 6G radio design aspects: waveform, numerology, channel coding, etc…
  Overall high-level aspects of 5G to 6G migration
  RAN architecture and interfaces, including RAN-Core interface
  Coordination of 6G AI/ML framework
Note: The detailed time plan for the high-level decisions above will be decided at RAN#108 at the approval of the 6G RAN WG SI and is to be aligned with the RAN SI progress.
Objective of Study on 6G Scenarios and Requirements (RP-250810)

## Slide 3
Highlight of the 6G SI workplan
  Part 1 (25Q3 ~ 26Q2@RAN1/2/3/4)
    Fundamental and common 6G radio design Feasibility studies
      Target for feasibility studies for fundamental 6G radio design aspects: waveform, numerology, channel coding and etc.
      2025Q4 to deliver high-level decision of technical identification of these fundamental and common aspects.
  Part 2 (26Q1 ~ 27Q1@RAN1, 27Q2@RAN2/3/4)
    More feasibility studies and functionality studies
      To address features that are followed by fundamental and common 6G radio design aspects
  Note: evaluations including discussion of link and system simulation assumptions are conducted across the SI.
Timeline for 6G SI workplan
Fundamental and common 6G radio design Feasibility studies
Functionality studies
More feasibility studies
Part 1
Part 2
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
2025
2026
2027
High-level decisions of technical identification

## Slide 4
Discussion on 6G workplans
Fundamental and common 6G radio design Feasibility studies
Fundamental 6G radio design aspects
  Waveform and multiple access schemes
  Bandwidth, Numerology and frame structure
  Channel coding and modulation
  Note: Check points @ 2025Q4 to deliver high-level decisions
Common design aspects
  Initial access and mobility
    Note: Including synchronization signal and initial access procedure, Broadcast signal/channel, Paging design, random access channel and random access procedure, Mobility procedure
  Duplexing
  NTN
    Note: Aim at a harmonized 6G Radio design for TN and NTN, including their integration
  LPWA
    Note: Aim at using common 6G Radio design, which meets mobile broadband service requirements as high priority, to also meet vertical needs.
Artificial Intelligence (AI)/Machine Learning (ML) for 6G air interface
  6G AI/ML framework
  Including identification of AI use cases. Check points@ 2025Q4 to deliver high-level decisions
RAN 1 areas
More feasibility studies and functionality studies
Network and UE Power saving
  Note: Including LP-WUS/WUR …
Multi-antenna scheme
Scheduling/HARQ aspects
  Note: Including L1/L2 control channel design (i.e., DL and UL), scheduling/HARQ mechanism.
Integrated sensing and communication
  Note: Including sensing related evaluation assumptions. Start from Q1@2026?
Evaluation for 6G
  Note: including simulation assumptions and scenarios. Including link and system-level simulation assumptions

## Slide 5
Discussion on 6G workplans
Control plane
    Functionality, Identification of functionality of the control plane
      Include the support of harmonization and simplification of the similar functions and/or signalling
      Note: Aim to minimize the adoption of multiple options for the same functionality, avoid excessive configurations
    RRC States
      Consideration of RRC states related to mobility, data activity, power saving etc.
    System information,Initial access, mobility
      Flexible system informaiton, unified access control, paging, unified mobility management etc.
      Note: Target flexible, simplified, scalable and forward compatible design for diverse device,service and scenario types
    Unified Multi-carrier Framework
      Note: target for common framework to support carrier aggregation, supplementary UL, multiple carrier operations as one cell and etc.
    UE capability
      Note: Aim to avoid excessive UE capabilities and UE capabilities reporting
        Note: Aim at a harmonized 6G functionality design for TN and NTN, including their integration
User plane, identification of functions of the user plane and allocation to user plane protocol layers, support of radio bearer within the 6G, etc.
    User plane protocol Simplification and function harmorization
      Note: study on simplification and/or customization/modular of protocol for diverse device,service and scenario types
      Note: including supporting of low latency, high reliability and high bit rates for immersive communication, e.g.,UE aggregation,Multiple-Factor Scheduling
RAN Data plane, identification of functions and protocol layers of the data plane, support of Data bearer within the 6G, etc.
    Support of AI/ISAC data collection, communication of AI models
    Note: including impact of supporting life cycle management for AI/ML and supporting of ISAC
NR-6G interworking aspects, identification of functionality of the NR-6G interworking (e.g. inter-RAT mobility, dual steer/dual stack etc.).
RAN 2 areas

## Slide 6
Discussion on 6G workplans
Radio Access Network architecture, interface protocols and procedures, including RAN-Core interface;
  Study and identify architecture for supporting new functionalities and interfaces, e.g. introduce new network entities / nodes for supporting AI/ML as a service;
  Study and identify the functionalities and use cases requiring service-based interface;
  Note: Overall high-level aspects of 5G to 6G migration
  Note: Coordination of 6G AI/ML framework
RAN 3 areas

## Slide 7
Discussion on 6G workplans
Spectrum and system parameters
  Spectrum and co-existence study
  System parameters
    Note: including for example channel raster, sync raster, channel bandwidth, spectrum utilization and etc.
UE RF
  Baseline assumptions for 6G NR UE
    Note: including for example number of Tx and Rx, power class, bandwidth and etc.
  Unified and simplified RF requirements
    Note: including for example power class, MPR, MSD and etc.
BS RF
  BS RF requirements considering MSR and AAS
  SBFD RF requirements for 6G BS
RRM
  Measurement gap
    Note: target for Unified and simplified measurement gap design considering different use cases and requirements, e.g. TN / NTN, immersive communication, energy efficiency
  Measurement for intra/inter frequency and inter-RAT (5G)
    Note: energy efficiency needs to be taken into account
AI
  Identify AI related use cases from RAN4 perspective
  Testability related
Specification simplification
  Including UE RF, BS RF and RRM spec simplification
RAN 4 areas

## Slide 8
Thank you!