## Slide 1: Scope discussion on CSI compression in AI/ML Air Interface
Sources: Panasonic
3GPP TSG RAN #108
Prague, Czech Republic, June 9-13, 2025
Agenda: 15.1.1
TDOC: RP-251403
For: discussion

## Slide 2: Background 1
For inter-vendor collaboration, RAN1 concludes that both Direction A and Direction C are feasible. For Direction A, RAN1 concludes that the feasible sub-options are sub-option 4-1 and sub-option 3a-1, and in case of sub-option 3a-1, with and without target CSI sharing from NW side.
Performance: Direction C with standardized reference model (structure + parameters) ensures a minimum performance requirement, while Direction A with standardized reference model structure + parameters (sub-option 3a-1), or standardized dataset exchange (sub-option 4-1) from NW-side to UE-side may achieve better performance.
Direction C addresses inter-vendor collaboration complexity: From RAN1 perspective, Direction C (a.k.a., option 1) eliminates the inter-vendor collaboration complexity if it is feasible to standardize the model. The fully standardized reference model (structure + parameters) should be trained using synthetic data. The model structure and parameters are assumed to be equivalent to the to-be-specified model, if specified, for performance requirements in RAN4. RAN1 concludes that the scalable model structure specification and model parameters specification is feasible, but the conclusion on interoperability and RAN4 testing feasibility is a separate study in RAN4.
For Direction A with sub-option 4-1 and 3a-1, RAN1 concludes that standardized signaling, if feasible and specified, can be used for model parameter / dataset exchange to alleviate / resolve the inter-vendor collaboration complexity. The standardized signaling, if needed, may be over-the-air, or other approaches. For OTA and non-OTA based standardized signaling, as well as the feasibility of standardized signaling, related status have been provided in [R2-2503169]. For sub-option 3a-1, the specified encoder (a.k.a., CSI generation part) structure should be determined using synthetic data, and the scalable encoder structure specification is feasible.
For NW-side performance monitoring, RAN1 concludes that target CSI reporting via legacy codebooks can be used. Target CSI reporting with CSI codebook enhancement via higher-resolution parameter combination may be beneficial for improving NW-side performance monitoring with additional cost of complexity and overhead at UE side.
For UE-side side monitoring, RAN1 concludes that it is feasible, but some companies think that, at least in some UE-side monitoring options, NW-side monitoring with target CSI reporting is needed to check the reliability of UE-side monitoring reports.
NW side data collection for training is studied including data format, configuration of rank / layer, number of subbands and mechanisms for ground-truth reporting, but not all aspects are concluded. UE side data collection for training is studied including NW configuration or UE request, configuration for temporal aspects, but not all aspects are concluded. Aspects that were not concluded can be discussed in the normative phase.

## Slide 3: Background 2
The study of CSI feedback using two-sided model is complete from RAN1 perspective.
Based on the study, for addressing inter-vendor collaboration complexity, RAN1 identifies the following specification impacts for supporting sub-option 3a-1 (including with target CSI and without target CSI), sub-option 4-1, and Direction C
Reference model / structure specification (for sub-option 3a-1 and Direction C)
  Note: The so called fully specified reference model discussed in RAN1 for Direction C is assumed to be equivalent to the to-be-specified model, if specified, for performance requirements in RAN4.
  Note: The model structure(s) for the reference encoder in inter-vendor collaboration sub-option 3a-1 can be same as/equivalent to the structure of the RAN4 defined/specified (if defined/specified for testability) reference encoder.
    To reduce the workload of the potential normative work scope, the model structure(s) for the reference encoder in inter-vendor collaboration sub-option 3a-1 is(are) same as/equivalent to the structure of the RAN4 defined/specified (if defined/specified for testability) reference encoder.
  Note: RAN1 has studied and agreed on a scalable model structure for feasibility study during Rel-19 study, and considers that can serve as a starting point for the model structure specification for the potential normative work.
Format and contents of parameter/dataset/information exchange: dataset (for 4-1 and 3a-1 with target CSI)/ encoder parameter (for 3a-1) / additional information (for 3a-1 and 4-1).
The workload can be reduced by identifying the common part among different aspects.
Based on the study, RAN1 recommends the following with potential RAN1 specification impacts common to all inter-vendor collaboration options.
Recommend Case 0
  Case 2 and 3 can be considered for further enhancement built upon the specification of case 0.
Recommend following specification impacts for the two-sided CSI compression use case
  Model pairing procedure including ID and applicability reporting
  Inference aspects including target CSI type, measurement and report configuration, CQI / RI determination, payload determination, quantization configuration / codebook, UCI mapping, CSI processing criteria and timeline, priority rules for CSI reports
  NW and UE side data collection for training,
    Target CSI format
    Note: The framework defined in BM and CSI prediction use cases could be reused.
  Specify performance monitoring, if needed

## Slide 4: Direction A and/or direction C?
Both Direction A and C are required and to be carried by following WGs.
  Direction A in RAN1/2 for better performance
  Direction C in RAN4 to ensure a minimum performance requirement

## Slide 5: Sub-option 4-1 and/or 3a-1 in Direction A
Within Direction A, our preference is to focus Sub-option 4-1
  Sub-option 3-1 would require more effort to NW vendor and/or operator for generate the parameters (in spite it allows more control UE behaviour possibility).
  Sub-option 3-1 would require more effort to UE/chip set vendor for optimization of the device complexity and power consumption as the given reference model/parameter may not be directly used.
  Sub-option 3-1 can be more difficult for the test as how much of the function is responsible to UE side or NW side are unclear.
  Sub-option 3-1 can be more standardization effort depending on the possible allowed amount of UE side modification from given reference model/parameter.
  Sub-option 3-1 can be longer standardization time as it is required to wait the outcome of RAN4 defined/specified reference model.

## Slide 6: Dataset and parameter sharing
Within R2-2503169, "non-OTA approaches" should be taken.
  OTA approach was no consensus on feasibility in RAN2.
  Non-OTA approaches can reduce the air-interface overhead.
Alternative 1 (non-OTA approach)
Alternative 2 (OTA approach):