## Slide 1: Views on Reconfigurable Intelligent Surface for 6G
Document for: Discussion and Decision
Agenda Item: 16.2
3GPP TSG RAN Meeting #108 RP-251406
Prague, Czech Republic, June 9-13, 2025
Source: Southeast University, Beijing Jiaotong University, Shanghai Jiao Tong University, Beijing University of Posts and Telecommunications, Zhejiang University, Peking University, Peking university shenzhen graduate school, Xidian University, Fudan University, Huazhong University of Science and Technology, Chongqing University of Posts and Telecommunications, Greenerwave, University of Glasgow, Queens University Belfast, Nanyang Technological University

## Slide 2: Background
Reconfigurable Intelligent Surface (RIS) is an advanced wireless technology that enhances signal coverage, capacity, and efficiency, enabling smart radio environments.
With lower cost, reduced power consumption, and easy deployment compared to traditional solutions, RIS is a potential game-changer for 6G and beyond.
As one of the most promising technologies in wireless communication, RIS has attracted active theoretical research from universities and institutes worldwide, along with joint industry efforts in engineering development and standardization.
Technically, RIS is mature and ready for standardization.
[1] RIS TECH Alliance, "Reconfigurable Intelligent Surface Technology White Paper, " Mar. 2023. [Online] https://doi.org/10.12142/RISTA.202302002
[2] ETSI. “Industry Specification Group (ISG) on Reconfigurable Intelligent Surfaces (RIS) Activity Report 2023,” https://www.etsi.org/committee-activity/activity-report-ris?utm_source
[3] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/
[4] FuTURE Forum, “White Paper on Channel Modeling and Simulation for Reconfigurable Intelligent Surface,” Nanjing, China, Apr 2025, doi: 10.12142/FuTURE.202504004. [Online] https://www.risalliance.com/en/channel-modeling-and-simulation-for-reconfigurable-intelligent-surface/
[5] FuTURE Forum ,“White Paper on Potential Standardization Work for Reconfigurable Intelligent Surface White Paper,” Nanjing, China, Apr. 2025. doi: 10.12142/FuTURE.202504003. [Online] https://www.risalliance.com/en/potential-standardization-work-for-reconfigurable-intelligent-surface-white-paper/

## Slide 3: Key Enabler for ITU-Defined 6G Requirements (1/2)
RIS are a key technology for enabling ubiquitous connectivity in 6G.
  RIS provides a low-cost solution for enabling continuous coverage in mid- to high-frequency bands.
  When deployed in a distributed manner, RIS can cost-effectively create a ubiquitous MIMO near-field propagation environment, thereby enabling full exploitation of the spatial resources available in near-field MIMO.
Enhanced Signal Coverage & Quality
  RIS consists of programmable meta-surfaces that can reflect, focus, or steer wireless signals to improve coverage in dead zones (e.g., indoors, urban areas, tunnels).
  Helps in extending network reach without additional power-intensive base stations.
Energy Efficiency
  RIS passively reflects signals with minimal energy consumption, unlike traditional relays or repeaters that require active power.
  Reduces the overall energy consumption of wireless networks, contributing to greener 6G systems.
[1] ITU, “Framework and overall objectives of the future development ​of IMT for 2030 and beyond,” Step. 2023.
[2] RIS TECH Alliance, "Reconfigurable Intelligent Surface Technology White Paper, " Mar. 2023. [Online] https://doi.org/10.12142/RISTA.202302002
[3] ETSI. “Industry Specification Group (ISG) on Reconfigurable Intelligent Surfaces (RIS) Activity Report 2023,” https://www.etsi.org/committee-activity/activity-report-ris?utm_source.
[4] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/

## Slide 4: Key Enabler for ITU-Defined 6G Requirements (2/2)
Improved Spectral Efficiency
  By intelligently controlling signal reflections, RIS reduces interference and enhances signal strength, leading to higher data rates and better spectrum utilization.
  Enables more users to connect simultaneously without degrading performance.
Cost-Effective Deployment
  RIS panels are low-cost and easy to install compared to deploying additional base stations or fiber optics.
  Ideal for rural areas, smart cities, and IoT networks where infrastructure costs are a concern.
Flexibility & Adaptability
  RIS can dynamically reconfigure its reflection properties to adapt to changing network conditions (e.g., user movement, obstacles).
  Supports massive MIMO and beamforming for better directional signals.
Security Enhancement
  RIS can direct signals away from eavesdroppers, improving physical-layer security in wireless networks.
  Helps prevent jamming and unauthorized access.
[1] ITU, “Framework and overall objectives of the future development ​of IMT for 2030 and beyond,” Step. 2023.
[2] RIS TECH Alliance, "Reconfigurable Intelligent Surface Technology White Paper, " Mar. 2023. [Online] https://doi.org/10.12142/RISTA.202302002.
[3] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/

## Slide 5: Enabling continuous coverage for mid- and high-frequency networks
Cost-Effective Deployment
  RIS can be installed on existing 5G BSs and ubiquitously deployed between them. This strategy facilitates continuous coverage in U6G, new mid-band, and millimeter-wave frequencies at a lower cost.
Mitigating Beam Blockage
  Strategically placing RIS along signal paths allows for the redirection of electromagnetic waves, effectively overcoming blockage issues prevalent in mid- and high-frequency bands.
Signal Enhancement and Interference Suppression
  The large aperture of RIS enables beamforming gains that enhance signal strength and control electromagnetic wave propagation, thereby suppressing interference.
Given that 6G NBs are expected to share sites with sub-6 GHz 5G NBs, RIS offer a promising solution for achieving continuous coverage in mid- to high-frequency networks. Their advantages—low cost, low power consumption, and ease of deployment—make them ideal for enhancing 6G network performance.
[1] RIS TECH Alliance, "Reconfigurable Intelligent Surface Technology White Paper, " Mar. 2023. [Online] https://doi.org/10.12142/RISTA.202302002.
[2] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/

## Slide 6: Enabling Ubiquitous Sensing and Positioning
Two approachs
  Enhancing SINR and Establishing Virtual LoS Channels with RIS
  Integrating Sensing Capabilities into RIS
  Key Benefits of RIS in Sensing and Positioning
  Continuous Sensing Coverage: RIS can establish ubiquitous near-field environments, supporting comprehensive 3D sensing and improving overall coverage.
  On-Demand LoS Path Construction: By strategically deploying RIS, LoS channels can be established as needed, enhancing the accuracy of sensing and positioning, especially in scenarios where direct paths are obstructed.
  High Spatial Resolution in Near-Field: The near-field operation of RIS enables high-resolution spatial sensing, thereby improving the precision of localization services.
  Sensing-Assisted Communication: By creating a twin electromagnetic channel environment, RIS can reduce the overhead associated with channel measurement feedback, thus enhancing communication efficiency.
RIS offer a cost-effective, low-power, and easily deployable solution for enhancing sensing and positioning services in 6G networks. Their capability to form large antenna apertures facilitates dense deployment, enabling the creation of near-field LoS environments that support continuous coverage for sensing and localization applications.
[1] RIS TECH Alliance, "Reconfigurable Intelligent Surface Technology White Paper, " Mar. 2023. [Online] https://doi.org/10.12142/RISTA.202302002.
[2] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/

## Slide 7: RIS-based Novel Phased Array Antenna (PAA)
RIS-based PAA
  A large-scale antenna array technology solution utilizing 6G RIS. This solution replaces traditional millimeter-wave active antenna arrays with 6G RIS arrays.
  By controlling a large number of low-cost, low-power controllable reflection/transmission elements within the 6G RIS, it effectively achieves large-scale antenna beam control and shaping.
RIS provide a cost-effective, low-power, and easily deployable solution for enhancing sensing and positioning services in 6G networks. Their capability to form large antenna apertures facilitates dense deployment, enabling the creation of near-field LoS environments that support continuous coverage for sensing and localization applications.
RIS-wing Base Station
  Two RIS panels are installed on either side of the AAU, resembling a pair of wings. By collecting and reflecting sidelobe signals through the RIS panels on both sides, a multipath effect is achieved, enhancing overall cell capacity.
[1] RIS TECH Alliance, "Reconfigurable Intelligent Surface Technology White Paper, " Mar. 2023. [Online] https://doi.org/10.12142/RISTA.202302002.
[2] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/

## Slide 8: RIS is ready for 6G
......... 2014 ...
2020
2021
2022
2023
2024
2025
Academic
IMT-2030(6G)
☆ 2020.6 Academia to industry
Establishment of RIS Task Group
June 2021:
White Paper on 6G Overall Vision and Potential Key Technologies
Sept. 2021:
RIS Technology Research Report (V1)
2022.12
RIS Technology Research Report (V2)
Publish RIS test results(V1)
CCSA
2020.9 TC5WG6
Initiate a project on the engineering research of RIS
2023.4 TC5WG6
Establish an engineering research project on RIS
ETSI
RISTA
ITU-R
2021.2
IMT Future Techonology Trends
RIS is a key candidate technology for 6G.
driving factor“Controllable Radio Environment”
2021.10.4
Establishment of theISG RIS
2021.9
1st RIS Tech Forum
☆ 2022.4.17
Establishment of the RIS Tech Alliance (RISTA)
2023.2.12
2nd RIS Tech Forum
Release of the RIS Technology White Paper
Others
2018.11
DOCOMO's early RIS prototype test
Series of RIS Engineering Experiments, testing in Live 5G Networks, RIS Prototype
2023.4
RIS Reports: Use Cases, Deployment Scenarios and Requirements
2020.1
DOCOMO's prototype trial of a transparent metasurface
Theoretical
&
Technical
Accumulation
ZTE Unveils Dynamic RIS 1.0 and 2.0
2023.12.6
RIS Technology Research Report (V3)
Publish RIS test results(V2)
RIS Reports: Engineering Implementation and Near-Field
RIS Selected as One of the Top 10 Emerging Technologies at the Summer Davos Forum
2024.11.9
3rd RIS Tech Forum
Global Initiative to Jointly Promote RIS Development
The inaugural year of 6G standardization
2024.11
RIS Technology Research Report (V4)
Publish RIS test results(V3)
2025.4.11
FuTURE, RIS White Paper Series
3GPP
2022 Rel-18
Proposals: RIS, RIS-like NCR
RIS-like NCR SI
2023 Rel-19
Channel model: ISAC, 7-24GHz
RIS-like NCR WI

## Slide 9: RIS is Ready for 6G: 3GPP Standardization
The RIS channel modeling work is rooted in the 3GPP TR 38.901 channel model and builds on the foundational work of ISAC and 7~24 GHz channel modeling.
Topics of ISAC channel modeling in the 3GPP Release 19 phase that can inspire the relevant solutions for RIS channel modeling
ISAC-Channel Modeling | Target channel modeling | Target modeling | Model simplification | Coupling of target channel and background channel | New features | ISAC-specific features
 | Whether the target channel is cascaded convolution or single point | Target modeling based on the RCS scheme RCS is categorized into large and small scales | Simplified schemes for cluster or path deleting, and multipath matching | The target channel and the background channel need to be power normalized | Spatial consistency | Monostatic modeling, environment object modeling, target micro-Doppler, blockage modeling, typical target RCS classification modeling, RCS randomness
RIS-Channel Modeling | RIS cascade channel modeling | RIS Physical Model | RIS Cascade channel simplification | RIS Cascaded channel coupled to BS-UE channel | New features | \
Near-field is an important research topic at 7-24 GHz, and large-size RIS is one way to generate a near-field environment.
[1] FuTURE Forum, . “[White Paper] Channel Modeling and Simulation for Reconfigurable Intelligent Surface,” Nanjing, China, Apr 2025, doi: 10.12142/FuTURE.202504004. [Online] https://www.risalliance.com/en/channel-modeling-and-simulation-for-reconfigurable-intelligent-surface/
[2] ETSI. “Industry Specification Group (ISG) on Reconfigurable Intelligent Surfaces (RIS) Activity Report 2023,” https://www.etsi.org/committee-activity/activity-report-ris?utm_source

## Slide 10: Observations and Proposals
Observations
  RIS are poised to be a game-changer for 6G, offering unprecedented control over wireless environments.
  With its characteristics of low cost, low power consumption, and low complexity, RIS represents a key enabling technology for supporting future 6G application scenarios.
  From a technical maturity standpoint, RIS is well-positioned for standardization.
Proposals
  RIS should be included as a key component in the scope of the 6G Rel-20 RAN Study Item.
  The standardization work on NCR and channel models in 5G-A Rel-18 and Rel-19 can lay the foundation for RIS standardization research in 6G.

## Slide 11: Appendix: RIS Prototype Test Cases
[1] FuTURE Forum., “White Paper on Prototyping of Reconfigurable Intelligent Surface ,” FuTURE Forum, Nanjing, China, Apr 2025. doi:10.12142/FuTURE.202504005. [Online] https://www.risalliance.com/en/white-paper-on-prototyping-of-reconfigurable-intelligent-surface/

## Slide 12: Case #1: Stadiums Scene
The Hangzhou Asian Games Velodrome covers an area of 2,500 square meters, with a size of about 85 meters long and 32 meters wide. Active antenna units (AAUs) are deployed in the venue, and there are blind spots covered by obstacles. By deploying RIS in the grandstand area, the distance between the AAU and the RIS is 14m, the angle from the RIS to the near point of the stadium center area is -7°, and the distance is between 40m~45m, and the RIS fully covers the entire central area
 | With RIS |  |  |  | Without RIS |  |  |  | Comparison |  |  | 
Beam ID | SS-RSRP(dBm) | SS-SINR(dB) | DL-Tput(Mbps) | UL-Tput(Mbps) | SS-RSRP(dBm) | SS-SINR(dB) | DL-Tput(Mbps) | UL-Tput(Mbps) | SS-RSRP提升(dB) | SS-SINR提升(dB) | DL-Tput提升(%) | UL-Tput提升(%)
2050 | -65.86 | 27.95 | 3138.38 | 536 | -75.21 | 18.19 | 1362.56 | 398.92 | 9.35 | 9.76 | 130.33 | 34.56
2066 | -69.07 | 27.46 | 2896.05 | 535.76 | -80.32 | 19.69 | 1418.42 | 377.57 | 11.25 | 7.77 | 104.17 | 41.90
2071 | -73.01 | 24.81 | 2528.21 | 534.46 | -91.54 | 9.01 | 373.08 | 197.79 | 18.53 | 15.8 | 577.66 | 170.22
2072 | -72.11 | 22.94 | 2028.48 | 536.72 | -87.998 | 6.83 | 354.76 | 167.83 | 15.87 | 16.11 | 471.79 | 219.80
2075 | -72.43 | 24.6 | 3165.02 | 536 | -92.02 | 8.25 | 273.79 | 230.79 | 19.59 | 16.35 | 1052.72 | 132.67
2078 | -72.41 | 22.43 | 2118.03 | 534.43 | -95.12 | 6.78 | 222.55 | 121.22 | 22.71 | 15.65 | 851.71 | 340.88
With RIS deployed, beam switching under RIS and handover from the base station to RIS are both smooth. RIS beams can track users accurately and promptly, maintaining stable signal strength.
RSRP, SINR, and uplink/downlink throughput at six test points show significant improvements—RSRP increases by up to 22 dB at distant points and nearly 10 dB at close range.
At beam ID 2075, user uplink and downlink rates increase by approximately 130% and 1050%, respectively.

## Slide 13: Case #2: Office Building
The office building test environments include AIS's office area in Thailand, the teaching area at Southeast University, and the experimental area at Xidian University. AIS has deployed millimeter-wave test base stations in its office area; Southeast University has commercial Sub-6GHz NR base stations in its teaching buildings; and Xidian University has a 5.8 GHz Wi-Fi network in its labs. Due to obstructions such as walls, partitions, office furniture, and lab equipment, all areas experience significant signal blind spots and weak coverage zones.
（a）Office （b）Campus （c）Laboratory
 | With RIS |  |  | Without RIS |  |  | Comparison |  | 
Static RIS testing | SS-RSRP(dBm) | DL-Tput(Mbps) | UL-Tput(Mbps) | SS-RSRP(dBm) | DL-Tput(Mbps) | UL-Tput(Mbps) | SS-RSRP gain(dB) | DL-Tputgain(%) | UL-Tputgain(%)
14m with FR2 in Office | -68 | 1550 | 266 | -90 | 700 | 80 | 22 | 121% | 232.5%
23m with FR2 in Office | -71 | 1500 | 266 | -92 | 400 | 70 | 21 | 275% | 280%
Dynamic RIS testing | SS-RSRP(dBm) | DL-Tput(Mbps) | SINR(dB) | SS-RSRP(dBm) | DL-Tput(Mbps) | SINR(dB) | SS-RSRP gain(dB) | DL-Tputgain(%) | SINRgain(dB)
FR2 in Office | -63.8 | 1576.5 | 27.8 | -87.5 | 418.9 | 11.7 | 23.7 | 276% | 16.1
Sub6G in Campus | -74.07 | / | / | -80.23 | / | / | 6.16 | / | /
in Laboratory (Point 2) | -44.56 | / | / | -51.37 | / | / | 6.81 | / | /
5.8G in Laboratory (Point 12) | -47.27 | / | / | -65.31 | / | / | 18.04 | / | /
5.8G in Laboratory (Point 16) | -63.33 | / | / | -79.29 | / | / | 15.96 | / | /
5.8G in Laboratory (Point 22) | -79.27 | / | / | -90.07 | / | / | 10.8 | / | /

## Slide 14: Case #3: mmWave Bands
In the millimeter-wave urban test environment in Turkey, buildings, vegetation, and other obstructions result in severe blockage, causing large areas at the cell edge to lack LoS with the base station. In dynamic terminal movement tests, beam switching between the base station and RIS was smooth, with average RSRP gains of about 12–16 dB and physical layer throughput improvements of approximately 500%–1800%. With dynamic coordination between the base station and RIS, RIS beams could accurately and promptly track users, maintaining stable signal strength and significantly improving coverage quality in non-LoS areas.
 | With RIS |  | Without RIS |  | Comparison | 
Distance | SS-RSRP(dBm) | DL-Tput(Mbps) | SS-RSRP(dBm) | DL-Tput(Mbps) | SS-RSRP(dB) | DL-Tput(%)
0-120m | -74.15 | 1403.23 | -86.92 | 233.66 | 12.77 | 500
120-240m | -79.07 | 1095.9 | -95.97 | 55.96 | 16.9 | 1858

## Slide 15: Case #4: cmWave Bands
The extended coverage test for a 10 GHz hyperscale hybrid RIS was conducted on Heqingli Pedestrian Street in Chengdu, which is 320 m long. The RIS consists of 16,800 units with an array size of 3.44 m × 1 m and is installed at the street entrance. The base station is 6 m from the RIS, with a 20° beam angle incident on the RIS surface. Compared to the no-RIS scenario, average RSRP improves by about 15 dB, and the terminal access range extends from 220 m to beyond 320 m.
RSRP
SNR
Throughput
w/ RIS
w/o RIS

## Slide 16: Case #5: Campus
Static RIS test environments for Sub-6GHz live networks were set up in Nanjing Wireless Valley, the South Campus of Xidian University, and the campus of Shanghai Jiao Tong University. In Wireless Valley and Xidian, the distance between the base station and RIS is about 50–100 m; in the Shanghai Jiao Tong setup, it's about 10 m, with the RIS-to-terminal distance around 50 m. As the test terminal moves through the campus, the static RIS improves RSRP in weak coverage areas by 2–12 dB.
 |  | With RIS | Without RIS | Comparison
Scenarios | Parameter | SS-RSRP(dBm) | SS-RSRP(dBm) | SS-RSRP提升(dB)
Crossing | 16*32 | -75.45 | -79.48 | 4.03
Building with BS on the roof | 16*32，2bit | -58.14 | -63.01 | 4.87
 | 16*16，2bit | -60.86 | -63.01 | 2.15
 | 16*32，1bit | -59.87 | -63.01 | 3.14
Building with RIS on the roof | 20*20，1bit | -85.74 | -97.98 | 12.24

## Slide 17: Case #6: Shadows under the Tower
The base station is mounted on the rooftop of the 5th floor at a height of approximately 24 m. A pedestrian passage, about 18 m long, runs below. The RIS is deployed at a nearby intersection, with a 45° azimuth and 20° elevation angle relative to the base station. The shadow area beneath the tower lies about 35–55 m from the RIS.
In non-shadowed areas, RIS has little impact on the test terminal’s signal quality.
In under-tower shadow areas (35–55 m from RIS), RSRP improves by approximately 5–10 dB.

## Slide 18: Case #7: Near-Field Focus
At Xidian University’s new campus, RIS-assisted near-field focusing performance was tested using a live network base station and commercial phones. The base station is 24 meters high, about 150 meters from the RIS, and the RIS-to-terminal distance ranges from 1 to 1.5 meters.
(a)Top view (b)Front view (c)RSRP CDF (d)SINR CDF
When the RIS near-field focus is at 1.5m, the average RSRP improves by about 6dB and SINR by about 3dB.
When the focus is at 1m, the average RSRP improves by about 8dB and SINR by about 5dB.

## Slide 19: Case #8: User Mobility with Distributed Multi-RIS
In an open area, AAUs are deployed on rooftops, with Zones 1, 2, and 3 as AAU coverage blind spots. RIS1 and RIS2, controlled by the network, are deployed in Zones 2 and 3 to enable distributed collaborative coverage enhancement. In the corridor scenario, four zones are formed based on the building structure, with three network-controlled RIS units deployed to coordinate coverage with the base station.
In the open area without RIS, Terminal 1 in Zone 1 receives an RSRP of about -65 dBm, with uplink and downlink throughput around 500 Mbps and 2800 Mbps. In Zones 2 and 3, the RSRP drops to about -80 to -90 dBm, with throughput around 100 Mbps uplink and 500 Mbps downlink. After deploying RIS1 and RIS2, the terminal achieves microsecond beam switching among AAU, RIS1, and RIS2. In RIS1-covered Zone 2 and RIS2-covered Zone 3, RSRP improves to -70 to -75 dBm, and throughput rises to 500 Mbps uplink and 2800 Mbps downlink. Brief drops in RSRP and throughput occur when the terminal turns away from the beam.
In the corridor scenario’s BS-NLOS areas, average RSRP improves by 4.56 to 13.98 dB compared to no RIS (S1: 13.98 dB, S2: 7.21 dB, S3: 4.56 dB). Downlink throughput averages 1.22 to 4.95 times higher without RIS (S1: 2.66×, S2: 4.95×, S3: 1.22×). In BS-LOS areas, distributed RIS does not affect mobile user performance.

## Slide 20: Case #9: Outdoor Multi-User Scheduling
AAU is deployed on the rooftop, with Zone 1 covered by AAU line-of-sight and Zone 2 as the AAU non-line-of-sight blind area. A network-controlled RIS is deployed in Zone 2 to enable coordinated coverage enhancement and multi-user scheduling with the base station.
When a single test terminal connects to RIS, the received RSRP is about -73 dBm, with peak uplink and downlink throughput around 266 Mbps and 1700 Mbps.
When two test terminals share RIS or AAU in time-division mode, uplink and downlink throughput correspond to their share of wireless resources.
When two terminals connect separately to RIS and AAU with successful MU-MIMO pairing, both achieve peak throughput.
When RIS is off, the terminal in Zone 2 has an RSRP of about -96 dBm and peak uplink/downlink throughput of about 17 Mbps and 40 Mbps.
Mode | Terminal | Anchor | SS-RSRP(dBm) | DL-Tput(Mbps) | UL-Tput(Mbps)
Single User | UE1 | RIS | -73 | 1700 | 266
 | UE2 | RIS | -72 | 1700 | 266
TDD Users | UE1 | RIS | -73 | 845 | 125
 | UE2 | RIS | -73 | 842 | 124
 | UE1 | RIS | -73 | 835 | 125
 | UE2 | AAU | -58 | 850 | 130
Multi-user with space diversity | UE1 | RIS | -73 | 1664 | 263
 | UE2 | AAU | -58 | 1702 | 264
 | UE1 | AAU(RIS OFF) | -96 | 40.8 | 17.2
 | UE2 | AAU | -58 | 1364 | 193

## Slide 21: Case #10: RIS-based Phased Array Antennas
The new phased array antenna multi-stream test environment is shown in Figure 28. The millimeter-wave phased array antenna based on RIS architecture is assembled and integrated by two RIS arrays, with a working bandwidth of 200MHz, a beam configuration period of 20ms, a frame structure configured as DDDSU, and a S configuration of 10:2:2, which can be configured with two analog beamforming channels at the same time.
Terminal | SS-RSRP(dBm) | DL-Tput(Mbps) | Beam ID
UE1 | -69.26 | 530.32 | 16
UE2 | -70.19 | 519.64 | 0
The new phased array antenna, integrating two RIS arrays, can simultaneously serve two users on the same frequency.
At 200 MHz bandwidth, the user downlink rate is about 500 Mbps.

## Slide 22: Case #11: Refractive RIS with Multi-Beam
In the dark chamber transmissive RIS multibeam test, the RIS array has 256 elements, a center frequency of 3.5 GHz, and 200 MHz bandwidth. Beam scanning covers ±60°. Multi-angle beams are generated via space-time coding, and beam patterns are measured using a vector network analyzer.
(b) Pattern of beamform ±20° (c)Pattern of beamform -20°/40° (d)Pattern of beamform ±30°

## Slide 23: Case #12: Indoor ISAC
The figure shows the test environment for millimeter-wave synaesthesia localization based on RIS. The sensing and positioning target continuously transmits a 27 GHz monotone carrier signal through the millimeter-wave front-end. Two distributed RIS units modulate the incident signal via the PXIe module and reflect it to two receiving antennas, enabling wave arrival angle estimation and positioning functions.
To evaluate the localization performance of the prototype system, the square test area was divided into 72 equal points, with synaesthesia localization targets placed at each point. Results show positioning errors under 10.2 cm for all points, with 43.06% within 5 cm and 97.22% within 10 cm, demonstrating that the RIS synaesthesia positioning prototype achieves centimeter-level accuracy.