## Slide 1: Views on Rel-20 5G-A AI/ML for Air Interface Enhancements
NTT DOCOMO, INC.
RP-251411
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
Agenda item: 15.1.1
Document for: Discussion

## Slide 2: Background
In RAN Plenary #107, the guidelines for 5G-Advanced in Rel-20 are endorsed in RP-250812.
  For Enhancements on AI/ML Air-interface
    [2] TUs in RAN1 and [2] TUs in RAN2 may be considered.

## Slide 3: Overview
Background
  In Rel-19, AI/ML-based CSI compression is studied without normative work.
    Case 2 and Case 3 of CSI compression with temporal domain aspects are prioritized in Rel-19 study.
    From the RAN1 perspective, the feasibility of three inter-vendor collaboration options has been verified.
  In Rel-19, RAN WGs had no consensus on feasibility of OTA solutions and asked SA WGs to confirm the feasibility of non-OTA solutions for NW-side sharing dataset/model parameters to UE-side training entity.
    No conclusion has been received from SA WGs so far.
  Rel-20 UE side data collection SA2 SID has been approved in SA (SP-250413).
Our views on Rel-20 5G-A AI/ML for air interface
  New AI/ML use cases should be included in 6G study.
  AI/ML-based CSI compression can be potentially considered as a Rel-20 work item, if allocated TUs for all corresponding RAN WGs.
  SA WGs should be involved especially on the non-OTA solution for NW-side sharing dataset/model parameter to UE-side training entity.

## Slide 4: AI/ML-based CSI Compression
Background
  For CSI compression with temporal domain aspects,
    Case 3 achieves the performance gain with reduced overhead due to less uplink report occasions, which brings practical benefits to commercial NWs.
    Case 2 achieves the performance gain but requires additional signallings for the alignment of the CSI information between NW and UE.
  For inter-vendor collaboration options, three options are feasible from RAN1 perspective.
    For Option 1/3a-1, the remaining feasibility issues will be solved if RAN4 specifies reference models.
    For Option 4-1/3a-1, feasibility of OTA and non-OTA solutions for NW-side sharing dataset/model parameters to UE-side training entity has not been confirmed from RAN and SA WGs. Besides, the user privacy and user consent compliance issues were not fully addressed in the Rel-19 study.
Our views on the normative work of AI/ML CSI compression
  There is little urgent commercial need for supporting AI/ML-based CSI compression, considering the remaining feasibility and user privacy/user consent compliance issues.
  The normative work of AI/ML-based CSI compression can provide a good reference for the 6G AI studies especially the use cases requiring two-sided model.
  If AI/ML-based CSI compression is specified in Rel-20, we have the following general views on the scope,
    Specification on the LCM procedure, inference, data collection, and performance monitoring for Case 3 considering its practical benefits.
    Specification on the inter-vendor collaboration Option 1 and Option 3a-1 with less concerns on the feasibility and user privacy.
      RAN should send an LS to invite SA WGs (SA2 and/or SA5) to specify the non-OTA mechanism(s) for model parameters/datasets/additional information exchange between the NW side and UE side training entities.

## Slide 5: Scope of the potential WID
If the AI/ML CSI compression is supported in Rel-20, we suggest providing the specification support for the following aspects,
  AI/ML general framework for two-sided models based on inter-vendor collaboration Direction A-Option 3a-1 (with and without target CSI), encompassing [RAN2/RAN1, and WGs beyond RAN]
    Necessary signalling/mechanism(s) to facilitate LCM operations of the two-sided model, including the model pairing procedure with ID and applicability reporting, inference, performance monitoring, and data collection (NW and UE side).
    Necessary signalling/mechanism(s) to facilitate the non-OTA exchange of model parameters/datasets/additional information.
      Note: Coordination with SA/SA WGs is required as this item is related to their work.
  AI/ML CSI compression with temporal domain Case 0 & Case 3, encompassing [RAN1/RAN2]
    Inference aspects including target CSI type, measurement and report configuration, CQI / RI determination, payload determination, quantization configuration/codebook, UCI mapping, CSI processing criteria and timeline, and priority rules for CSI reports.
    Formats and contents of model parameters/datasets/additional information exchange.
      Note: The specified model structures for model parameter exchange are equivalent to the structure of the reference models defined/specified by RAN4 (as described in the following aspects).
    Target CSI format for the NW and UE side data collection.
    Performance monitoring, including at least the necessary enhancements of UE reports for NW side performance monitoring.
  Core requirements for the above AI/ML CSI compression and inter-vendor collaboration aspects. [RAN4]
    Specify necessary RAN4 core requirements for the above aspects. This includes the test setup and methodology for AI/ML CSI compression and inter-vendor collaboration, where reference models (incl. model structures and parameters) will be defined/specified to verify the satisfaction of the requirements (i.e., Direction C-Option 1).
    Specify necessary RAN4 core requirements for LCM procedures, including performance monitoring.

## Slide 6: Proposed way forward
Background
  TU in chair’s guidance [2] may not be enough for all WID items in the previous slide
Our views
  Some options can be considered to fit the allocated TU if it is not enough
    Opt. 1
      Keep the current scope with increased TU to 2.5
    Opt. 2
      Drop 5G-A AIML in Rel-20
    Opt. 3
      Drop some scope (e.g. Case 3) to fit into the allocated TU