## Slide 1: Views on Rel-20 Ambient IoT
RP-251519
3GPP TSG RAN #108
Prague, Czech Republic, June 09-13, 2025
Agenda Item: 15.1.3
CEWiT, Tejas Networks, IIT Kanpur,
IIT Madras

## Slide 2
Background
Scope of Rel. 19 A-IoT was limited due to time constraints
  Studied only limited set of use cases/scenarios /device types in TR 38.848 [1]
    Indoor and O2I scenarios
    Topologies D1T1 and D2T2
    Inventory and command use cases
    Device Type 1/2a/2b
  WI further down selected the scope [2] from study outcome in TR 38.769 [3]
    Included only indoor scenario and topology D1T1
    Included only Device Type 1
    Assumed Device unavailability direction 1
High level Scope of A-IoT in Rel. 20 was discussed in RAN#107 [4], and it includes
  Device 1 in D2T2
  Device 2b in D1T1 and D2T2
  Study on A-IoT for outdoor scenarios
Discussion on details of the scope and support for additional scenarios are pending for RAN#108

## Slide 3
D2T2 Scenario
D2T2 offers distinct coverage benefits for certain scenarios
  Enables A-IoT operation when gNB is outdoor
  Enables reuse of the existing infrastructure
  Mobility of reader/intermediate UE can overcome the coverage limitation (especially in case of Device 1)
RRC based A-IoT architecture [3] must be supported for D2T2
  A-IoT upper layer information is explicitly forwarded via UE reader’s NR Uu RRC message.
  gNB can do a better job in selection and controlling of UE reader compared to CORE network
  D1T1 scenario in Rel. 19 is based on control plane option

## Slide 4
D2T2 Scenario
Intermediate UE must be under the control of serving gNB
  Assigning resources for Ambient IoT reader operation
  Multiplexing NR and Ambient IoT operations
L1 and higher-layer based control signaling
  Provides higher flexibility and better resource utilization
  Inline with the configurations in NR
  Mobility management/handover procedures
Design of D2T2 should ensure
  co-existence between D1T1 and D2T2
  smooth and transparent transition across D1T1 and D2T2 for devices

## Slide 5
D2T2 Scenario
Spectrum for D2T2 should be same as D1T1 scenario
  R2D in DL spectrum and D2R in UL spectrum
    UE to UE CLI can be handled by
      Spectrum gap between NR and A-IoT spectrums
      gNB configuration
  Scenario D1T1 or D2T2 should be transparent to device
  Simplify device design/implementation
    To avoid device scanning for R2D in both DL and UL spectrum if R2D spectrum is different across the topologies (D1T1 and D2T2)
    To avoid device generating signals in both DL and UL spectrum if D2R spectrum is different across the topologies (D1T1 and D2T2)

## Slide 6
Scope for Device 2b
Rel 19 framework should be a baseline.
Additional beneficial features
  Enhancement to multiple access techniques for R2D and D2R
  Enhancement for repetition
  Enhancement to scheduling/monitoring
    L1-layer control
    Defining monitoring window
    Extension of the operation time/Sleep state
    For sensor based use cases/Do-A traffic

## Slide 7
Ambient IoT outdoor use cases
Study A-IoT for deployment scenario D4 (device outdoor, BS outdoor)
Support Topology 1 and Topology 2 (with NCR as intermediate node)
  NCR is already specified in Rel 18 as a coverage extension feature
  Enhanced capability compared to UE
Enhancements to device architecture and procedure to improve coverage for outdoor use cases
Enhancements to extend device operational time
Enhancements to support the device mobility
02-06-2025

## Slide 8
Other Aspects
Support Device unavailability direction 2
  Optimum use of device capability
    Support for sleep state for devices
    Extension of the operation time
  Low latency and efficient resource utilization
    Discontinuous operation based on device availability/energy status
Support Do-A Traffic
  Sensor based application
  Device initiated A-IoT operation

## Slide 9
Leftovers from Rel. 19
Rel-19 assumes
  no Parallel service requests by the same reader
  no multi reader scenarios, overlap among A-IoT carriers/coverage regions
Above assumptions may not hold true in Rel. 20, due to
  Reader mobility in D2T2
  New/Additional use cases and services supported
Rel 20 should consider following enhancements
  Parallel service requests by the same reader,
  Multi reader scenarios
  Different services under the same request
  Co-existence between Rel. 19 and Rel. 20 scenarios
02-06-2025

## Slide 10
Proposals
  Specify D2T2 scenario for A-IoT with following included under the scope
    For Device 1 and 2b
    Rel. 19 design should be the baseline
    Smooth and transparent transition across D1T1 and D2T2 for devices
    Spectrum for D2T2 should be same as D1T1 scenario
    R2D in DL spectrum and D2R in UL spectrum
    RRC based A-IoT architecture
    L1 and higher-layer based control signaling for intermediate UE
      Resource configuration for A-IoT
      Multiplexing of A-IoT/NR operation
    Mobility management/handover procedures/behaviors for devices
    Co-existence with Rel. 19 A-IoT

## Slide 11
Proposals
Support following additional features for Device 2b
  Enhancement to multiple access techniques for R2D and D2R
  Enhancement to scheduling/monitoring
    L1-layer control
    Defining monitoring window
  Device unavailability direction 2
    Enhancements for device sleep state/extension of the operation time
  Enhancements for Do-A traffic/ sensor use cases
    Device initiated A-IoT round
  Enhancements for repetition
  Support A-IoT in outdoor scenario
  Deployment scenario D4 (device outdoor, BS outdoor)
  Support Topology 1 and Topology 2 (with NCR as intermediate node)
  Enhancements to device architecture/ procedures/behaviors
    To improve coverage
    To extend device operational time
    To support device mobility
02-06-2025

## Slide 12
Proposals
Support following for A-IoT in Rel. 20
    Device unavailability direction 2
      Support for sleep state for devices
      Extension of the operation time
      Discontinuous operation based on device availability/energy status
    Do-A Traffic
      Device initiated A-IoT operation
  Support following leftovers from Rel. 19
    Parallel service requests by the same reader,
    Multi reader scenarios
    Different services under the same request
    Co-existence between Rel. 19 and Rel. 20 scenarios

## Slide 13
References
[1] 3GPP TR 38.848, “Study on solutions for Ambient IoT (Internet of Things) in RAN”.
[2] RP-243326. “New Work Item: Solutions for Ambient IoT (Internet of Things) in NR”, RAN# 106, Madrid, Spain, December 9-12, 2024.
[3] 3GPP TR 38.769, “Study on solutions for Ambient IoT (Internet of Things) in NR”.
[4] RP-250802, “Moderator's summary for RAN1 led Rel-20 topics”, RAN# 107, Incheon, Korea, March 12-14, 2025.

## Slide 14: Thank You