## Slide 1: Network energy saving enhancements for 5G-Advanced in Rel-20
3GPP TSG RAN#108 RP-251521
Prague, Czech Republic, June 9th-13th, 2025
Agenda Item: 15.1.6
Source: CEWiT

## Slide 2
Background
Energy consumption accounts for a substantial share of operators’ OPEX, highlighting the importance of network energy-saving techniques.
  The solutions developed in Rel-18/19, however, are limited in scope and only address a subset of deployment situations. Consequently, there is a strong need to continue advancing network energy-saving features for 5G-Advanced in Rel-20.
  These ongoing enhancements will improve the prospects for widespread and effective deployment of NES techniques within the current 5G timeframe.
The contribution provides a way forward on network energy saving enhancements for 5G-Advanced in Rel-20.
In Rel-18, Cell DTX/DRX is specified, which is beneficial for both network and UE from energy saving perspective.
    However, network would face constraints to enable cell DTX/DRX in practical deployment, if the traffic information of a UE is not available at the network side.
    Further, Rel-18 DTX/DRX target specific signals (PDSCH, selected PDCCH) but excludes common signals like SSB, forcing gNBs to transmit them continuously.
      This limits sleep intervals, causes frequent active-sleep state transitions, and limits NES gains.
Rel. 19 introduces OD-SIB1 transmission in SCells triggered by UL WUS from UEs, alongside OD-SSB limited to NCD-SSB for connected-mode operations like carrier aggregation.
    The continued periodic transmission of CD-SSBs at intervals like 20 ms restricting deeper sleep states. This limits maximum gains compared to scenarios allowing full SSB shutdown during low-traffic periods.
Always on SSB with 20ms periodicity prevents cells from going to deeper sleep modes, and thus leads to high energy consumption, especially for the case of low load.
    SSB periodicity extension can achieve very promising energy saving gain according to the Rel-18 study as shown in TR 38.864.

## Slide 3
© CEWiT 2022
<number>
  Motivation
  In Rel-18 and 19, SSB less Scell and OD-SSB for SCell is specified, beneficial for the network energy saving in multi cell scenarios.
  However, in a network with a single NR carrier, neither SSB-less nor on-demand SSB can be used, leading to always-on SSB transmission and high energy consumption.
  According to study outcome for NES in Rel-18 TR 38.864, SSB Periodicity extension can achieve promising energy savings of 0.9% to 84.8% by adapting the periodicity of SSB from 20ms to 1280ms, with the assumption that UEs are not active during initial access. Periodicity extension to 160ms can lead to a further 73% energy saving compared to the baseline
  Energy saving can be increased to a significant level if the extension of assumed SSB periodicity is supported.
  Potential Enhancements
    Specify SSB Periodicity extension beyond 20ms assumed by UE During Initial Access
  UE Impact and Specification Impact
  SSB periodicity extension is applicable to cells in greenfield (new frequency band deployment) or where legacy UE constraints are minimal.
  Legacy UEs can latch to frequency band supporting 20ms SSB periodicity and still work with extended SSB periodicity beyond 20ms to the additional bands
  Impact on initial cell selection and RRM (Radio Resource Management) can be minimized by proper design of sync raster or with the help of frequency bands supporting 20ms SSB periodicity.
  The work has specification impacts in RAN1/RAN2/RAN4 for supporting extended SSB periodicity.
Proposal 1: Specify an extended SSB periodicity beyond 20ms assumed by UE during initial access [RAN1, RAN4, RAN2]
  Specify procedures and signaling for SSB periodicity extension [RAN1, RAN2]
  Specify RRM requirements based on extended SSB periodicity [RAN4]
SSB Periodicity Extension

## Slide 4
© CEWiT 2022
<number>
On-demand SSB for IDLE/INACTIVE UE
Motivation
  Rel. 19 supports on-demand SIB1 in Scell based on UL WUS from UE
  Rel. 19 on-demand SSB is applicable only for NCD SSB and UEs in connected mode
  In both cases, the gNB still need to transmit CD-SSBs periodically (e.g. with 20 ms) for synchronization
    Reduces sleep time of gNB and restricts energy saving gains
  Turning off SSB transmissions allows for deeper sleep at the gNB and greater NES gain
On-demand SSB for Idle/Inactive UE should be supported in Rel. 20
  gNB transmitting SSB based on WUS
  Provide significant energy saving gains as observed in TR 38.864, as shown below.
    For UEs in RRC_IDLE/INACTIVE without C-DRX and no DL transmission including SSB before WUS reception, NES gains reach 83.7% (52.5%) with Cat-1 (Cat-2) BS power model at zero or low load.
  Considered in Rel. 19 and dropped due to time constraints and lack of consensus
On-demand SSB for multi cell scenarios:
  Extend the On-demand SIB1 framework in Rel. 19 to SSB
  NES cell transmitting SSB on request from UE
    UE transmit UL-WUS to request SSB
    UE can transmit a UL-WUS to NES Cell or Anchor Cell
  The UE receives WUS configuration from Anchor Cell.
  gNB monitors for WUS on NES Cell based on the configuration.
Impact on standards and legacy UE is minimized by
  Legacy UE can use SSB of anchor cell for initial access
  In case NES cells not serving legacy UEs
  Adaptation in Scells similar to OD-SIB1 mechanism as the baseline.
Proposal 2: Support to specify On-demand SSB for IDLE/INACTIVE UE
  Specify procedures and signaling method(s) for On-demand SSB in multi cell scenarios [RAN1/2]
  UE obtains UL WUS configuration from Anchor Cell, UE transmits UL WUS on Anchor Cell, UE receives on-demand SSB from NES Cell (Scell)
Fig. 1: On-demand SSB in multi cell scenario

## Slide 5
© CEWiT 2022
<number>
  Motivation
  In Rel-18, Cell DTX/DRX is specified, beneficial for both the network and UE in terms of energy saving.
  The network would typically face constraints in enabling cell DTX/DRX in practical deployments if UE traffic info is unavailable to avoid adverse impact on user experience.
  UE is aware of its traffic information and can determine the optimal cell DTX/DRX pattern, providing better energy savings and user experience.
  Potential Enhancements
  Specify UE-recommended cell DTX/DRX via UAI (UE Assistance Information) [RAN1/2]
  Candidate DTX/DRX patterns can be same as those developed in Rel-18.
  Enable significant energy saving gain for both network and UE for cell low/light/medium load cases, as more time for sleep is available
Proposal 3: Specify UE recommended cell DTX/DRX via UAI (UE Assistance Information)
  Specify signaling & procedures for UE assistance.
  The candidate cell DTX/DRX configurations to be reported by UE can be same as the cell DTX/DRX configurations developed in Rel-18
Enhancements for DTX/DRX Adaptation (Connected UEs)

## Slide 6
© CEWiT 2022
<number>
  Motivation
  Rel-18 DTX/DRX is limited to specific signals, such as PDSCH and a subset of PDCCH.
  Rel-18 DTX/DRX is not applicable to common signals such as SSB
    Transmissions of common signals reduces sleep time of gNB
    Results in frequent switching between active and sleep states
    Reduces NES gains significantly
    Sparser SSB transmission occasions, when longer periods are enabled, impacts measurements and performance at UE
  Rel. 19 considered adaptation of cell specific signals under certain scenarios (E.g., multi cell scenario, adaptation of NCD SSBs, etc.)
  Extending Cell DTX/DRX operation to common signals in multi cell scenario should be supported in Rel.20
  A multi cell scenarios with Pcell (Anchor cell) and SCells (NES cells) can be considered.
  Cell DTX/DRX pattern can be enabled for common signals of SCells (NES cells)
  gNB transmit SSB only during active period of the cell DTX/DRX pattern and no transmissions during inactive period
  Impact on legacy UEs and specifications is minimized
    legacy UEs can be served by the SSBs in PCell (Anchor cell)
    Adaptation in Scell (NES cell) is not serving legacy UEs
Proposal 4: Extend Rel. 18 cell DTX/DRX mechanism to common signals in multi cell scenarios
Specify procedures and signaling methods for extending cell DTX/DRX operation to common signals in Scells
  Transmission of SSBs with certain periodicities within active period of cell DTX/DRX pattern and no transmission in non active period
Enhancements for DTX/DRX Adaptation (Idle/inactive UEs)

## Slide 7
Proposal 1: Support a 5G-A Rel-20 item on enhancements of network energy saving.
Proposal 2: Take the following as the candidate enhancements for further discussion:
    SSB periodicity extension
    UE triggered On-demand SSB for UEs in idle/inactive mode in Scells.
    Cell DTX/DRX enhancements for RRC CONNECTED UEs, with UE recommended Cell DTX/DRX via UAI (UE Assistance Information)
    Cell DTX/DRX enhancements for RRC IDLE/INACTIVE UEs in Scells.
Proposals