## Slide 1
Integrated Sensing and Communication: Scope in Rel.20
3GPP TSG RAN Meeting #108 RP-251523
Prague, CZ, June 2024

## Slide 2
30/05/2025
© CEWiT 2022
2
Motivation
ISAC SI proposed in Rel. 19
  Ensure improvement in safety and quality of life (civilian applications)
  UAV tracking and detection (Commercial and military applications)
Efficient resource utilization by incorporating sensing along with communication
Sensing and communication can aid each other and improve performance of both the systems
Six sensing modes proposed
  BS-BS (mono static and bi-static), BS-UE ( bi-static), UE-UE (mono static and bi-static)
Notes: 2

## Slide 3
© CEWiT 2022
3
Rel. 19 highlights
Object detection and tracking use cases are prioritized
  Certain deployment scenarios chosen
Channel modelling studied
  Target channel and background channel considered
  Channel between Tx-target and target-Rx considered
  Doppler effects of transmitter, receiver and targets considered
  Cross polarization matrix of target considered
  RCS modelling done
  Modeling of environmental objects considered
30/05/2025
Notes: 3

## Slide 4
Further study
Study needs to be performed based on the proposed evaluation methodology
  feasibility of different scenarios
  suitable sensing modes
  sensing performance in different frequency bands (FR1,FR2, FR3)
KPIs suitable for sensing need to be defined
Since certain modes/use cases involve full duplexing/SI cancellation capability, study to be restricted to gNB mono-static sensing
Among the proposed deployment scenarios, UAV tracking is more feasible owing to the presence of LoS path. Therefore, UAV use cases can be prioritized for study.
© CEWiT 2022
4
30/05/2025

## Slide 5
Additional signaling could be required when sensing is incorporated with communication
Existing call flow from CORE to RAN will undergo a change due to inclusion of sensing. Therefore, call flow enhancements should be studied.
Certain symbols/slots to be allocated for sensing and may not be available for communications. Therefore, handling symbol unavailability needs to be studied
Further study
© CEWiT 2022
5
30/05/2025

## Slide 6
Rel. 20: 5G Advanced Proposals
Definition of KPIs for sensing and study on feasibility to be done on
  different scenarios
  suitable sensing modes
  sensing performance in different frequency bands (FR1,FR2, FR3)
Restrict the study to gNB mono-static sensing
More emphasis on study on UAV use cases
Support study on
  Signaling enhancements
  Call flow modifications
  Handling slots/symbols unavailability for communications
© CEWiT 2022
6
30/05/2025

## Slide 7
Thank you