## Slide 1: Motivation for new study on VSAT testability
Eutelsat Group, Intelsat, Thales, JSAT, Airbus, Gilat, Rohde & Schwarz, Viavi Solutions, Sharp, Hispasat, ESA, LG electronics, MediaTek Inc., Lockheed Martin Corporation, SES, Gatehouse Satcom, Toyota
3GPP TSG-RAN Meeting # 108 RP-251526
Prague, Czech Republic, June 9-13, 2025 Agenda Item 15.4.2

## Slide 2: Background
Summary
This paper describes the urgent need to start work on VSAT testability, and proposes the approval of a revised or new SID to address the VSAT testability issues that have arisen from the introduction of VSAT core requirements in Rel-18 for Ka band and the ongoing working Rel-19 to specify VSAT for Ku bands.

## Slide 3: Background
It is the default procedure once RAN approves a WI with UE core requirements, that after RAN4 completes the core requirements, RAN5 automatically follows up with a WI on conformance testing without further discussion about priorities. This normal flow of approving conformance test WIs has only been interrupted when the core requirements have involved the development of new test methods - which have typically been related to radiated testing. In these cases, RAN4 has started feasibility studies to develop the test methods before RAN5 takes over and follows up with the detailed test system design and resulting conformance test cases. This precedent has been documented in changes to the terms of reference of RAN4 [1]. In the NR era, RAN4 started the testability FS process in 2016 to handle FR2 handsets, and this work is now on its third cycle of radiated test method development with the ongoing study FS_NR_FR2_OTA_Ph3.

## Slide 4: Background
When RAN approved the Rel-18 WI NR_NTN_enh for VSATs operating above 10 GHz there was an implicit and obvious consequence on test methods since the size of VSATs is much larger than the size of the FR2 handsets used to develop the current FR2 NR radiated test systems whose quiet zone was only 15 cm (now 40 cm). Also, the FR2-NTN frequency range has a lower limit of 17.3 GHz, well below the 24.25 GHz of existing approved FR2 radiated test methods. When RAN approved the WI Introduction of Ku bands for NR NTN in June 2024, the lower frequency dropped further to 10.7 GHz.
In addition to the frequency range and VSAT device size issues, the introduction of Ka band added the issue of polarization. Current radiated test systems are all based on cross polarized antennas, but Ka band (and Ku band) operates with circular polarization.

## Slide 5: Background
Unfortunately, there is no obvious way to convert existing test systems to use circular polarization without reverting to using a vector network analyzer approach which would mean the loss of the L3 signalling connectivity normally provided by a base station emulator, which lacks the phase control to generate stable circular polarization.
The urgent need to address the large and growing need for VSAT testability is further evidenced by a Feb 2025 industry press release [2] which announced the first successful connection between a Ku band VSAT using an NR air interface and a LEO constellation. This indicates the demand for 3GPP-based NTN standards since current commercial developments are actually ahead of 3GPP rather than being a couple of years behind the standards.

## Slide 6: Motivation
There has now been a one-year delay since RAN was first requested to address the VSAT testability issues from Rel-18 [3]. This has prevented RAN5 from starting the usual process of developing conformance test cases required to complete the 3GPP specifications. The need has grown during Rel-19 with the new Ku bands.
The key current and future VSAT testability issues are:
VSAT device sizes exceed by far what is currently testable in existing 3GPP FR2 test systems
The introduction of Ka band with its 17.3 GHz lower limit falls well below the range of existing FR2 test systems of 24.25 GHz.
The introduction of Ku band (10.7 and 14.5 GHz) further challenges the operating range of existing test methods.
The need to support circular polarization adds a significant challenge to existing test systems which may require regressing to using non-signalling methods.

## Slide 7: Proposals
Proposal: Start a new OTA Phase 4 SI in Rel-20 including VSAT testability
The objectives for the study are in the following slide taken from the revised SID in RP-250640 [4]

## Slide 8: SID Objectives (from RP-250640)
Investigate the applicability of current 3GPP test methods established in TR 38.810 and TR 38.871 for UE testing for the following example VSAT device types (from 38.101-5 v18.5.0 Table 9.2.1.0-1:
Mobile VSAT UE type 4 and 5 (mechanical and electronic steering antenna)
Investigate how to support both linear and circular polarization measurements in uplink and downlink
Confirm that an L3 signalling approach to VSAT testing is to be used
Investigate the required size of the quiet zone based on industry needs. A preliminary assumption for quiet zone is 60 cm, larger volumes will be needed for some antenna types
Test methodologies are studied for the following frequency ranges:
  Ka bands (i.e., existing bands n510, n511, n512)
  Ku bands with DL from 10.7 to 12.75 GHz and UL from 13.75 – 14.5 GHz)
Study ETSI Harmonised Standards for access to radio spectrum and any other applicable specifications in other regions

## Slide 9: References
[1] RP-210786 Terms of Reference (ToR) for 3GPP TSG RAN WG4 (RAN4), RAN#91-e, Mar 2021
[2] https://www.eutelsat.com/en/news/press.html#/pressreleases/eutelsat-mediatek-and-airbus-announce-worlds-first-5g-non-terrestrial-network-connection-leveraging-oneweb-leo-satellites-3371519
[3] RP-241171 New SID on VSAT test methods (Eutelsat Group, RAN #104 Shanghai June 2024)
[4] RP-250640 Revised SID to add VSAT testability to NR FR2 OTA (Over the Air) testing Phase 3 (Eutelsat Group, RAN #107 Incheon March 2025)