## Slide 1
Huawei, HiSilicon
Views on Rel-20 NR NTN scope
3GPP TSG RAN#108 RP-251618
Prague, Czech, June 09-13 2025
Agenda Item: 15.1.5

## Slide 2
Background: RAN#107 Conclusion (in RP-250812)
Conclusion for GNSS resilient operation
  Study Item with checkpoint to determine whether we have normative work and the scope based on results of study item phase.
  Study should consider Rel-16 as baseline for discussion. Study should focus on NR NTN and be backward compatible with legacy UEs. Aim to minimize physical layer procedures impact to 5GA and avoid physical layer channel/signal changes.
  Objective to be narrowed down for RAN#108
  No additional NR NTN enhancements with RAN1 impact can be considered at this point given limited 5GA TUs

## Slide 3
GNSS resilient operation: benefit and applicable Scenario
Existing mechanism
Rel-17/18/19 NR NTN assumes uplink timing and frequency compensation at UE using ephemeris and UE GNSS location
Uplink transmissions, including PRACH, assume UE acquires GNSS location with an accuracy of 50 meters
Motivation for GNSS resilient operation
Frequent GNSS acquisition needed for location accuracy of 50meters ➔ high UE power consumption,
GNSS signal may be temporarily unavailable,
If requirement on timing and frequency error of uplink transmissions, including PRACH, is relaxed, UE power consumption can be greatly reduced and dependent on GNSS availability can be relaxed
Positioning accuracy requirement (m) | Velocity (km/h) | Needed GNSS measurement periodicity (s) | Energy consumption per day (mAh)*
50 | 180 | 1 | 480
 | 30 | 6 | 80
2500 | 180 | 50 | 9.6
 | 30 | 300 | 1.6
*Assume one GNSS measurement per second leads to 20 mAh energy consumption per hour
For idle mode:
Preamble C2 can afford at least 2.5km location error (covered by ¼ CP).
UE location error relaxed from 50m to 2.5km can save 98% power without enhancement for preamble.
 |  | GNSS measurement periodicity (s) |  |  | 
 | UE velocity (km/h) | 1 | 5 | 20 | No GNSS
Required # of TA adjustments | 30 | 0 | 187 | 835 | 6728
 | 180 | 0 | 187 | 836 | 6764
Required # of CFO adjustments | 30 | 0 | 0 | 100 | 888
 | 180 | 0 | 0 | 102 | 892
For RRC connected mode:
When closed-loop time and frequency correction is used to guarantee certain timing and frequency accuracy, requirements on GNSS measurement can be relaxed.
The signaling overhead is accumulated from 30° to 150° elevation for LEO600, the duration is around 247s. Assume tolerable timing error of 29*64Tc and tolerable frequency error of 200 Hz

## Slide 4
GNSS-resilient operation for NR NTN
Proposal 1: RAN#108 to approve a study item for NR NTN GNSS resilient operation, and RAN#112 to check and determine whether we have normative work and the scope based on results of study item phase.
Proposal 2: RAN1 objectives include:
Study the performance of PUSCH and PRACH preamble with relaxed GNSS measurement.
Study closed-loop frequency adjustment during initial access and RRC connected mode
Study enhancement in timing adjustment, e.g. negative TAC indication in Msg2.
Study closed-loop signaling overhead saving, if needed.
Note: the study should consider coexistence of new UEs and legacy UEs in a same cell
Proposal 3: RAN2 objectives include:
Study signaling design of closed-loop frequency correction as well as its timer if indicated by MAC CE.
Study impact of GNSS relaxation on mobility.
Proposal 4: RAN4 objectives include:
Study relaxation on the requirements for uplink transmissions, GNSS measurement, and SMTC.