## Slide 1
Huawei, HiSilicon
Views on Rel-20 IoT NTN scope
3GPP TSG RAN#108 RP-251619 Prague, Czech Republic, June 09-13, 2025
Agenda Item: 15.2.2

## Slide 2
Justification: IMS Voice call over GEO in Rel-20
Motivation:
GEO satellite provides wide coverage. Voice service over GEO is important for the scenarios where there is no TN coverage or TN is temporarily unavailable due to e.g. natural disasters.
Two new SIDs and one new WID were approved for Rel-20 in SA WGs (SA2: S2-2502778; SA4: S4-250384; SA1: S1-244772). One objective is to support IMS voice call over GEO, with the following requirements captured in TR 22.887 as baseline:
RANP#107 conclusion:
Scenario | UE type | Transmission data rate |  | Call setup time NOTE 1
 |  | UL | DL | 
IMS voice call using GEO | Handheld | [1-3] kbit/s | [1-3] kbit/s | [4-30] s NOTE 2
NOTE 1: call set up time refers to [4]; NOTE 2: the lower bound of 4s originated from the experience in terrestrial VoNR/VoLTE, while the upper bound of the 30s is derived based on the user’s patience suggestions (30s) in [13]; |  |  |  | 
Only the following objective will be considered as baseline for IoT NTN WI: Voice over NB-IoT-NTN via GEO Study phase for 1 or 2 Quarters to downselect between CP or UP. Checkpoint by RAN#1xy (TBD) Work on detailed objectives for RAN#108

## Slide 3
IMS Voice call over GEO: Design target
1ms
Design for traditional TN VoIP services:
Codec rate to ensure quality, e.g. a speech frame of 244 bits per 20ms is assumed for AMR-NB 12.2 kbps.
Packet Delay Budget for conversational voice in VoLTE is 100 ms.
20ms
Codec
IP+UDP+RTP
PDCP+RLC+MAC
20ms
payload
payload
Header
Header
Header
VoIP traffic for TN
Constraints for NB-IoT NTN to support voice call over GEO:
According to link budget analysis in TR 36.763, existing VoIP Codec is unlikely to be supported by NB-IoT voice call over GEO  SA4 SI for ultra low bitrate speech codec includes study of mouth-to-ear delay, bit rates, frame length, dis-continuous transmission etc.
Propagation delay of 270 ms makes packet delay budget requirement of 100 ms (for TN VoIP services) no longer relevant  new design target needed
Proposal 1: Design target for TN VoIP services can not apply directly to NB-IoT voice call over GEO, and new design target for RAN need to be defined for NB-IoT NTN voice call over GEO in coordination with SA WGs.

## Slide 4
IMS Voice call over GEO in Rel-20: potential RAN enhancements
Link budget of IoT NTN with different UE RF parameters
For GEO, the limited link budget may affect the user experience of voice service. According to the link budget analysis in the left table, the result of CNR is largely impacted by UE RF parameters and reference scenarios, such as UE Tx Power, UE Antenna Gain, UE antenna configuration, Elevation Angle.
Proposal 2: According to the link budget analysis, the service performance is largely impacted by UE RF parameters and reference scenarios. For a meaningful RAN design to support IoT NTN voice over GEO,
  Baseline UE RF parameters e.g. UE Tx Power, UE Antenna Gain, UE antenna configuration, need to be decided, and enhanced if needed.
  Reference scenarios, e.g. Elevation Angle, need to be decided.
Parameters | Value |  |  |  |  | 
Target elevation angle | 2.3°[1] |  |  |  | 20°[2] | 
Freq. band /GHz | 2 |  | 2 |  | 2 | 
Channel BW /kHz | 180, 15/3.75 |  | 180, 15/3.75 |  | 180, 15/3.75 | 
UE Tx Power /dBm | 31 |  | 31 |  | 31 | 
NF /dB | 7 |  | 7 |  | 7 | 
Antenna Gain /dBi | -5.5 |  | 0 |  | 0 | 
UE Antenna config. | 1Tx, 1Rx |  | 1Tx, 1Rx |  | 1Tx, 2Rx(3dB) | 
EIRP /dBW | 51.55(DL)/-4.5(UL) |  | 51.55(DL)/1(UL) |  | 51.55(DL)/1(UL) | 
G/T / dB/K | -37.12(DL)/19(UL) |  | -31.62(DL)/19(UL) |  | -31.62(DL)/19(UL) | 
/dB | 190.81 |  | 190.81 |  | 190.41 | 
/dB | 0.2 |  | 0.2 |  | 0.2 | 
/dB | 3 |  | 3 |  | 3 | 
/dB | 2.2 |  | 2.2 |  | 0 | 
/dB | 0(DL)/3(UL) |  | 0(DL)/3(UL) |  | 0(DL)/3(UL) | 
/dB | 3 |  | 3 |  | 3 | 
B(dBHZ) | 52.55(DL)/41.76(15k UL)35.74(3.75k UL) |  |  |  |  | 
K(dBw/K/Hz) | -228.6 |  |  |  |  | 
CNR /dB | DL | UL | DL | UL | DL | UL
 | -8.8 | -0.9/5.1 | -3.3 | 4.6/10.6 | 2.3 | 7.2/13.2
Parameters | Value |  |  |  |  | 
Target elevation angle | 2.3°[1] |  |  |  | 20°[2] | 
Freq. band /GHz | 2 |  | 2 |  | 2 | 
Channel BW /kHz | 180, 15/3.75 |  | 180, 15/3.75 |  | 180, 15/3.75 | 
UE Tx Power /dBm | 31 |  | 31 |  | 31 | 
NF /dB | 7 |  | 7 |  | 7 | 
Antenna Gain /dBi | -5.5 |  | 0 |  | 0 | 
UE Antenna config. | 1Tx, 1Rx |  | 1Tx, 1Rx |  | 1Tx, 2Rx(3dB) | 
EIRP /dBW | 51.55(DL)/-4.5(UL) |  | 51.55(DL)/1(UL) |  | 51.55(DL)/1(UL) | 
G/T / dB/K | -37.12(DL)/19(UL) |  | -31.62(DL)/19(UL) |  | -31.62(DL)/19(UL) | 
 | 190.81 |  | 190.81 |  | 190.41 | 
 | 0.2 |  | 0.2 |  | 0.2 | 
 | 3 |  | 3 |  | 3 | 
 | 2.2 |  | 2.2 |  | 0 | 
 | 0(DL)/3(UL) |  | 0(DL)/3(UL) |  | 0(DL)/3(UL) | 
 | 3 |  | 3 |  | 3 | 
B(dBHZ) | 52.55(DL)/41.76(15k UL)35.74(3.75k UL) |  |  |  |  | 
K(dBw/K/Hz) | -228.6 |  |  |  |  | 
CNR /dB | DL | UL | DL | UL | DL | UL
 | -8.8 | -0.9/5.1 | -3.3 | 4.6/10.6 | 2.3 | 7.2/13.2
[1] Central beam edge elevation of satellite parameter set-1
[2] Central beam center elevation of satellite parameter set-2

## Slide 5
IMS Voice call over GEO in Rel-20: potential RAN enhancements
Both UP solution and CP solution were standardized for NB-IoT in TN and CP solution is more widely commercialized. Voice data packets and signaling should be transmitted via separating radio bearers to satisfy different QoS requirements. RAN needs to coordinate with SA WGs to study and decide which solution to choose for voice over GEO.
The protocol header reduction can be further studied based on the decision of CP solution or UP solution.
Proposal 3: Study and choose one solution from CP solution and UP solution to support GEO voice service in coordination with SA WGs. Necessary enhancements can be further considered based on the decision of CP solution or UP solution.
SPS is an efficient way to reduce the NPDCCH overhead to schedule periodic UL and DL transmissions, and further increase the system capacity.
Proposal 4: Considering GEO voice characteristics, the following RAN enhancements can be considered:
  semi-persistent scheduling (SPS) enhancements in DL and UL to reduce NPDCCH overhead for scheduling periodic UL and DL transmissions

## Slide 6
Summary
In this contribution, we have the following proposals:
Proposal 1: Design target for TN VoIP services can not apply directly to NB-IoT voice call over GEO, and new design target for RAN need to be defined for NB-IoT NTN voice call over GEO in coordination with SA WGs.
Proposal 2: According to the link budget analysis, the service performance is largely impacted by UE RF parameters and reference scenarios. For a meaningful RAN design to support IoT NTN voice over GEO,
  Baseline UE RF parameters e.g. UE Tx Power, UE Antenna Gain, UE antenna configuration, need to be decided, and enhanced if needed.
  Reference scenarios, e.g. Elevation Angle, need to be decided.
Proposal 3: Study and choose one solution from CP solution and UP solution to support GEO voice service in coordination with SA WGs. Necessary enhancements can be further considered based on the decision of CP solution or UP solution.
Proposal 4: Considering GEO voice characteristics, the following RAN enhancements can be considered:
  semi-persistent scheduling (SPS) enhancements in DL and UL to reduce NPDCCH overhead for scheduling periodic UL and DL transmissions

## Slide 7
Observation: The link-level coverage enhancement for UL and DL has been carried out in R18 and R19 to close the coverage gaps, further enhancement at system-level is left un-finished can could be beneficial for improving system throughput and initial access capacity.