## Slide 1: Views on Ambient IoT work in 5G-A Rel-20
Agenda item: 15.1.3
Source: CATT
3GPP TSG RAN Meeting #108 RP-251636
Prague, Czech Republic, 9th -13th June, 2025

## Slide 2: Ambient IoT Normative works after RAN study
RAN working group complete the study of solution for Ambient IoT in Rel-19
The outcome of A-IoT study
  Target to have the common air interface design for different deployment scenarios and topologies for all types of devices.
  Evaluation methodology and evaluation results of coverage and latency for inventory use case
  The frame structure and timing for A-IoT operation
  The A-IoT device architecture – devices 1/2a/2b
  The device availability/unavailability associated with energy harvesting,
  The physical layer design -
    Modulation and waveform – including CP handling for OFDM waveform
    Channel coding – Line code, FEC, CRC, bit/chip/block-level repetition
  Physical channels/signals –
    DL PRDCH
    UL PDRCH
    Preamble
  Carrier wave –
    Single tone and dual single tone
    Operation spectrums and transmission node
    Interference cancellation
  Multiple Access – TDMA/FDMA/CDMA
  Random Access procedures
    Paging
    3-step/2-step/unified
  Topology 2 resource allocation for UE reader

## Slide 3: Rel-19 Works on Solutions for Ambient IoT in NR
Rel-19 Solutions for Ambient IoT (Internet of Things) in NR WID in RP-243326
  Device 1: ~1 µW peak power consumption,
  Deployment scenario 1 with Topology 1, according to D1T1-B.
  FR1 licensed spectrum in FDD, with R2D in DL spectrum and D2R and CW in UL spectrum.
  Spectrum deployment in-band to NR and standalone, with A-IoT BS located indoor.
  ETraffic types DO-DTT, DT, for rUC1 (indoor inventory) and rUC4 (indoor command).
  Carrier wave transmission for waveform 1 only, without hopping, per the following cases in TR 38.769:
  Case 1-4 for D1T1-B
  Proximity determination via Solution 1 in TR 38.769 only.
  Device (un)availability via Direction 1 in TR 38.769 only.

## Slide 4: Normative work in Rel-20
Workplan for Rel-20 endorsed in RAN#106 (RP-243280)
  Includes D2T2
  Includes Device 2
  A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point
  Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed.
  Details to be discussed at a later RAN plenary meeting, including the need for study phase.
Moderator summary in RAN#107 discussion of Rel-20 Ambient IoT normative work(RP-250802)
  There was general consensus on the support of device 1 in D2T2 in Release 20 A-IoT
  Clear majority of companies were supportive of having only device 2b in D1T1 and D2T2 in Release 20 A-IoT
    Only support device 2b in D1T1 and D2T2 - majority
    Support both device 2a and 2b in D1T1 and D2T2
  Multiple companies voiced support for outdoor scenarios based on commercial needs – concerns from some companies
  For the purpose of TU planning:
    Device 1 in D2T2
    Device 2b in D1T1 and D2T2
    Study on A-IoT for outdoor scenarios
    Further discuss other aspects of Rel-20 A-IoT (e.g. DO-A traffic, unavailability direction 2) in RAN#108
    [3~3.5] TUs in RAN1 and [2] TUs in RAN2 for Release 20 5G-Adv A-IoT

## Slide 5: Outdoor Coverage with A-IoT device Mobility
Motivation:
  Tracking outdoor/indoor A-IoT device with device mobility
  The target coverage distance of 50-1000 m for A-IoT device with mobility
  Outdoor use cases:
    Outdoor inventory: airport port terminal/shipping port
    Outdoor positioning: personal belonging finding, cargo tracking, luggage tracking
      Autonomous A-IoT device triggering focuses on device 2A/2B
Objective:
  Specify mechanism in extension of the A-IoT coverage to maximum distance of 50-1000m with device mobility for outdoor scenarios
  Specify autonomous A-IoT device triggering for device initiated use case for outdoor inventory and positioning
  Specify the control mechanism for Topologies 3 and 4 in addition to Topologies 1 and 2.
Outdoor sensor: ultra-high voltage substation
Outdoor inventory airport terminal/shipping port and cargo tracking
Outdoor Positioning: personal belonging finding

## Slide 6: Autonomous/network trigger Report Sensing
Motivation:
  Sensor service: periodic/aperiodic A-IoT device triggering device triggering reporting or network-initiated reporting for sensing and tracking
  Support of use case for A-IoT device triggering reporting/alarming e.g., cargo monitoring, fire monitoring, room monitoring with alarming
Objective:
  Specify DO-DTT and Do-A traffic for triggering periodic/aperiodic reporting in indoor/outdoor scenarios
Fire monitor sensor
Room Environmental Supervision
Smart grid

## Slide 7: A-IoT Positioning for Positioning Use Cases
Motivation:
  A-IoT positioning use cases of locating and tracking A-IoT devices could not get the required positioning accuracy from Proximity determination in Rel-19 A-IoT study
  Support the positioning method for tracking A-IoT device with device mobility.
  Low hearability in signals backscattered/transmitted from the A-IoT device
Objective:
  Specify the positioning method for the reader to enable the A-IoT device positioning estimation for positioning use cases
Smart Parking
Tracking and locating A-IoT devices indoors and outdoors
Inventory management and positioning base payment