## Slide 1: Network energy saving enhancements for 5G-Advanced in Rel-20
Huawei, HiSilicon, TIM, Orange, Deutsche Telekom, Telefonica, China Unicom, Fraunhofer IIS, Fraunhofer HHI, CAICT, TCL, CEWiT, Sharp, Rohde & Schwarz
3GPP TSG RAN#108 RP-251648
Prague, Czech, June 09-13 2025
Agenda Item: 15.1.6

## Slide 2
Background
Energy consumption is a key part of the operators’ OPEX, and thus it is worthwhile to apply network energy saving techniques to as many scenarios and use cases as possible.
The techniques developed in Rel-18/19 can only apply to part of the use cases and/or deployment scenarios. Therefore, there is still strong need to continue the enhancements on network energy saving for 5G-Advanced in Rel-20. This way, the chance of successful deployment of NES techniques in the field within the ongoing 5G timeframe increases.
In Rel-18, Cell DTX/DRX is specified, which is beneficial for both network and UE from energy saving perspective. However, network would be conservative to enable cell DTX/DRX in practical deployment, if the traffic information of a UE is not available at the network side.
Always on SSB with 20ms periodicity prevents cells from going to deeper sleep modes, and thus leads to high energy consumption, especially for the case of low load. SSB periodicity extension can achieve very promising energy saving gain according to the Rel-18 study as shown in TR 38.864.

## Slide 3
  Proposal 1: Support a 5G-A Rel-20 item on enhancements of network energy saving.
  Proposal 2: 5G-A Rel-20 enhancements of network energy saving shall include the following objectives:
    Specify UE recommended cell DTX/DRX via UAI (UE Assistance Information) [RAN2]
      Note: The candidate cell DTX/DRX configurations to be reported by UE can refer to the cell DTX/DRX configurations developed in Rel-18
    Specify an extended SSB periodicity of 160ms assumed by UE during initial access [RAN1, RAN4, RAN2]
      Note 1: Consider default 160ms SSB periodicity for certain specific band(s), e.g. n104
      Note 2: The number of frequency raster points the UE is expected to search during initial frequency scan will be proportionally reduced, i.e. by 1/8 if the SSB periodicity is increased from 20ms to 160ms
Proposals