## Slide 1: Priority RAN4 led NTN topics for 5GAdv Rel-20
Viasat, Inmarsat
3GPP TSG RAN #108, Prague
Agenda: 15.4.1 (REL-20 proposals led by RAN4 - General)
TDOC: RP-251714
For: discussion

## Slide 2: Priority RAN4 led NTN topics for 5GAdv Rel-20
NTN HPUE
Intra SAN Carrier Aggregation
Irregular CBW for NR-NTN
Good user experience is key to NTN
Beyond PC1 is desired for some markets
Existing satellite terminals in some markets go well beyond PC1
  Existing EIRP 7dBW class terminals: BGAN (Maritime, Aero) terminals, Thuraya Terminals
  3GPP needs to maintain parity
  3GPP technology should allow operators to transition these to 3GPP NTN technology
NTN (especially in FR1) spectrum allocations are fragmented across operators
UEs have multiple amplifiers available
CA is common in TN networks
Increasing user speeds is key to improving user experience
Spectrum allocation globally is non-uniform, often fragmented
Operators need options for deployment flexibility
Irregular CBW options for NR-NTN will increase operational flexibility for operators

## Slide 3: 3GPP Satellite Performance Requirements TS 22.261
Key markets such as vehicular, aeronautical and maritime where Viasat has significant investments and customers require data rates ranging from 25 to 50 Mbps at FR1
Terminals have to be cost effective to compete and price points with FR2 mmWave may not be competitive

## Slide 4: Link capabilities evaluation
An L band NGSO LEO system was evaluated at 600 km using a 2 m antenna for uplink performance
  Slant range of 630 km and 30° elevation assumed, 5 dBW EIRP from UE
  With 5 MHz BW (50 RB) typical user data rate of 10.5 Mbps achieved on uplink (worst case 8 Mbps)
  Increasing EIRP to 7 dBW achieves 13 Mbps typical
We would like to have HPUEs >> PC1 for the non handheld case (ie automotive, aviation, and maritime) with higher powers where SAR and other considerations are lower and greater front end capabilities may be cost effective
To meet 3GPP objectives for UL data rates, Viasat can provide 10 MHz with CA

## Slide 5: Proposals
Proposal 1:
  RAN to consider at RAN #109 the following RAN4 led topics for Rel 20, 5GAdvanced work plan
    HPUE (Beyond PC1)
    Intra SAN CA
    Irregular CBW deployments for NR-NTN