## Slide 1
Views on further mobility
enhancement in 5G-A Rel-20
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.2.3
TDoc number: RP-251727
Source: ZTE Corporation, Sanechips

## Slide 2: Status from RAN#107
The potential objectives for a Rel-20 Work Item on Mobility Enhancements were discussed in detail at RAN#107, leading to the following conclusion (as captured in the summary on the Rel-20 5G-A discussion provided by the RAN VCs and WG Chairs in RP-250812):
  RAN2: Mobility
The following objectives are considered as baseline for Rel-20
Specify LTM SCell improvements for further reducing interruption delays
  SCell activation
    Specify the necessary configuration and UE procedures for NW triggering of LTM SCell activation with LTM cell switch [RAN2, RAN3].
    Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4].
NOTE: Reuse the candidate cell LTM measurement and reporting procedures where possible for the SCell improvements
NOTE: This objective is NOT applicable to non-co-located CA and is NOT applicable to C-LTM
NOTE: This objective is applicable to MCG and SCG
Dynamic L1 measurement and reporting configuration change
  Specify the necessary configuration and procedures for MAC CE based configuration selection among prior provided RRC configurations of UE L1 measurement and reporting LTM configuration [RAN2]
  Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4]. ????
NOTE 1: This sub-objective is applicable to C-LTM as well.
NOTE 2: For this objective, we strive to avoid RAN1 impact (including reporting)
NOTE 3: RAN1/RAN3/RAN4(?) involvement is based on LS if necessary
No further RAN2 objectives are considered for Rel-20

## Slide 3: ZTE view
The list of objectives for a Rel-20 Work Item on Mobility Enhancements (as in RP-250812) is fully stable, no changes to the current objectives’ description is needed and no new objectives should be added
The discussion at RAN#108 should only focus on resolving the “?” for the second objective in the summary in RP-250812, i.e. on whether RAN4 should be impacted and on possibly removing the last Note
  Regarding this, we think that:
    There should be no RAN4 impact due to a dynamic L1 measurement and reporting configuration change (i.e. via MAC CE controlled selection from a previously provided RRC configuration), so that RAN4 should not be included for the second objective
    Also RAN1 and RAN3 are not expected to be impacted by the second objective, so the last Note could be removed

## Slide 4: Proposal for the Rel-20 Mobility Enhancements WID objectives
Specify LTM SCell improvements for further reducing interruption delays
  SCell activation
    Specify the necessary configuration and UE procedures for NW triggering of LTM SCell activation with LTM cell switch [RAN2, RAN3].
    Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4].
NOTE: Reuse the candidate cell LTM measurement and reporting procedures where possible for the SCell improvements
NOTE: This objective is NOT applicable to non-co-located CA and is NOT applicable to C-LTM
NOTE: This objective is applicable to MCG and SCG
Dynamic L1 measurement and reporting configuration change
  Specify the necessary configuration and procedures for MAC CE based configuration selection among prior provided RRC configurations of UE L1 measurement and reporting LTM configuration [RAN2]
  Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4]. ????
NOTE 1: This sub-objective is applicable to C-LTM as well.
NOTE 2: For this objective, we strive to avoid RAN1 impact (including reporting)
NOTE 3: RAN1/RAN3/RAN4(?) involvement is based on LS if necessary

## Slide 5: Thank You！