## Slide 1: Motivation for Irregular Channel Bandwidth Work Item in Rel-20
T-Mobile USA, China Telecom, China Unicom, Bell Mobility, Boost Mobile, UScellular, Murata, Iridium
June 2025
3GPP TSG RAN Meeting #108
Prague, Czechia, June 9-13, 2025
Agenda: 15.4.2
Document for: Discussion
RP-251752

## Slide 2: Introduction
  In Release 18, a Study Item (SI) titled "FS_NR_eff_BW_util" was established to facilitate more efficient utilization of licensed spectrum that does not conform to existing NR channel bandwidths, commonly referred to as "irregular channel bandwidth." To date, the irregular channel bandwidths to the right have been proposed.
  The SI was concluded at RAN#99 meeting with the general conclusions (TR 38.844 ) that two promising methods – overlapping channels from network perspective and the next larger channel – can be used to support irregular channels. However, there has been no follow-on work that could lead to commercialization of any of the techniques studied in the study item.
  3MHz channel BW has been added, primarily at the request of railroad operators. Yet, we still don’t have a standardized NR mechanism for efficient use of licensed mobile spectrum for irregular channel bandwidth such as the ones listed to the right
  Given the importance and value of low band spectrum, it is critical that operators with irregular channel bandwidths can use the spectrum efficiently
  This document discusses the motivation for a new Work Item for Irregular Channel Bandwidths in Rel-20.
Band (s) | Irregular Channel Bandwidth(s)
n5 | 6, 7, 11, 12 MHz
n8 | 6,11 MHz
n12, n85 | 6, 12 MHz
n26 | 7 MHz
n28 | 13 MHz
n29 | 6, 11 MHz

## Slide 3: Discussion
  The following solutions were proposed in the Study Item:
  Solution 1. Next larger channel bandwidth
  Solution 2. Overlapping CBWs from the network perspective
  Solution 3. Combined UE CBW
  Solution 4. Overlapping CA
  Each of these have certain pros and cons, summarized in Table 7.2.1 from 38.844.
  Proposal 1： Given the complexity and effectiveness, solution 1 and 2 are preferred :
  Next larger channel bandwidth can be supported as a generic optional solution.
  Overlapping CBWs from the network perspective can be a default solution for channel bandwidth larger than 7MHz.
  Problem with next wider channel BW or overlapping carriers for low band, 6 and 7 MHz channel BWs:
  Next wider channel BW with PRB blanking isn’t ideal for a coverage band, because of the potential for blocking from neighboring services
  Overlapping CBWs from the network perspective for 6 and 7 MHz channels would require frequency overlapping but time offset SSBs, which are not explicitly required by 3GPP specs and have not been tested, so it is likely such configurations are not supported by legacy UEs.
  To avoid these issues, it would be better to support native 6 and 7 MHz channel BWs.
  Proposal 2： Create native channel bandwidths for 6 and 7 MHz only.

## Slide 4: Updates from RAN#106
A new RAN4 Work Item was created for 7 MHz channel bandwidth
Work on a 6 MHz channel bandwidth was deferred due to RAN4 Time Unit limitations
  Operators have requested 6 MHz for n5, n12, n29 and n85
No work yet on the general approach for irregular channel bandwidths wider than 7 MHz

## Slide 5: Exemplary objectives for Rel-20 WID
  New standard channel bandwidth for 6 MHz:
    Specify necessary RAN4 requirements to support deploying UE and gNB NR channel bandwidths of 6 MHz [RAN4]:
    Specify RF requirements:
      Specify the required RF requirements for optional 6 MHz channel bandwidths, including PRB numbers, minimum guard band and reference sensitivity
      Use n85/n12/n5/n29 for example bands for 6 MHz:
      Limit to 15 kHz for FDD bands only to minimize RAN4 workload
  Define Overlapping channels from network perspective for channel bandwidth larger than 7MHz as default solution for irregular channel bandwidth.
    No UE changes needed (as per 38.144 table 7.2.1)
    RAN4 to decide if new gNB channel bandwidths are needed
  Define Next larger channel bandwidth with PRB blanking as optional solution:
    For the UE, define Asymmetric BCSs for relevant bands to allow next wider BW on the DL, next smaller BW on the UL
    RAN4 to decide if new gNB channel bandwidths are needed

## Slide 6: Conclusions
  In this paper we have presented our views on how irregular channel bandwidths can finally be supported for several solutions .These solutions could be used for both terrestrial and non-terrestrial networks.
  Proposal 1: Given the complexity and effectiveness, solution 1 and 2 are preferred :
    Next larger channel bandwidth can be supported as a generic optional solution.
    Overlapping CBWs from the network perspective can be a default solution for channel bandwidth larger than 7MHz.
  Proposal 2: Add 6 MHz UE and gNB channel bandwidths.
  Proposal 3: Create a new Rel-20 WI to enable support of irregular channel bandwidths.

## Slide 7: Thanks!