## Slide 1: Concerns about Coexistence between NTN band n252 and n2/n25
T-Mobile USA, RAN#108, June, 2025
RP-251754

## Slide 2: Introduction
T-Mobile USA and other operators previously documented our concerns about coexistence between the n252 uplink and the B2/n2/B25/n25 downlink in several RAN4 contributions, including R4-2413305, R4-2416507, R4-2419375 and R4-2502202.
In this document we would like to summarize our concerns for RAN Plenary

## Slide 3: Concerns
5 MHz is not sufficient separation for the uplink of one band to the downlink of another band, especially for wider uplink channel bandwidths
The SEM only provides -13 dBm/MHz protection from 5 MHz to the channel bandwidth of the uplink signal
The normal practice of defining -50 dBm/MHz protection with A-MPR would not be ideal for an NTN system because the A-MPR could break the uplink link budget for many configurations

## Slide 4: Protection based on the SEM
5 MHz is not sufficient frequency separation for the uplink of one band to the downlink of another band
The SEM only provides -13 dBm/MHz protection from 5 MHz to the channel bandwidth, which is 37 dB higher than the normal UE-UE coexistence limit
Depending on the assumptions, at -13 dBm/MHz into another band, the UE-UE distance could be 60 meters with the baseline 3GPP UE-UE assumptions, up to 956 meters based on more conservative assumptions (R4-2502202)

## Slide 5: A-MPR vs. limiting UL BW to provide protection
Some simulations showed that significant A-MPR would be needed to provide the typical -50 dBm/MHz protection that one 3GPP band provides to other 3GPP band downlinks that are deployed in the same region (R4-2415314). The amount of A-MPR would severely impact the n252 uplink link budget
T-Mobile USA and others proposed limiting the n252 UL Channel Bandwidth to 5 MHz to minimize the interference
In R4-2502202 T-Mobile showed how -30 dBm/MHz be met without NS signalling for most 5 MHz uplink locations
The proponents did not want to limit the uplink for the band to 5 MHz because they said that would limit deployments where there was no n2 or n25, like northern remote areas in Canada
The agreement was to define two protection levels, -40 dBm/MHz and -30 dBm/MHz and the associated A-MRP, and to define asymmetric BCSs to allow an n252 UE to use narrower uplink CBWs with wider downlink CBWs. With narrower uplink channel bandwidths, little or no A-MPR is required.

## Slide 6: Summary
T-Mobile USA would like RAN Plenary to understand the potential coexistence issues which have been discussed in RAN4
Hopefully, NTN operators will make deployment choices that minimize the negative impacts to other networks

## Slide 7: References
[1] R4-2413305, “Coexistence between S-Band NTN and Terrestrial Networks.” T-Mobile USA
[2] R4-2416507, “NTN S-Band UE-UE coexistence with TN,” T-Mobile USA Inc., AT&T, UScellular
[3] R4-2419375, “NTN S-Band UE-UE coexistence,” T-Mobile USA Inc., US Cellular, Verizon, AT&T, Deutsche Telekom
[4] R4-2502202, “NTN S-Band UE-UE coexistence,” T-Mobile USA, Verizon
[5] R4-2415314, “Initial view on the UE power back-off while operating in 2000-2020 MHz UL range,” Apple