## Slide 1: Applicability of Rel-19 common PDCCH repetition for terrestrial networks
Huawei, HiSilicon, China telecom, Apple, OPPO, Lenovo
3GPP TSG RAN#108 RP-251857
Prague, Czech, June 9-13, 2025
Agenda Item: 9.3.2.2

## Slide 2
Common PDCCH repetition for link level coverage enhancement is introduced under R19 NR NTN (see details in Appendix).
UE feature groups (FG 65-1-2/FG[65-1-3]) are introduced for common PDCCH repetition with the latest version as copied below:
  As shown in the FG above, one discussion point (FFS) is the applicability of these FGs for TN
  There are solid supports from companies to support applying these FGs to TN.
  There are some comments raised in RAN1#121 saying that whether to apply these FGs to TN needs to be discussed in RAN plenary first.
Background
65-1-2 | PDCCH repetition for Type0 PDCCH CSS | 1. Support reception of PDCCH repetition for Type0 PDCCH CSS [of searchSpaceZero configured within MIB pdcch-ConfigSIB1] FFS: whether to merge this FG with FG(s) for PDCCH repetition for other than Type0 PDCCH CSS FFS: whether to merge this FG with FG(s) for SIB1 PDSCH repetition | FFS: | FFS | N/A | PDCCH repetition for Type0 PDCCH CSS is not supported | Per band | N/A | N/A | N/A | Note: This UE feature group is applicable [only] for bands in Tables 5.2.2-1 [and 5.2.3-1] in TS 38.101-5 [FFS: Applicabilitiy of this FG to TN] | Optional [with/without] capability signaling
65-1-3 | PDCCH repetition for Type [0A/0B/1/1A/2/2A] PDCCH CSS | 1. Support reception of PDCCH repetition for Type [0A/0B/1/1A/2/2A] PDCCH CSS | FFS: | FFS | N/A | FFS | Per band | N/A | N/A | N/A | Note: This UE feature group is applicable [only] for bands in Tables 5.2.2-1 [and 5.2.3-1] in TS 38.101-5 [FFS: Applicabilitiy of this FG to TN] | Optional [without] capability signaling

## Slide 3
Proposal for applicability of common PDCCH repetition for TN
  Proposal：Common PDCCH repetition introduced in Rel-19 NR NTN WI is also applicable for TN for FR1 only.

## Slide 4
Appendix: RAN1 key agreements for common PDCCH repetition
Agreement in RAN1#120bis
For PDCCH repetition for Type0 PDCCH CSS of searchSpaceZero configured within MIB pdcch-ConfigSIB1, support repeated PDCCH candidates in the two consecutive slots and associated with the same SSB index ( as defined in section 13 of TS 38.213) at least for M=2.
Repeated PDCCH candidates share the same aggregation level (AL), coded bits and same candidate index
    Note: if the network repeats the Type 0 PDCCH across two consecutive slots, a legacy UE might decode the PDCCH and associated PDSCH in one slot and skip PDCCH monitoring in the other slot.
Note: further discuss the potential solution for M=1 and M=1/2.
Agreement in RAN1#121
For PDCCH repetition for Type0 PDCCH CSS of searchSpaceZero configured within MIB pdcch-ConfigSIB1, the solution agreed for M = 2 is also applied to M = 1 and M = 1/2.
Agreement in RAN1#121
For PDCCH CSS other than Type-0 CSS and other than Type-3 CSS for common search spaces other than SearchSpaceZero, support intra-slot repetition based on:
The starting symbol of monitoring occasion of the second SS is located right after the ending symbol of monitoring occasion of the first SS.
BD is counted as one or two, subject to UE capability, in RRC connected mode
  UE assumes that a DCI Format with the same content is repeated on two PDCCH candidates.
  Note: From RAN1 perspective UE is expected to deliver performance no worse than soft combining
PDCCH repetition is applicable to RNTI of the CSS.
Repeated PDCCH candidates within the same CORESET repeated in the slot, and share the same aggregation level (AL), coded bits and same candidate index.
  Up to editor how to capture this in writing the relevant RAN1 specification.