## Slide 1: Motivation for HD-FDD operation for NR NTN in bands above 10 GHz
Source: Eutelsat, MediaTek Inc, SES, Thales, Airbus, CHTTL, Gilat, ESA, Fraunhofer IIS, BMW, ST Engineering iDirect, Lockheed Martin, Robert Bosch GmbH
3GPP TSG-RAN Meeting # 109 RP-252587
Beijing, China, 15th – 19th September 2025 Agenda Item 9.1.4.6

## Slide 2: Background
In RP#107, there were contributions raising the strong commercial demand of reducing the antenna size and/or support for half duplex mode for Ku band (RP-250240, RP-250457, RP-250483, RP-250648).
In RP#108, RAN4 Rel-20 5G-A package was discussed. The discussions were summarized in RP-251879 which was endorsed.
In this contribution, we provide a consolidated motivation of introducing half-duplex FDD (HD-FDD) devices for antenna size reduction on Ku/Ka band and propose it as an essential part of the RAN4 Rel-20 5G-A package.

## Slide 3: Motivation: Commercial
Current market landscape
  HD-FDD technology has been widely used, demonstrating the fact that cost reduction is a key driving factor for successful markets in other non-3GPP satellite communication systems, including:
    Starlink’s progression from generation 1 to generation 4
    Amazon’s Kuiper project, except for its high-end, larger antennas.
    Eutelsat OneWeb terminals (Intellian 10HX, HNS HL-1100)
Commercial demand
  The global automotive antenna market is expected to be $12.2Bn by the end of the decade [1] and automotive satellite connectivity has a forecast value of $10.3Bn by 2033 [2].​ Automotive-mounted VSAT (circa. 20 x 20 cm) are considered a key segment for Ku/Ka band NR-NTN market penetration due to large volumes.
  HD-FDD antennas are simpler to implement than FD-FDD antennas and better match the consumer expected price point.
  HD-FDD increases the addressable market; it avoids the need for a duplexer thus makes feasible and cost effective a full-band VSAT terminal architecture for use in bands >10 GHz including bands where the Tx/ Rx gap is small
Observation 1: There is a clear commercial demand for HD-FDD VSAT terminals today and demand is expected to grow significantly.
[1] https://www.globenewswire.com/news-release/2023/04/26/2654771/0/en/Global-Automotive-Antenna-Market-Size-To-Grow-USD-7253-13-Million-By-2030-CAGR-of-6-30.html
[2] https://growthmarketreports.com/report/satellite-connectivity-for-automotive-market

## Slide 4: Motivation: Technical aspects
Implementation constraints
  HD-FDD eliminates the need for separate transmit and receive FD-FDD antenna panels, reducing antenna size by about 50%.
  HD-FDD avoids complex duplexers/filters in a FD-FDD single antenna panel; typically reducing performance by over 3 dB thus requiring at least double the antenna size (area) to compensate.
  Footprint and cost are critical factors for general adoption especially in the automotive market. Passenger vehicles, especially those with more aerodynamic designs and glass roofs, require compact antenna arrays due to limited physical space.
System and Service impact
  Assuming HD-FDD for the UE only, the SAN can continue operating in full duplex mode and the overall system capacity is not compromised.
  In principle, the amount of radio resource assigned to Rx and to Tx respectively can be flexibly allocated. So peak performance of the UE is only slightly reduced.
Observation 2: HD-FDD reduces implementation complexity and enables small VSAT with no impact on system capacity and minimal impact on end user experience.

## Slide 5: Specification impact
We propose RAN to consider the objective to introduce half-duplex (HD) NR-NTN devices for Ku band and Ka band as part of RAN4 Rel-20 5G-A package.
Only a small, well defined, workload is expected:
  Rel-19 NR_NTN_Ph3 WI already introduced HD (e)RedCap devices for NTN in FR1, providing a good starting point for defining HD-FDD requirements for Ku/Ka band.
  RRM specs related to VSAT will need to take HD-FDD into account.
  No additional RAN1 spec impact is needed (expected/foreseen) for operating Ku bands with FR1 SCS. For FR2 SCS, the additional workload, if identified, is expected to be minimal.
Observation 3: Given HD-FDD for (e)RedCap NTN was introduced in Rel-19 (NR_NTN_Ph3), only minimal RAN1 effort is expected to extend it to non-RedCap NTN UEs.
Proposal 1: Specify HD-FDD NR-NTN for bands above 10 GHz as an essential part of the RAN4 Rel-20 5G-A package.
Proposal 2: Study and specify a new VSAT type for antenna sizes below the current assumption 45 x 45 cm down to 20 x 20 cm (“ultra-small”) using HD-FDD.

## Slide 6: Conclusions: Observations and Proposals
Observation 1: There is a clear commercial demand for HD-FDD VSAT terminals today and demand is expected to grow significantly.
Observation 2: HD-FDD reduces implementation complexity and enables small VSAT with no impact on system capacity and minimal impact on end user experience.
Observation 3: Given HD-FDD for (e)RedCap NTN was introduced in Rel-19 (NR_NTN_Ph3), only minimal RAN1 effort is expected to extend it to non-RedCap NTN UEs.
Proposal 1: Specify HD-FDD NR-NTN for bands above 10 GHz as an essential part of the RAN4 Rel-20 5G-A package.
Proposal 2: Study and specify a new VSAT type for antenna sizes below the current assumption 45 x 45 cm down to 20 x 20 cm (“ultra-small”) using HD-FDD.

## Slide 7: Thank you!