## Slide 1: Views on RAN4 Rel-20 5G-A UE RF topics
T-Mobile USA, RAN#109, September 2025
RP-252760

## Slide 2: Way Forward from RAN#108
UE RF centric evolution
  Agreements:
The high-level scope of the WI on UE RF centric evolution (the exact scope and WID draft will be discussed and decided in RAN#109):
FR1 HPUE enhancement
  Further consider/discuss until RAN#109 on the detailed scope
  This work is to focus on the TN application
6MHz channel bandwidth
  It can be prioritized to FDD band <1GHz
Study and, if feasible, reduce UE MPR values with the relaxed Tx EVM requirement for 5G NR higher modulation orders, i.e., 64QAM , 256QAM
  BS demod scope is included.
  The study is performed based on non-AI-based approach at BS receiver as baseline and without RAN1 impact
    The details for study is to be discussed until RAN#109
  This work will be started in Q1’26. If the similar scope (The examples include the enhancements enabled by BS advanced receiver and UE Tx signal modifications. It is noted that referring to these examples in this WF should not be deemed as taking these examples as the baseline or starting point in 6G study) is agreed by RAN4 to be studied in 6G, it will be removed from 5G-A package. In this case, it is possible that 6G related conclusion can be applied to 5G.
No RAN1/2 scope is expected
Target 0.5 RF TU in Q4’25 and 1.25 TU (0.75 RF and [0.5] Demod for EVM relaxation and 6MHz) from Q1’26.

## Slide 3: FR1 HPUE Enhancements Priorities from RP-251753
High power PC1.5/PC1 UE for TN single carrier in NR FR1
  PC1 with 4Tx UL for FWA. Super High
  PC1 with 2Tx and UL-MIMO Super High
  PC1.5 FDD with 2Tx High
  PC1.5 with 1Tx Medium (although needed for PC1 with 2Tx)
  PC1.5 TDD and FDD with 3Tx High
High power [PC1]/PC1.5/PC2 UE for TN single carrier in EN-DC and NR CA
  PC2/PC1.5 EN-DC with PC2 LTE band with 2Tx or 3Tx Low (Already can be in baskets)
  PC1.5 with 4Tx or 8Tx for UL intra-band and inter-band CA High
  PC1 with DL CA (was listed as PC1.5, but we already have that) High
  3UL CC in two bands for CA/EN-DC with PC2 / PC1.5 (2Tx) with 2CC in NR Already in Rel-19
  PC1.5(2Tx) FR1 PDE for intra-band CA Medium
    NOTE: PDE power domain enhancement
Consider postponing lower priority items until the June 2026 Rel-20 checkpoint
Updates since RP-251753 highlighted in yellow

## Slide 4: 6 MHz Channel Bandwidth
We strongly support the introduction of 6 MHz channels for reasons captured in RP-242872.
We appreciate the support this item has received so far.

## Slide 5: Reduced UE MPR values with relaxed Tx EVM
We support this work, but given the limited TUs available we support it as part of a 6G study