## Slide 1: On 3GPP internal requirement on 6G peak rate target
AI 8.2.1.1 Key performance indicators
Ericsson
3GPP TSG RAN Meeting #110 RP-253111
Baltimore, MD, USA, December 8-11, 2025

## Slide 2: Background
  RAN plenary did not recommend a value of peak data rate TPR for IMT-2030 in the LS sent to ITU (RP-252966)
  There is no set KPI value for 6GR peak data rate in TR 38.914
  RAN1 has made an interim assumption (in RAN1#122b) regarding the target peak data rate in the study of 6G channel coding
  Extreme peak data rate metrics have little, if any, bearing on the end-user experience in the field
  Decision on peak target data rates for 6GR should be done by RAN plenary only (R1-2509398)

## Slide 3: Proposals
  RAN plenary to provide guidance on 3GPP internal requirement on the 6GR peak data rate target
    6GR peak data rate target is assumed to be 1x-2x of the target peak data rate defined in TR38.913, with the exact value (between 1x and 2x) to be selected during RAN#110, hence
      6GR downlink peak data rate is selected in the range 20-40 Gbit/s
      6GR uplink peak data rate is selected in the range 10-20 Gbit/s