## Slide 1
On scalable and forward compatible design for diverse device types
RP-253175
3GPP TSG RAN#110
Baltimore, MD, USA, December 8 – 11, 2025
Source: Ericsson
Agenda Item: 8.2.1.3.2
Document for: Decision

## Slide 2: Background Agreements from RAN#109
The 6G WG SI has as an objective to “target scalable and forward compatible design for diverse device types”
RAN#109 made several agreements related to diverse device types (agreed Proposals 1, 3, and 4)
  In this contribution, we provide our view on some aspects of these agreements
For agreed Proposal 1, we provide our view on the two aspects identified to be revisited in RAN#110
  Minimum spectrum allocation
  Smallest maximum UE bandwidth
Proposal 1: Endorse the following two RAN1 agreements (with the clarification that the 2nd agreement is applicable to FR1). Companies are invited to bring contributions regarding the minimum spectrum allocation in RAN#110, while RAN1 is requested to continue the study on both the minimum spectrum allocation and the smallest maximum UE bandwidth from the 6GR design perspective. Revisit in RAN#110.
Agreement
For the study of RAN1 6GR design, consider the minimum spectrum allocation in which 6G can operate, subject to further discussion and confirmation in RAN.
  Note: RAN4 involvement is necessary.
Agreement
Study the following smallest maximum supported RF and BB UE BW without spectrum aggregation for at least one low-tier device type supported by 6GR framework from physical layer perspective, subject to further discussion and confirmation in RAN
  Opt1: 3MHz
  Opt2: 5MHz
  Opt3: 10MHz
  Opt4: 20MHz
  FFS: the UL bandwidth may be different to the DL bandwidth
  FFS: the bandwidth value may be different for different SCS, duplex modes, and bands.
FFS: whether RF and BB UE BW are same or different

## Slide 3: Background Agreements from RAN#109
While the agreed Proposals 3 and 4 contain many aspects related to diverse device types, we provide our view on the more urgent ones that impact system design
  BW for initial access (related to smallest maximum UE bandwidth)
  Duplex mode, particularly HD-FDD
  Coverage (our view provided in RP-253174)
Many aspects in Proposals 3 and 4 are not urgent to address and can be deferred until more progress is made in the WG SI, e.g.,
  Whether or not to define device types
  Mandatory and optional features
While not urgent, we provide thoughts on disallowing undesirable capability combinations, e.g., disallowing 1-Rx antenna and HD-FDD for devices with high data rate capability
Proposal 3: To investigate further: (In RAN Plenary)
  Motivations/justifications behind the proposed diverse device types, which should be a limited set
  Whether/how to have one or more device types for eMBB or 6G IoT
  Whether/how to have other device types for, e.g., XR/immersive experiences, FWA, VUE, wearables/RedCap, sensing, NTN-specific, AI agents, collaborative robots, etc.
  Whether/how to explicitly standardize device types
  Ensuring forward compatibility
  Minimizing/avoiding potential market fragmentation
Note: the terminology “device type” is subject to further discussion and possible refinement.
Proposal 4: In terms of diverse device types, study further: (In RAN Plenary)
Possible parameters/factors, e.g.:
  Number of Tx antennas/chains
  Number of Rx antennas/chains
  Power classes
  Maximum UE bandwidth (DL/UL)
  Peak data rate (DL/UL)
  Maximum MIMO layers (DL/UL)
  Duplex mode
  Max modulation order (DL/UL)
  CA/spectrum aggregation (DL/UL)
  UE processing capabilities
  Coverage
  Energy efficiency
  Mobility/speed
  Sensing
  AI
Note: some of the above parameters/factors may be related with form factor
Note: aim to have a focused/limited set of parameters/factors for a device type
The value(s) for the identified parameters for a device type

## Slide 4: Minimum Spectrum Allocation
6G should be designed to operate in a wide range of spectrum allocations. While it typically is not that difficult to scale up a design to support wider spectrum allocations, it is significantly more difficult to scale down an already designed system to smaller allocations (cf. the introduction of 3 MHz in 5G Rel-18). Given that there are allocations of 3 MHz in some FR1 bands, the smallest supported allocation for FR1 FDD should be 3 MHz. This primarily affects the initial access design (e.g., SSB, PRACH) as data transmissions are scheduled and can be adapted to whatever amount of spectrum is available. The requirement on supporting 3 MHz should not unnecessarily restrict the performance when operating in wider spectrum allocations. One such technical solutions is optimizing the SSB for 5 MHz and using puncturing to support 3 MHz.
The latter solution is hinted by the following agreement captured in TR 38.914 during RAN#109:
Proposal 1: 6G should support a minimum spectrum allocation of 3 MHz in FR1 FDD with 15 kHz subcarrier spacing. Initial access design is optimized for operation in wider bandwidths, i.e., ≥ 5 MHz.
5.4.3 Massive Communication (IoT) The 6GR and 6G RAN architecture shall support the following minimum requirements for Massive Communication (IoT): 6G Massive Communication (IoT) shall be supported for FR1. 6GR should have a common/scalable design that supports the above usage scenario in addition to eMBB Prioritize 6GR design for eMBB The above usage scenario should not overlap with Ambient IoT and NB-IoT [PHY or MAC] [minimum] peak data rate is [TBD] Mbps in DL and [TBD] Mbps in UL for lowest-tier device.

## Slide 5: Smallest Maximum UE Bandwidth (+ HD-FDD Operation)*
DL UE Bandwidth
  To maintain a common air interface for 6G IoT UEs and other 6G UEs (same SSB, CORESET#0, SIB transmissions, etc.), it is desired that the smallest mandatory DL UE bandwidth is not too small, to avoid negative impacts on initial access for other 6G UEs. From a pure network perspective, having all UEs support a wide bandwidth simplifies the operation of the system and provides high performance.
UL UE Bandwidth
  Regarding the UE RF Tx side, it has been suggested that to enable a single, cost-efficient HD-FDD UE implementation to address a global market it is desired to facilitate implementations that do not require several band-specific analogue RF (SAW) filters. There may be different ways to enable this, for example using a relatively small maximum UE Tx (RF and/or BB) bandwidth of 3~5 MHz or using UE Tx power back-offs or UL scheduling restrictions to avoid the carrier edges. RAN4 should study feasibility from UE and NW points of view before further decisions are made regarding these aspects. The RAN4 study could potentially also cover the TDD case, where there may be stronger motivation for keeping the RF bandwidths for UE Tx and UE Rx the same.
Proposal 2: The smallest maximum UE RF Rx bandwidth (DL bandwidth) for the lowest-tier UE is at least 5 MHz for FR1 FDD (15 kHz SCS).
Proposal 3: The smallest maximum UE RF Rx bandwidth (DL bandwidth) for the lowest-tier UE is at least 10 MHz for FR1 TDD (30 kHz SCS).
Proposal 4: To aid in decisions on smallest maximum UE RF Tx bandwidth (UL bandwidth), ask RAN4 to study [until June 2026] feasibility from UE and NW points of view of supporting cost-efficient HD-FDD UE implementations addressing a global market without the need for several band-specific analogue UE RF Tx (SAW) filters.
* See our related contribution RP-253099 “Massive Communication (IoT) requirements” for additional discussion

## Slide 6: Initial Access Bandwidth
The smallest maximum UE bandwidth (previous slide) will determine the bandwidth of common signals/channels (CORESET#0, SIB, etc.) if a particular carrier is intended to serve both the lowest-tier UEs and other UEs
However, an operator may also choose to configure the network so that the lowest-tier UEs are only served on some carriers while the other carriers are reserved for more capable UEs
  This means that the bandwidth of the common signals/channels (initial access bandwidth) can be wider than the smallest maximum UE bandwidth on those other carriers
It should be noted that the bandwidths of these signals/channels may depend on, e.g., the SCS and thus effectively be band dependent
Proposal 5: To enable operation on a variety of carrier bandwidths, the 6GR design should support configurability of the bandwidth(s) of common signals/channels (initial access bandwidth), e.g., CORESET#0, SIBx, etc. Hence, the network can configure the initial access bandwidth on a carrier to be the same or wider than the smallest maximum UE bandwidth depending on whether or not the lowest-tier UEs (for IoT) are intended to be served on that carrier.

## Slide 7: Disallowing Undesirable Capability Combinations
All 6G UEs should support a mandatory baseline functionality
  The properties of the lowest-tier 6G UE must be considered when defining this mandatory baseline functionality
Catering for the lowest-tier UE already in the first 6G release is easier and ensures both forward and backward compatibility
  Experience from earlier generations shows it is much easier to scale up functionality in a later release than to it scale down
The lowest-tier UE should be the starting point for discussion on scalable and forward compatible design for diverse device types
  See our related contribution RP-253099 “Massive Communication (IoT) requirements”
Undesired capability combinations can be prevented by making 6G UE capabilities conditional on other capabilities (prerequisites)
  For example, the support of 1 Rx antenna and HD-FDD can be tied to support of very low peak rates, to disallow 1-Rx and HD-FDD for devices with high data rate capability (e.g., smartphones, XR devices, etc.)
Observation 1: Conditional capabilities (prerequisites) can be used to disallow undesired capability combinations for 6G UEs

## Slide 8: Observations and Proposals
Proposal 1: 6G should support a minimum spectrum allocation of 3 MHz in FR1 FDD with 15 kHz subcarrier spacing. Initial access design is optimized for operation in wider bandwidths, i.e., ≥ 5 MHz.
Proposal 2: The smallest maximum UE RF Rx bandwidth (DL bandwidth) for the lowest-tier UE is at least 5 MHz for FR1 FDD (15 kHz SCS).
Proposal 3: The smallest maximum UE RF Rx bandwidth (DL bandwidth) for the lowest-tier UE is at least 10 MHz for FR1 TDD (30 kHz SCS).
Proposal 4: To aid in decisions on smallest maximum UE RF Tx bandwidth (UL bandwidth), ask RAN4 to study [until June 2026] feasibility from UE and NW points of view of supporting cost-efficient HD-FDD UE implementations addressing a global market without the need for several band-specific analogue UE RF Tx (SAW) filters.
Proposal 5: To enable operation on a variety of carrier bandwidths, the 6GR design should support configurability of the bandwidth(s) of common signals/channels (initial access bandwidth), e.g., CORESET#0, SIBx, etc. Hence, the network can configure the initial access bandwidth on a carrier to be the same or wider than the smallest maximum UE bandwidth depending on whether or not the lowest-tier UEs (for IoT) are intended to be served on that carrier.
Observation 1: Conditional capabilities (prerequisites) can be used to disallow undesired capability combinations for 6G UEs