## Slide 1
Discussion on 6G requirements for IoT
RP-253255
3GPP TSG RAN Meeting #110
Baltimore, USA, December 8-11, 2025
Agenda Item: 8.2.1.4
Document for：Discussion/Decision

## Slide 2
Proposal 1: 6G Massive Communication (IoT) shall be supported for FR1. - 6GR should have a common/scalable design that supports the above usage scenario in addition to eMBB Prioritize 6GR design for eMBB The above usage scenario should not overlap with Ambient IoT and NB-IoT Proposal 2: For 6G Massive Communication (IoT), the minimum number of UE receive/transmit antenna is 1 for lowest-tier device - Reflect this agreement in the device type section of the TR
  Following proposals were agreed in RAN#109 for massive communication (IoT)
Introduction: Agreements and open issues
  Remaining aspects to be decided
  Maximum UE bandwidth
  Duplex operation
  UE data rate
  Target coverage

## Slide 3
Background: LTE & NR Low Cost IoTs
  Lessons learned from LTE & NR
  Too many device types result in fragmented market
  Device with extremely small BW results in separate RAT/deployment
  Extreme coverage without real requirement results in poor resource efficiency
  Low data rate capable of limited service
Note: 20MHz RF BW, 5MHz BB BW for unicast PDSCH & PUSCH, while others in 20MHz BB BW
 | Max UE BW | Data rate (DL/UL) | Coverage (MCL) | Antenna
Rel-13 NB-IoT | 200KHz | 26/66Kbps | 164dB | 1T1R
Rel-13 LTE-MTC | 1.4MHz | 1Mbps | 164 dB | 1T1R
Cat 1b | 20MHz | 10/5Mbps | 141dB | 1T1R
eRedcap | 20MHz (Note) | 10Mbps | 137dB | 1T1R/1T2R
Redcap | 20MHz | 170/85Mbps | 132dB | 1T1R/1T2R
Table 1. Brief summary of LTE/NR IoT device types

## Slide 4
  Low cost with reasonable RF & BB restriction
    Max 20MHz UE BW for 6G massive communication as good balance between cost and system efficiency, with minimal impact on eMBB performance
  Half-duplex FDD for low cost
    Half-duplex FDD to lower the cost and reduce UE power consumption
  Moderate peak data rate to support various service types
    Moderate PHY-layer peak data rate, e.g., up to 10Mbps to accommodate wide range of services (e.g. data rates) as well as improve both network and UE energy efficiency, allowing longer sleep time due to shorter transmission/reception time
  Practical coverage target
    up to [154dB MCL] with data rate [no less than 1kbps], as good balance between real deployment requirement and overall resource efficiency
Consideration of 6G massive communication (IoT)

## Slide 5
Justification for 20MHz UE BW massive communication
  20MHz UE BW small enough for substantial device cost saving
    Based on NR study for Redcap & eRedcap TR 38.875/865
      Significant cost reduction (>50%) by 20MHz RF & BB BW compared to 100MHz RF&BB
      Additional minimal cost reduction (< 5%) by 5MHz BB and/or RF BW compared to 20MHz RF&BB
    Based on LTE Cat 1bis product in Market
      The commercial device cost of Cat 1bis (20MHz BW) is comparable to that of LTE-M (1.4MHz BW) and NB-IoT (180KHz BW), as low as 1 USD for chipset and 2 USD for module cost
  Simplified design for common signals/channels with 20MHz BW
    Single structure for SSB/SIB1 and other common signals/channels with sufficient bandwidth shared by different device types without degradation of eMBB performance
      In NR, 3.6~7.2MHz for SSB and 10~ 20MHz for SIB1 (for 15kHz and 30kHz SCS) is assumed as reference for NR Redcap/eRedcap study. Similar BW for 6G SSB/SIB1 is expected.
  20MHz UE capability with functional support for smaller network operating BW
    Device with 20MHz BW capability can work properly when operator’s Channel Bandwidth is smaller than 20MHz, e.g., Channel BW down to 3MHz if supported.
From Table 7.2.2-1 in TR 38.865

## Slide 6
Text Proposals
  Adopt following TP for massive communication requirements in 3GPP TR 38.914
5.4.3 Massive Communication The 6GR and 6G RAN architecture shall support the following minimum requirements for Massive Communication (IoT): - 6G Massive Communication (IoT) shall be supported for FR1. 6GR should have a common/scalable design that supports the above usage scenario in addition to eMBB Prioritize 6GR design for eMBB The above usage scenario should not overlap with Ambient IoT and NB-IoT -[PHY or MAC] [minimum] peak data rate is [10] Mbps in DL and [5] Mbps in UL for lowest-tier device. Maximum UE bandwidth is 20MHz for both TDD and FDD bands. The UE can operate in a network with smaller channel bandwidth (e.g. around 3~5MHz). A UE supports either Half-duplex or full duplex FDD The target coverage is [154dB MCL] with data rate [no less than 1kbps]. Long battery life is supported. Editor note: “6G should support coexistence with NB-IoT (all deployment modes) and eMTC via semi-static configuration” is moved to 5.2 (migration and architecture)