## Slide 1
Views on the release independence for UE 6RX feature
RP-253312
3GPP TSG RAN #110
Baltimore, USA, December 8-11, 2025
Agenda: 9.5.4.1
Source: Samsung
Document for : Discussion and decision

## Slide 2
RAN4 agreements
Way forward for 6-layers support for handheld UE and FWA devices (R4-2503014, RAN4#114)
RAN4 Chair to take note of the following in the meeting report:
  “RAN4 unable to conclude on a common set of simulation assumptions to determine feasibility of 6 layer for handheld UE In Rel-19”
6-layer performance requirements will be only defined for FWA.
4-layer performance requirements will be defined and will apply to FWA and handheld UE devices.
The fact that 6-layer is only supported for FWA shall be explicitly captured at least in the RAN4 specifications.
RAN4 Chair’s opinion: (RAN4#116)
RAN4 requests RAN2 to provide feedback that if the signaling associated with new 6Rx requirements in R19 will be specified. If YES, can this signaling be introduced in R18?  Step 1
Depending on RAN2’s response, RAN4 can further discuss if release independence is feasible for this feature with new R19 signaling?
If the answers in both 1) and 2) are YES, the following agreement will be followed.
  Support 6Rx requirements with up to 4 MIMO layers for handheld UE from Rel-19
  Support 6Rx requirements for FWA UE from Rel-18 including 4 MIMO and 6 MIMO layer requirements
Outcome of 6 layer feasibility study
Observation 1: Agreement achieved in RAN4#114 as compromised WF (R4-2503014).
Outcome of 6Rx release independence discussion
Observation 2: RAN4 agreed a compromised option, which was dependent on 2-step conditions.
 Step 2

## Slide 3
Answers from RAN2 (Step 1)
RAN decision (Step 1-1)
Observation 4: RAN2 replied that it is up to RAN4 to decide whether the feature should be introduced in Rel-18 or not.
Reply LS to RAN4 (Step 1-2)
RAN approved RAN2 endorsed CRs for introduction of UE capability on 6 DL MIMO layers (RAN#109)
  It is captured in TS 38.306 that a new capability of 6 DL MIMO layers is only applicable for FWA UE as provided in R2-2506466 and R2-2506467
  CR introduces a new capability of 6 DL MIMO layers for FWA UE as an optional feature following RAN4 agreements
…
RAN4 also asked “If Yes, can this signalling be implemented early in Rel-18?”. RAN2 would like to inform RAN4 that RAN2 had implemented a means to allow early implementation of features in the specifications.
…
So to answer the RAN4 question, it is possible to specify the early implementation of the UE capability signalling on the support of maximum 6 DL MIMO layers for PDSCH. RAN2 assumes that it is up to RAN4 to decide whether the feature should be made early implementable in the standard or not.
Observation 3: Signaling associated with new 6Rx requirements in Rel-19 was specified.

## Slide 4
Release independence (Step 2)
Background
Observation 5: Release independence is limited to spectrum-related works as specified in TS 38.307.
Proposal 1: UE 6Rx shall not be a release independent feature.
Scope of release independence (TS 38.307)
The present document specifies requirements for Rel-P UEs supporting release independent features like:
  additional NR operating bands and power classes on top of Rel-P of TS 38.101-1/-2/-3/-4 and TS 38.133;
Furthermore, for Rel-P UEs supporting satellite access operation, the present document specifies requirements supporting release independent features like:
  additional NR operating bands on top of Rel-P of TS 38.101-5 and TS 38.133.
RAN4 discussion on release independence feasibility (Step 2)
RAN4 Chair Guidance: (RAN4#117)
the non-spectrum features which have spec impact including signaling impact should not be considered as release independent and should not be included in 38.307
  Case 1: 6Rx with up to 4 MIMO layers for handheld/FWA UE from Rel-18
  Case 3: 6Rx with up to 6 MIMO layer for FWA UE only from Rel-19
Observation 6: No consensus was reached on the feasibility of 6Rx release independence in RAN4#117.
Proposal 2: Both Case 1 and Case 3 shall be applied from Rel-19.
Not agreed in RAN4#117, due to no consensus was reached on the feasibility of 6Rx release independence in RAN4#117

## Slide 5
Conclusions
Observation 1: Agreement achieved in RAN4#114 as compromised WF (R4-2503014).
Observation 2: RAN4 agreed a compromised option, which was dependent on 2-step conditions.
  Support 6Rx requirements with up to 4 MIMO layers for handheld UE from Rel-19
  Support 6Rx requirements for FWA UE from Rel-18 including 4 MIMO and 6 MIMO layer requirements
Observation 3: Signaling associated with new 6Rx requirements in Rel-19 was specified.
Observation 4: RAN2 replied that it is up to RAN4 to decide whether the feature should be introduced earlier or not.
Observation 5: Release independence is limited to spectrum-related works as specified in TS 38.307.
Observation 6: No consensus was reached on the feasibility of 6Rx release independence in RAN4#117.
Observations
Proposal 1: UE 6Rx shall not be a release independent features.
Proposal 2: Both Case 1 and Case 3 shall be applied from Rel-19.
Proposals