## Slide 1: Discussion on 6G Radio - Coverage design target methodology - Time domain resource utilization - Design from tailor-made to ready-made - Design of device types - How to share the agreements among WGs
Sources: Panasonic
3GPP TSG RAN Meeting #110
Baltimore, USA, December 8-11, 2025
Agenda: 8.2.2 Study on 6G Radio
TDOC: RP-253410
For: Discussion

## Slide 2: Coverage design target methodology
MPL represents the coverage requirement in the specific deployment scenarios and conditions including layout, BS/UE antenna gain, BS/UE transmission power, BS/UE receiver sensitivities, Tx/Rx losses, occupied channel bandwidth, penetration loss, shadow fading, data rate.
  In order to obtain the calculation of "re-use of existing 5G mid-band (~3.5GHz) site grid for 6G deployments in at least around 7 GHz and targeting comparable coverage to 5G mid-band", MPL is required.
When Tx power is predetermined, MaxCL represents the coverage requirement of the baseband. It means several of specific deployment scenarios and conditions are at the time of the deployment decisions including the possibility of the usage of the repetition. MCL is similar to MaxCL if receiver gain is fixed assumption.
Therefore, we propose following:
  "Coverage target(s) considering diverse use cases and device types" is based on MaxCL as the deployment decision should not be included in the target.
  For re-use of 5G mid-band site grid for 6G deployment scenario around 7G, MPL should be used. This is to be continued within RAN1.

## Slide 3: Coverage design target methodology
For re-use of 5G mid-band(~3.5GHz) site grid for 6G deployment scenario around 7GHz, the difference between "initial access/random accesss" and "data channel" was identified. This relates the wording choice between "same or exceeding coverage" or "comparable coverage".
Between 3.5G and 7GHz, in addition to path-loss, specific deployment scenarios and conditions like BS/UE antenna gain and BS/UE transmission power can be different. Especially what deployment scenarios and conditions for NW is up to NW side decision.
  If specific deployment scenarios and conditions is very good, "same or exceeding coverage" with the same data rate may be possible.
  If specific deployment scenarios and conditions is low cost choice, "same or exceeding coverage" with the same data rate would not possible within reasonable complexity of PHY design.
  What specific deployment scenarios and conditions should be taken as the comparison is to be further discussed in RAN1. Therefore, for data channel, the target should be "comparable coverage". Depending on specific deployment scenarios and conditions, the target data rate may be adjusted.
  On the other hand, for "initial access/random accesss", regardless of what specific deployment scenarios and conditions, the reachbility is important by any means including the usage of the repetition of channels/signals. Therefore, the target of "initial access/random accesss" should be written as "same or exceeding coverage".
Therefore, we propose following:
  For initial access/random accesss, target around 7GHz should be "same or exceeding coverage" of mid-band regardless of specific deployment scenarios and conditions.
  For data channels, target around 7GHz should be comparable coverage of mid-band. The data rate depends on specific deployment scenarios and conditions to be discussed in RAN1.

## Slide 4: Time domain resource utilization
Any of device types should be supported in the spectrum by the 3gpp design and which device types should be operated in the spectrum should be up to NW choice.
  When the certain spectrum is operated in MRSS, dynamic TDD, SBFD, Network energy saving, ISAC, or any of future extension, any of the device types including low end 6G IoT device should be operatable in this the spectrum. It means following.
    Low end 6G IoT device should not prevent or support dynamic resource usage of MRSS.
    Low end 6G IoT device should not prevent or support dynamic TDD.
    Low end 6G IoT device should support SBFD for the extension of the UL coverage.
    Low end 6G IoT device should support network energy saving.
    Low end 6G IoT device should not prevent dynamic resource usage of ISAC.
    Low end 6G IoT device should not prevent dynamic resource usage of future extension.
  Therefore, we propose following:
    Time domain resource utilization should be flexible and transparent regardless of MRSS, dynamic TDD, SBFD, Network energy saving, ISAC, or any of future extension.

## Slide 5: Design from tailor-made to ready-made
5G NR design principle was tailor-made design principle. i.e. many options/configurations allows customization of the specific deployment including URLLC.
  It may allow optimization of the specific usage.
  It allowed to reduce the time for 3gpp standardization discussion as optimization of the prameters are up to NW and markets (of UE capability choices).
  It resulted many of UE features choices and many of configurations parameters. The fragmentation of choices made the difficulty on which feature to be supported.
6GR design principle was agreed to be single technology framework to reduce the options. On the other hand, the diverse usage targets (eMBB, URLLC, IoT, FWA etc) have conflict requirement among efficiency, complexity, energy usage and latency.
  To improve efficiency or latency would result increased complexity or energy usage.
  To reduce complexity or energy usage would result reduced efficiency and longer latency.
  The balanced point for difference of the diverse usage are different depending on the usage target.
We propose following.
  Within a single technology framework, several of balanced points as ready-made options/configurations for the diverse usage targets (eMBB, URLLC, IoT, FWA etc) should be seeked in 6GR.
    This can require more 3gpp standardization discussion but could reduce overall complexity of the system.

## Slide 6: Design of device types
Current NR UE capability has many features. Basic features are described as "for UE supports XXX, UE must indicate this FG is supported" but these FGs are separated for reception, transmission, synchronization, power control and so on.
One of reasons of too many UE features are UE features are spitted for reception, transmission, synchronization, power control and so on.
If basic feature indication of reception, transmission, synchronization, power control and so on are merged and indicated by one bit (or one codepoint), the amount of FG can be reduced.
In addition, enhancement more than basic features in each FG of respective groups of reception, transmission, synchronization and so on are merged as "enhance level 1", "enhance level 2" and so on instead of respective parameters of each FGs.
Above way of UE feature design could reduce the possible UE features and it could be the definition of device type.
  Basic UE feature XXX, enhance level 1, enhance level 2, ....
  We propose following.
  Basic UE features among different group like reception, transmission, synchronization are merged to one FG. In addition, instead of respective parameter for each FG, different FGs from reception, transmission, synchronization and so on is merged to "enhance level 1, enhance level 2,, ". These can be basic of "device type".

## Slide 7: How to share the agreements among WGs
RAN1 discussed how to share the RAN1 agreement with other WGs for the better progress of 6GR. To select specific agreements for respective WGs would be more convenient for the receiving WG but it requires more RAN1 discussion on which one to be seletected. Then at the end, the whole 6GR related agreements were sent as LS.
To capture all agreements is also carried out by the status report. But it is before RAN plenary only.
Agreements are to be captured in TR but it would take time for more reader friendly description.
We propose following to improve the cycle of status report and reduce LS exchange of full agreement.
  Within 3gpp RAN1 folder, to have the file to capture all past RAN1 agreement of 6GR study and it is informed to other WGs. It is updated by the Rapporteur(s) after each of WG meeting. No specific LS is sent for the update. Status report can refer this document.

## Slide 8: Summary
We propose following for 6GR:
  "Coverage target(s) considering diverse use cases and device types" is based on MaxCL as the deployment decision should not be included in the target.
  For re-use of 5G mid-band site grid for 6G deployment scenario around 7G, MPL should be used. This is to be continued within RAN1.
  For initial access/random accesss, target around 7GHz should be "same or exceeding coverage" of mid-band regardless of specific deployment scenarios and conditions.
  For data channels, target around 7GHz should be comparable coverage of mid-band. The data rate depends on specific deployment scenarios and conditions to be discussed in RAN1.
  Time domain resource utilization should be flexible and transparent regardless of MRSS, dynamic TDD, SBFD, Network energy saving, ISAC, or any of future extension.
  Within a single technology framework, several of balanced points as ready-made options/configurations for the diverse usage targets (eMBB, URLLC, IoT, FWA etc) should be seeked in 6GR.
  Basic UE features among different group like reception, transmission, synchronization are merged to one FG. In addition, instead of respective parameter for each FG, different FGs from reception, transmission, synchronization and so on is merged to "enhance level 1, enhance level 2,, ". These can be basic of "device type".
  Within 3gpp RAN1 folder, to have the file to capture all past RAN1 agreement of 6GR study and it is informed to other WGs. It is updated by the Rapporteur(s) after each of WG meeting. No specific LS is sent for the update. Status report can refer this document.