## Slide 1: Motivation on introduction of new NR band for 1.5GHz Japanese allocation
3GPP TSG RAN meeting #110
Baltimore, USA, December 8-11, 2025
RP-253495
KDDI, NTT DOCOMO, SoftBank, Apple, Ericsson, Fujitsu, HiSilicon, Huawei, Kyocera, Murata, NEC, Nokia, OPPO, Qualcomm, Samsung, Sharp, Skyworks Solutions Inc., Sony, Xiaomi

## Slide 2: Justification
In Rel-15, band n74(UL: 1427-1470 MHz, DL: 1475-1518 MHz) was standardized to aim for achieving an eco-system with wider frequency range, to accommodate demands of some MNOs from different regions/countries. The above frequency range is aligned to the result of WRC-15. Therefore, n11 and n21 corresponding to LTE as B11 and B21 were not standardized.
On the other hand, a technical complexity of n74 is found from UE implementation point of view. This is mainly because the 5MHz gap between UL/DL of n74 is too narrow so that the requirements were established assuming two duplexers as known well. Consequently, even now, no n74 UE products are still provided in the market.
Japanese MNO operating 1.5GHz frequency [1] are intending migrations from 4G LTE(B11/B21) to 5G NR, and also facing the above issue on any UE products for operating 1.5GHz NR band.
Reference: [1] https://www.tele.soumu.go.jp/resource/e/search/myuse/use0303/1400m.pdf
Notes: In the 5G era, the non-collocated scenarios for B42 and n77/n78 as shown in the previous slides still occur in Japanese, Korean and European operators. Tx antenna co-location at network side is not always available since the co-existence conditions are not always same for all the bands.

## Slide 3: Frequency range
We propose a new NR band with narrower frequency range and assuming a single duplexer.
Existing NR band n74 with dual duplexer
New NR band with a single duplexer
UL : 43MHz
1427
1470
1475
1518
UL : 35MHz
1462.9
DL : 35MHz
1475.9
Gap: Only 5MHz
Expand Gap: 13MHz
SoftBank
KDDI
docomo
SoftBank
KDDI
docomo
DL : 43MHz
(B11:20MHz)
(B11:20MHz)
(B21:15MHz)
(B21:15MHz)
【Reference】
1427.9
1510.9
Notes: And then, in this slide, we’re proposing Rel-19 potential enhancement area based on results of Rel-18 WI.
Firstly, Type 1 UE is legacy Rel-15 UE. We had an easy mistake in this slide. Next, Type 2 UE is developed in Rel-18.
And then, Rel-19 potential enhancement area will be Type 3 and Type 4 UEs.
Specifically, Type 4 UE should reuse Type 2 UE requirements for power imbalance on UE RF and MRTD/MTTD on RRM.

## Slide 4: Potential Objectives
Proposal
  Specify a new NR FDD band for the Japanese 1.5GHz frequency allocation spanning 1427.9-1462.9 MHz for UL and 1475.9-1510.9 MHz for DL
Assumption/Requirement
  Channel BW/SCS (*based on B11/B21 and n74) in Table 1.
  Power Class: PC3 (23dBm)
  UE architecture assumption: Single duplexer
    UE supports both the new NR band for 1.5GHz and/or B11/B21 with a common single duplexer.
SCS (kHz) | channel bandwidth (MHz) |  | 
15 | 5 | 10 | 15
30 |  | 10 | 15
60 |  | 10 | 15
Table 1
Notes: Finally, same as proposals proposed by RAN chair and RAN4 chair, we propose two aspects.
Firstly, consider Type 4 UE assuming MRTD>CP for FWA with reusing Type 2 requirements.
And then, not to include Type 3 in March’24, but also check it in Dec’24. Type 3 requirements assuming MRTD<CP without intended impacts on the NW side.

## Slide 5: Potential Objectives
Assumption/Requirement
  Consider the requirements that the power of any UE emission shall not exceed the levels specified in Table 2 and whether A-MPR is needed or not is FFS.
  Other UE/RRM requirements
  The new NR band is intended to be used only in Japan.
Table 2
Frequency range (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) | Measurement bandwidth
 | 5, 10, 15 | 
1475.9 ≤ f ≤ 1510.9 | -35 | 1 MHz
Notes: Finally, same as proposals proposed by RAN chair and RAN4 chair, we propose two aspects.
Firstly, consider Type 4 UE assuming MRTD>CP for FWA with reusing Type 2 requirements.
And then, not to include Type 3 in March’24, but also check it in Dec’24. Type 3 requirements assuming MRTD<CP without intended impacts on the NW side.

## Slide 6
Appendix

## Slide 7: Example) WI Objectives
The objective of this work item is to:
Specify a new NR FDD operating band to include a new band numbering and core requirements for Japanese 1.5GHz allocation spanning 1427.9-1462.9 MHz for UL and 1475.9-1510.9 MHz for DL by considering that:
  Support the channel bandwidth and SCS in Table 1;
  The use of UE power class 3 (*23dBm).
  UE architecture assumption: Single duplexer
    UE supports both the new NR band for 1.5GHz and/or B11/B21 with a common single duplexer.
SCS (kHz) | channel bandwidth (MHz) |  | 
15 | 5 | 10 | 15
30 |  | 10 | 15
60 |  | 10 | 15

## Slide 8: Example) WI Objectives
The objective of this work item is to:
  Consider the requirements that the power of any UE emission shall not exceed the levels specified in Table 2 and whether A-MPR is needed or not is FFS.
  Other UE RF/RRM requirements
  The new NR band is intended to be used only in Japan.
Table 2
Frequency range (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) | Measurement bandwidth
 | 5, 10, 15 | 
1475.9 ≤ f ≤ 1510.9 | -35 | 1 MHz

## Slide 9
EOF