## Slide 1
Huawei, HiSilicon
Discussion on checkpoints for Rel-20 AI/ML work item
3GPP TSG RAN#110 RP-253497
Baltimore, USA, December 8-11, 2025
Agenda Item: 9.3.1.3

## Slide 2
Contents
Progress and proposal on inter-vendor collaboration options
Progress and proposal on UE side data collection
Check points in WID (RP-251870)
Inter-vendor training collaboration for two-sided AI/ML models
Fully defined/specified reference model (“Direction C”) with RAN1 scalability study outcome taken into account [RAN4/RAN1] – check-point in RAN#110 upon RAN4 feedback
  Specification of standardized encoder model structure plus parameter exchange (“Direction A, sub-option 3a-1” without target CSI sharing) leveraging defined/reference model of “Direction C” and taking RAN1 scalability study outcome into account [RAN4/RAN1/RAN2/RAN3] – check-point in RAN#110 upon SA WG feedback
Specification of standardized dataset format/content plus dataset exchange (“Direction A, sub-option 4-1”) [RAN1/RAN2/RAN3/RAN4] – check-point in RAN#110 upon SA WG feedback
Data collection [RAN2]:
Further study and specify if deemed necessary, standards-based UE data collection at least for UE-side model training in close collaboration with SA WGs and taking into account the agreed principles during the Rel-19 study – check-point in RAN#110 based on SA WG feedback and SA2 study on data collection

## Slide 3
Progress and proposal on inter-vendor collaboration (1/4)
RAN4 progress on model design of Direction C/Option 3a-1
  Some progress (R4-2522432) is achieved, but still with FFS on some essential aspects
Number of TX ports:
Agreement:
  It was agreed that 32 and 16 ports are considered for the final test decoder and reference encoder (and direction C model), associated with RAN4 performance requirements
    It is FFS whether to additionally consider 8 ports
    It is FFS whether to additionally consider 64 and 128 ports
Token and feature dimension:
Agreement:
  Assuming <=32 ports supported, sub-band as token dimension and TX port as feature dimension
Sub-band size:
There was no agreement on sub-band size. The following options were proposed but not agreed.
Option 1: 6, 12 sub-bands
Option 2: 13 (10MHz), 26 (20 MHz) sub-bands
Option 3: 4 (5MHz), 8 (10 MHz) and 16 (20 MHz) sub-bands
(Further options not precluded for future meetings)
How to generate the dataset (LLS, SLS etc.)
There was a discussion on whether to include SLS (Uma, Umi etc.) and/or LLS (TDL or CDL) in the dataset, but no conclusion.
Dataset contents:
Agreement:
  Dataset consists of Eigenvectors
  At least Rank 2 considered
    FFS for rank 3 and rank 4
  Common procedure to select Eigenvectors:
    Select the right eigenvectors corresponding to the top-maximum- layer-number eigen values
    Perform column normalization by normalizing the L2 norm of each eigenvector in to 1
    Perform phase normalization by subtracting the angle of the first element from the angles of all the elements in each eigenvector
Option 3 is feasible for RAN4 to complete. RAN4 will take into account the conclusions in RAN1 on scalability in order to create a scalable model.
  RAN4 agrees that the test decoder of option 3 is the same as the reference decoder of direction C and the reference encoder of option 3 is the same as the reference encoder of direction C. If so, RAN4 believes that direction C should be feasible to complete too.
Direction A 3a-1 is feasible for RAN4 to complete from reference encoder perspective. Hence, RAN1 could possibly consider the RAN4 reference encoder for the standardized encoder model structure for Direction A 3a-1.
RAN4 agreed the detailed steps to develop the model.
LS to RAN (R4-2522434)
Observation 1: Only a limited set of parameters are agreed in RAN4 for model design of Direction C/Option 3a-1. Some typical configurations and assumptions of real network have not been agreed yet. E.g.,
Tx port number of 64 ports and 128ports
BW larger than 20MHz and its corresponding sub-bands
Rank 3 and rank 4 for dataset
SLS based dataset (Uma, Umi, etc.)
Note: If the above are not considered for model design of Dirction C/Option 3a-1, the standardized model/model structure can hardly be applicable in real network.
Observation 2: RAN4 only concluded that the completion of Direction C/Option 3a-1 is feasible, but has not started the evaluations yet, and therefore cannot ensure whether the specified model can gurantee a justified performance or not.

## Slide 4
SA2 progress
LS reply to RAN2 (S2-2508104)
Observation 3: SA2 replies that Rel-19 SA2 specifications do not support dataset and model parameter exchange. A new WT has been set up for further study whether and how to support dataset and model parameter sharing for non-OTA scenarios in Rel-20.
New WT for R20 study (S2-2511314)
Observation 4: SA5 confirms that it is feasible for OAM to transfer the NW-side dataset/model parameter to UE-side training entity. A new WT has been set up for further study the solution in Rel-20.
LS reply to RAN2 (S5-254083)
New WT for R20 study (S5-255334)
Progress on dataset/parameter exchange of Option 3a-1/4-1
Progress and proposal on inter-vendor collaboration (2/4)
SA5 progress

## Slide 5
Observation 5: Good progress has been achieved for Option 4-1 on the content/type of Target CSI and CSI feedback, performance target, and mapping of Target CSI set and CSI feedback set. No discussion in RAN1 on the content/format of Option 3a-1.
Progress on dataset/parameter exchange of Option 3a-1/4-1
RAN1 progress
Progress and proposal on inter-vendor collaboration (3/4)

## Slide 6
  Analysis on the study status on Direction C/Option 3a-1
  RAN4 has confirmed the feasibility of completion of standardizing scalable model, and the steps for developing reference encoder are agreed. On the other hand, the discussion on the set of to-be-supported Tx port/subband/rank/dataset configurations is still ongoing, and the evaluations have not started yet. Thus, the current progress has not fully justified the performance of Direction C/Option 3a-1, and whether achievable performance of the scalable model can be achieved needs further evaluation and justification.
  Option 4-1 has been widely evaluated in Rel-19, and is more flexible for supporting various configurations and datasets.
  Analysis on the study status in SA WGs
  Both SA2 and SA5 have replied the LS, and SA5 replied with a more positive tone. SA5 would be able to support dataset/parameter exchange with smaller standard effort than SA2.
  Both SA2 and SA5 have introduced the WT to the Rel-20 study for the solution of dataset/parameter delivery.
  Proposal 1: For inter-vendor training collaboration options, support Option 4-1.
  Further check whether the dataset sharing is achieved via OAM or CN, depending on the study outcome in Q2 2026.
Progress and proposal on inter-vendor collaboration (4/4)

## Slide 7
Progress and proposal on UE side data collection (1/3)
Observation 6: The study on Option 2-UP is incomplete, and commercialization challenges of such operator-managed application client in Option 2-UP have not been fully analyzed.
Progress on Option 2-UP (CN-based)
References:
[1] S2-2510958, LS on AI/ML UE sided data collection, Source: SA2, To: RAN2, RAN, Cc: SA, SA3, SA5, RAN1
[2] S2-2510959_was0956_KI#1 interim conclusion update-r11
[3] R2-2506088, Discussion on UE-side data collection, Huawei, HiSilicon, OPPO, China Telecom, CATT, China Unicom, ZTE, NTT DoCoMo
SA2 has conducted a study and agreed some principles for KI#1 (i.e. Transfer of data over UP for UE data collection) according to [1][2]. However, there are still 20 open issues at least in SA2 (as shown on the right excerpted from [2]).
Option 2-UP needs the deployment of an operator-managed APP client on the UE, which collects data from the UE's AS layers and reports it to the Data Collection entity in the CN. Even if technically feasible, this option would pose substantial commercialization challenges and has not been evaluated in SA2/RAN2.
UE controlled APP client
AS
UE
gNB
UPF
CN NF
Data collection APP server
UE server
Data collection APP server
Option 1a
Option 2-UP, 1b
Operator controlled APP client
SA2 progress

## Slide 8
Observation 7: Option 3-CP has minimal spec impacts, and some aspects identified by RAN2 can be solved if Option 3-CP can re-use R19 NW-side data collection solution.
Progress on Option 3-CP (OAM-based)
References:
[1] TR 38.843 v19.0.0
[2] R2-2506088, Discussion on UE-side data collection, Huawei, HiSilicon, OPPO, China Telecom, CATT, China Unicom, ZTE, NTT DoCoMo
In R19, NW-side data collection has been introduced, and UE can store and report logged measurement to NW based on NW requests. There is no real difference between Option 3-CP for UE-side data collection and NW-side data collection (OAM-centric). It means that Option 3-CP can largely re-use NW-side data collection procedure and the only change could be that more measurements would be added.
In the TR 38.843 [1], section 7.2.1.3.2.1 captures some analysis on UE memory allocation, Segmentation for UE side data collection, and Continuity of the collected data reporting.
Firstly, these analysis assumes that a large amount of data requires to be transferred from a UE, but the data volume highly depends on network configuration, i.e., the network can be implemented so that the data volume for a UE is reasonable and controllable. Further, the data to be reported by the UE does not require to be transmitted in a single RRC message, i.e. segmentation is not necessary.
In addition, the three aspects can be solved if 3-CP can re-use NW-side data collection, and details can be found in [2].
Observations on other options:
Progress on 1a (implementation-based): No standard work needed. Already supported in R19.
Progress on Option 2-CP (CN-based): Transparent to RAN. The feasibility has been confirmed by RAN, but SA2/CT1 has not studied details of the solutions.
Progress on Option 3-UP (OAM-based): According to the SA5 LS S5-250828, Option 3-UP can be categorized into other options.
Progress and proposal on UE side data collection (2/3)
RAN2 progress

## Slide 9
  Proposal 2: For UE side data collection in Rel-20, if a standardized option is required, only Option 3-CP (OAM-based) is selected; otherwise, only Option 1a (implementation-based) is supported.
Candidate options | Progress & views
1a (implementation-based) | No standard work needed. Already supported in R19.
2-CP (CN-based) | Transparent to RAN. The feasibility has been confirmed by RAN, but SA2/CT1 has not studied details of the solutions.
2-UP (CN-based) | The study on Option 2-UP is incomplete, and commercialization challenges of such operator-managed application client in Option 2-UP have not been fully analyzed.
3-CP (OAM-based) | Option 3-CP has minimal spec impacts, and some aspects identified by RAN2 can be solved if Option 3-CP can re-use R19 NW-side data collection solution.
3-UP (OAM-based) | According to the SA5 LS S5-250828, Option 3-UP can be categorized into other options.
Summary of progress & views on candidate options
Progress and proposal on UE side data collection (3/3)

## Slide 10
Summary
Observations and proposal for inter-vendor collaboration
Observations and proposal for UE-side data collection
Observation 6: The study on Option 2-UP is incomplete, and commercialization challenges of such operator-managed application client in Option 2-UP have not been fully analyzed.
Observation 7: Option 3-CP has minimal spec impacts, and some aspects identified by RAN2 can be solved if Option 3-CP can re-use R19 NW-side data collection solution.
  Proposal 2: For UE side data collection in Rel-20, if a standardized option is required, only Option 3-CP (OAM-based) is selected; otherwise, only Option 1a (implementation-based) is supported.
Observation 1: Only a limited set of parameters are agreed in RAN4 for model design of Direction C/Option 3a-1. Some typical configurations and assumptions of real network have not been agreed yet. E.g.,
Tx port number of 64 ports and 128ports
BW larger than 20MHz and its corresponding sub-bands
Rank 3 and rank 4 for dataset
SLS based dataset (Uma, Umi, etc.)
Note: If the above are not considered for model design of Dirction C/Option 3a-1, the standardized model/model structure can hardly be applicable in real network.
Observation 2: RAN4 only concluded that the completion of Direction C/Option 3a-1 is feasible, but has not started the evaluations yet, and therefore cannot ensure whether the specified model can gurantee a justified performance or not.
Observation 3: SA2 replies that Rel-19 SA2 specifications do not support dataset and model parameter exchange. A new WT has been set up for further study whether and how to support dataset and model parameter sharing for non-OTA scenarios in Rel-20.
Observation 4: SA5 confirms that it is feasible for OAM to transfer the NW-side dataset/model parameter to UE-side training entity. A new WT has been set up for further study the solution in Rel-20.
  Proposal 1: For inter-vendor training collaboration options, support Option 4-1.
  Further check whether the dataset sharing is achieved via OAM or CN, depending on the study outcome in Q2 2026.

## Slide 11
Appendix: Definition of directions/options for inter-vendor training collaboration
  The key agreements on the definition of direction A/C and sub-option 3a-1/4-1 are as below:
    Direction A: Sharing parameters/dataset that enables UE-side offline engineering
      Option 3a-1: Standardized reference model structure + Parameter exchange between NW-side and UE-side. Parameters exchanged from the NW-side to UE-side is CSI generation part
      Option 4-1: Standardized data / dataset format + Dataset exchange between NW-side and UE-side. The dataset exchange originates from the NW-side and ends at the UE-side. Dataset exchanged from the NW-side to UE-side consists of (target CSI, CSI feedback)
    Direction C: Fully standardized reference model(s) and parameters with specified CSI generation part and/or CSI reconstruction part
  UE side data collection options (based on TR 38.843 v19.0.0):
    Option 1a) UE collects and directly transfers training data to the data collection entity outside the MNO (e.g. Over-The-Top (OTT) server) for UE-side model training. No 3GPP specification impact is expected.
    Option 2) UE collects training data and transfers it to Core Network. Core Network transfers the training data to the server for data collection for UE-side model training/OTT server
    Option 3) UE collects training data and transfers it to OAM. OAM transfers the training data to the server for data collection for UE-side model training/OTT server.